LIGO Laboratory / LIGO Scientific Collaboration

LIGO-E1100519-v1	LIGO	6/8/11

Test Procedure for Test Oscillator Boxes.

Paul Schwinberg and Daniel Sigg

Distribution of this document:

LIGO Scientific Collaboration

This is an internal working note

of the LIGO Laboratory.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 159 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

# Introduction

The following Test Procedure describes the test of proper operation of the Test Oscillator Boxes, D0902705-v2.

# Test Equipment

- Voltmeter

- Oscilloscope

- Stanford Research SR785 analyzer

- RF Power Meter HP E4418A or Agilent N1914A

- Board Schematics—D1100663

# Tests

The Test Oscillators  use the Low Noise Power Module (D0901846-D).

- Verify the proper current draw.  Using a bench DC supply apply ±24 Volts to P7 and ±17 Volts to P6 of the low noise power Module (D0901846-D).  Measure the current draw of the board.

+24 Volt current ___________0.1 A Nom.

‒24 Volt current ___________0.0 A Nom.

+17 Volt current ______________     less than 1.1 A

‒17  Volt current ______________     less than 0.01 A

- On the low noise power module check the voltage on TP 1-13.

TP1 ( +17V ) ______________		TP2 (‒17V ) _______________

TP3 , 4 ( GND )				TP5 (+ 5V)_________________

TP6 (‒15V ) ________________		TP7 (+24V ) ________________

TP8 ( GND )				TP9 (‒24V ) ________________

TP10 ( GND )				TP11 (+15V ) _______________

TP12 (+VREF ) _____________		TP13  (‒VREF ) ______________

- If  TP 1 , 2, 7 , 9 and 8 are correct then TP14 ( OK  ) should be logic high ~3Volts.

Confirm._____________________

- The noise on TP 12, 13, 11 and 6 should be measured with a SR785 using an

rms power spectrum.

TP12  noise ____________________less than 20 nVrms/√Hz at 140 Hz

TP13 noise _____________________less than 20 nVrms/√Hz at 140 Hz

TP11 noise _____________________ less than 20 nVrms/√Hz at 140 Hz

TP6 noise ______________________ less than 30 nVrms/√Hz at 140 Hz.

This concludes the test of the power supply. Now test the crystal oscillators.

5)  With the frequency control input grounded measure the RF output with a RF Power meter. The nominal output level is 12 dBm ± 2dBm.

RF Output levels (dBm)

| OSC1 | OSC2 | OSC3 | OSC4 |
| --- | --- | --- | --- |

- Apply a dc voltage to the frequency control input. Measure the output frequency as a function of input voltage. The frequency change is typically 50 ppm for ± 10 Volt input.

Oscillator 1 frequency change for 10 Volt input change _________________ ppm

Oscillator 2 frequency change for 10 Volt input change _________________ ppm.

Oscillator 3 frequency change for 10 Volt input change _________________ ppm.

Oscillator 4 frequency change for 10 Volt input change _________________ ppm

Oscillator 1:

Center Frequency =

| Frequency |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Voltage | 10 | 9 | 8 | 7 | 6 |
| Voltage | 1 | 2 | 3 | 4 | 5 |
| Frequency |  |  |  |  |  |
| Frequency |  |  |  |  |  |
| Voltage | -1 | -2 | -3 | -4 | -5 |
| Voltage | -10 | -9 | -8 | -7 | -6 |
| Frequency |  |  |  |  |  |

Oscillator 2:

Center Frequency =

| Frequency |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Voltage | 10 | 9 | 8 | 7 | 6 |
| Voltage | 1 | 2 | 3 | 4 | 5 |
| Frequency |  |  |  |  |  |
| Frequency |  |  |  |  |  |
| Voltage | -1 | -2 | -3 | -4 | -5 |
| Voltage | -10 | -9 | -8 | -7 | -6 |
| Frequency |  |  |  |  |  |

Oscillator 3:

Center Frequency =

| Frequency |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Voltage | 10 | 9 | 8 | 7 | 6 |
| Voltage | 1 | 2 | 3 | 4 | 5 |
| Frequency |  |  |  |  |  |
| Frequency |  |  |  |  |  |
| Voltage | -1 | -2 | -3 | -4 | -5 |
| Voltage | -10 | -9 | -8 | -7 | -6 |
| Frequency |  |  |  |  |  |

Oscillator 4:

Center Frequency =

| Frequency |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Voltage | 10 | 9 | 8 | 7 | 6 |
| Voltage | 1 | 2 | 3 | 4 | 5 |
| Frequency |  |  |  |  |  |
| Frequency |  |  |  |  |  |
| Voltage | -1 | -2 | -3 | -4 | -5 |
| Voltage | -10 | -9 | -8 | -7 | -6 |
| Frequency |  |  |  |  |  |