LIGO Laboratory / LIGO Scientific Collaboration

LIGO- T1100445-v2	LIGO	10/1311

AOS SLC

Signal Recycling Cavity Baffles

Final Design

Michael Smith, Lisa C. Austin, Mike Hillard, Heidy Kelman, Tim Nguyen, Manuel Ruiz, Jesse Terrazas, Virginio Sannibale

Distribution of this document:

LIGO Scientific Collaboration

This is an internal working note

of the LIGO Laboratory.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 159 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

Table of Contents

1	INTRODUCTION	7

1.1	Scope	7

1.2	Final Design Review Checklist	7

1.2.1	Final requirements – any changes or refinements from PDR?	7

1.2.1.1	Direct Requirements	7

1.2.1.2	Hartmann Baffle Requirements—NEW	7

1.2.1.3	Ghost Beam Baffle Requirements	7

1.2.1.4	Clear Aperture Requirements	7

1.2.2	Resolutions of action items from SLC PDR	7

1.2.2.1	Lower BRDF Material for Baffles	7

1.2.3	Final Parts Lists and Drawing Package	8

1.2.4	Final specifications	8

1.2.5	Final interface control documents	8

1.2.6	Relevant RODA changes and actions completed	8

1.2.7	Signed Hazard Analysis	8

1.2.8	Final Failure Modes and Effects Analysis	8

1.2.9	Risk Registry items discussed	8

1.2.10	Design analysis and engineering test data	8

1.2.11	Software detailed design	8

1.2.12	Final approach to safety and use issues	8

1.2.13	Production Plans for Acquisition of Parts, Components, Materials Needed For Fabrication	8

1.2.14	Installation Plans and Procedures	8

1.2.15	Final hardware test plans	9

1.2.16	Final software test plans	9

1.2.17	Cost compatibility with cost book	9

1.2.18	Fabrication, installation and test schedule	9

1.2.19	Lessons Learned Documented, Circulated	9

1.2.20	Porcelainizing	9

1.2.21	Problems and concerns	9

1.3	Applicable Documents	9

2	SIGNAL RECYCLING CAVITY BAFFLES	10

2.1	FUNCTION	10

2.1.1	SR3 HR BAFFLE	10

2.1.2	SR3 AR BAFFLE	10

2.1.3	SR2 SCRAPER BAFFLE	10

2.1.4	HAM SCRAPER BAFFLE	10

2.1.5	HARTMANN Beam Dump	10

2.1.6	SRM HR BAFFLE	10

2.2	ZEMAX LAYOUT	10

2.2.1	H1 & L1 IFO ZEMAX LAYOUT	10

2.2.2	H2 IFO ZEMAX LAYOUT	12

2.3	BEAM SIZES	14

2.3.1	H1/L1 BEAM SIZES IN SIGNAL RECYCLING CAVITY	14

2.3.1.1	H1/L1 ZEMAX PHYSICAL OPTICS PROPAGATION MODEL	14

2.3.2	H2 BEAM SIZES IN SIGNAL RECYCLING CAVITY	23

2.3.2.1	H2 ZEMAX PHYSICAL OPTICS PROPAGATION MODEL	23

3	DESCRIPTIONS OF SIGNAL RECYCLING CAVITY BAFFLES	32

3.1	SR3 HR BAFFLE	32

3.2	SR3 AR BAFFLE	33

3.3	SR2 SCRAPER BAFFLE	34

3.4	HAM SCRAPER BAFFLE	35

3.5	SRM HR BAFFLE	37

3.6	HARTMANN Beam Dump	38

3.7	BAFFLE HEIGHTS	40

3.8	OPTICAL INTERFACES	40

4	SCATTERED LIGHT DISPLACEMENT NOISE	42

4.1	Scattered Light Requirement	42

4.1.1	Scattered Light Parameters	43

4.1.2	BRDF of Baffle Surfaces	46

4.1.3	HAM ISI Seismic Motion	46

4.1.4	Naming Convention for Wedged Optics	46

4.1.5	SR3 HR Baffle Scatter	48

4.1.6	SR3 AR Baffle Scatter	48

4.1.6.1	Transmission of Signal Recycling Cavity Main Beam through SR3 HR	48

4.1.6.2	SR3 GBAR3 Ghost Beam	49

4.1.6.3	SR3 GBHR3 Ghost Beam	50

4.1.7	SR2 Scraper Baffle Scatter	51

4.1.7.1	ITM Ghosts Beams	52

4.1.7.2	BS Ghosts Beam	53

4.1.7.3	CP Ghosts Beam	53

4.1.7.3.1	CP_GBAR1 H1	53

4.1.7.3.1.1	CP_GBAR3 H1	54

4.1.7.4	Summary SR2 Scraper Baffle Scatter	55

4.1.7.5	SRM GBAR3 Ghost Beam	55

4.1.7.6	SRM GBHR3 Ghost Beam	56

4.1.7.7	Summary SR3, SR2, SRM Ghost Beam Scatter	57

4.1.8	H2 Hartmann Y Scatter	57

4.1.8.1	Scattered Light Displacement Noise from H2 HWSYM1	57

4.1.8.2	Scattered Light Displacement Noise from H2 HWSYM2	58

4.1.8.3	Scattered Light Displacement Noise from H2 HPY-F1	59

4.1.8.4	H2 Hartmann Y Viewport Scatter	59

4.1.8.5	H2 Hartmann Y Viewport Reflection, HAM Chamber Scatter	60

4.1.8.6	Summary of H2 Hartmann Y Scatter	61

4.1.9	H2 Hartmann X Scatter	62

4.1.9.1	Scattered Light Displacement Noise from H2 HWSXM1	62

4.1.9.2	Scattered Light Displacement Noise from H2 HWSXM2	62

4.1.9.3	H2 Scattered Light Displacement Noise from HWSXM3	63

4.1.9.4	H2 Scattered Light Displacement Noise from HWSXM4	64

4.1.9.5	H2 Scattered Light Displacement Noise from HPXF1	64

4.1.9.6	H2 Hartmann X Viewport Scatter	65

4.1.9.7	H2 Hartmann X Viewport Reflection, HAM Chamber Scatter	66

4.1.9.8	Summary of H2 Hartmann X Scatter	67

4.1.9.9	Summary of H2 Hartmann X Viewport Scatter	67

4.1.10	H1 & L1 Hartmann Beam Scatter	68

4.1.10.1	H1 & L1 Hartmann X Arm	68

4.1.10.2	H1 & L1 Hartmann Y Arm	70

4.1.10.3	Summary of H1 & L1 Hartmann Scatter	70

5	INTERFACE CONTROL DOCUMENT	71

Table of Figures

Figure 1: H1 & L1 HAM4: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump	11

Figure 2: H1& L1 HAM5: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle	12

Figure 3: H2 HAM10: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump	13

Figure 4: H2 HAM11: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle	14

Figure 5: 3D Layout, H1/L1 Physical Optics Propagation	15

Figure 6: H1/L1 SR3, Horizontal Beam Profile	16

Figure 7: H1/L1 SR3, Vertical Beam Profile	17

Figure 8: : H1/L1 SR2 Scraper Baffle, Horizontal Beam Profile	18

Figure 9: H1/L1 SR2 Scraper Baffle, Vertical Beam Profile	19

Figure 10: H1/L1 HAM Scraper Baffle (SR2 AR Baffle), Horizontal Beam Profile	20

Figure 11: H1/L1 HAM Scraper Baffle (SR2 AR Baffle), Vertical Beam Profile	21

Figure 12: H1/L1 SRM, Horizontal Beam Profile	22

Figure 13: H1/L1 SRM, Vertical Beam Profile	23

Figure 14: 3D Layout, H2 Physical Optics Propagation	24

Figure 15: H2 SR3, Horizontal Beam Profile	25

Figure 16: H2 SR3, Vertical Beam Profile	26

Figure 17: : H2 SR2 Scraper Baffle, Horizontal Beam Profile	27

Figure 18: H2 SR2 Scraper Baffle, Vertical Beam Profile	28

Figure 19: H2 HAM Scraper Baffle (SR2 AR Baffle), Horizontal Beam Profile	29

Figure 20: H2 HAM Scraper Baffle (SR2 AR Baffle), Vertical Beam Profile	30

Figure 21: H2 SRM, Horizontal Beam Profile	31

Figure 22: H2 SRM, Vertical Beam Profile	32

Figure 23: SR3 HR Baffle	33

Figure 24: SR3 AR Baffle	34

Figure 25: SR2 Scraper Baffle, H2	35

Figure 26: HAM Scraper Baffle	36

Figure 27: Internal Frequencies of HAM Scraper Baffle Assembly	37

Figure 28: SRM HR Baffle	38

Figure 29: Hartmann Beam Dump	39

Figure 30: FEA Analysis of Hartmann Beam Dump	40

Figure 32: Scattered Light Noise Transfer Functions	43

Figure 33: HAM optics table Seismic Motion, m/rtHz	46

Figure 34: Wedged Core Optic ghost beam naming convention	47

Figure 35: BS ghost beam naming convention	47

Figure 36: SR2 Scraper Baffle Scatter	55

Figure 37: Summary of SR Ghost Beam Scatter	57

Figure 38: Summary of H2 Hartmann Y Surfaces Scatter	61

Figure 39: Summary of H2 Hartmann X Surfaces Scatter	67

Figure 40: Summary of H2 Hartmann Viewport Scatter	68

Figure 41: Summary of H1 & L1 Hartmann X and Y Scatter	70

Table of Figures

Table 1: Heights and Sizes of SR Baffles	41

# INTRODUCTION

## Scope

This document provides the final designs for the Signal Recycling Cavity Baffle for aLIGO.

## Final Design Review Checklist

### Final requirements – any changes or refinements from PDR?

- The updated requirements for the Signal Recycling Cavity Baffles are listed in T070061 Stray Light Control Design Requirements.

- The Hartmann Viewport Beam Dumps were eliminated; see section 4.1.9.9.

#### Direct Requirements

Phase noise due to scattered light fields injected into the interferometer is treated as a technical noise source. Therefore, the total scattered light phase noise, expressed in equivalent displacement noise, must be < 1/10th of the quadrature sum of the suspension thermal noise and the test mass thermal noise (referred to as the SRD), as given in Figure 1 of M060056-06, Advanced LIGO Reference Design.

#### Hartmann Baffle Requirements—NEW

Baffles shall be placed to mitigate the scattered displacement noise caused by scatter from Hartmann optics in the Hartmann sensing train for the ITM mirrors; the total scattered light displacement noise, must be < 1/10th of the quadrature sum of the suspension thermal noise and the test mass thermal noise (referred to as the SRD), as given in Figure 1 of M060056-06, Advanced LIGO Reference Design.

#### Ghost Beam Baffle Requirements

Baffles shall be placed to mitigate the scattered light displacement noise caused by scatter from the ghost beams generated by the wedged optics, ITM, FM, BS, SR3, SR2, and SRM; the total scattered light displacement noise, must be < 1/10th of the quadrature sum of the suspension thermal noise and the test mass thermal noise (referred to as the SRD), as given in Figure 1 of M060056-06, Advanced LIGO Reference Design.

#### Clear Aperture Requirements

All Scraper Baffles shall not vignette the recycling cavity beam > 100 ppm power loss;

### Resolutions of action items from SLC PDR

Refer to: LIGO-L0900119-v1

#### Lower BRDF Material for Baffles

We suggest the team consider a lower-BRDF material for the more critical baffles,

and in particular suggest looking at the electro-static frit black-enameled steel as an option

that would give better optical performance.

Ans:	The lowest BRDF material that is practical at the moment is oxidized polished stainless steel.

### Final Parts Lists and Drawing Package

TBD

### Final specifications

E1100842 Specification for Mirror Finished (Super #8) Stainless Steel to be used in the LIGO Ultra-High Vacuum System

E0900364-v8 Metal components intended for use in the Adv LIGO Vacuum System

### Final interface control documents

TBD The mechanical and optical interfaces of the Signal Recycling Cavity Baffles are described in E110XXX-v1AOS SLC Signal Recycling Cavity Baffles Interface Control Doc.

### Relevant RODA changes and actions completed

NO Rodas!

### Signed Hazard Analysis

E1100984 SLC Signal Recycling Cavity Baffle Install Hazard Analysis

### Final Failure Modes and Effects Analysis

Not Required

### Risk Registry items discussed

None for this subsystem

### Design analysis and engineering test data

See Section 3, Descriptions of Signal Recycling Cavity Baffles and Section 4, Scattered Light Displacement Noise

### Software detailed design

Not applicable

### Final approach to safety and use issues

No operational safety issues

### Production Plans for Acquisition of Parts, Components, Materials Needed For Fabrication

E1101001-v1_AOS SLC Signal Recycling Cavity Baffles production plan

### Installation Plans and Procedures

This will be deferred until after FDR

### Final hardware test plans

See E1101023 Signal Recycling Cavity Baffles Fabrication, Installation, and Test Plan

### Final software test plans

Not applicable.

### Cost compatibility with cost book

See E1101001-v1_AOS SLC Signal Recycling Cavity Baffles production plan

### Fabrication, installation and test schedule

See E1101023 Signal Recycling Cavity Baffles Fabrication, Installation, and Test Plan

### Lessons Learned Documented, Circulated

### Porcelainizing

The baffles will be constructed of oxidized polished stainless steel to avoid shedding of the porcelain surface.

### Problems and concerns

There are presently no problems or concerns with the recycling cavity baffles.

## Applicable Documents

T070303 Arm Cavity Finesse for aLIGO

T070247 aLIGO ISC Conceptual Design

E0900364-v8 LIGO Metal in Vacuum

E1101023 Signal Recycling Cavity Baffles Fabrication, Installation, and Test Plan

T060073-00 Transfer Functions of Injected Noise

T070061-v2 Stray light Control Design Requirements

T0900269-v2 Stray Light Control (SLC) Preliminary Design

T1100056-v2 Arm Cavity Baffle Edge Scatter

E1100984_SLC Signal Recycling Cavity Baffle Install Hazard Analysis

E1101001-v1_AOS SLC Signal Recycling Cavity Baffles production plan

TBD E110XXX-v1AOS SLC Signal Recycling Cavity Baffles Interface Control Doc.

# SIGNAL RECYCLING CAVITY BAFFLES

## FUNCTION

### SR3 HR BAFFLE

The SR3 HR Baffle catches, on its recycling cavity side, some of the ghost beams from the ITM, CP, and BS; the stray light that is not absorbed is reflected toward the mode cleaner tube baffle near HAM5 and HAM11.

### SR3 AR BAFFLE

The SR3 AR Baffle catches and absorbs the signal recycling cavity power that leaks through the SR3AR surface.

### SR2 SCRAPER BAFFLE

The SR2 Scraper Baffle catches most of the ghost beams from ITM, CP, and BS. It also catches, on the side facing the SR2 mirror, some of the SR2 HR ghost beams.

### HAM SCRAPER BAFFLE

The HAM Scraper Baffle behind the SR2 AR side catches some of the SR2 AR ghost beams, and the reverse-path main IFO beam reflected by SRM that transmits through the SR2 AR surface.

### HARTMANN Beam Dump

The Hartmann Beam Dumps catch the 1064nm light that transmits through the first two dichroic  steering mirrors in the Hartmann beam paths.

### SRM HR BAFFLE

The SRM HR Baffle catches the reflected beam from the OFI TGG crystal

## ZEMAX LAYOUT

### H1 & L1 IFO ZEMAX LAYOUT

The H1 and L1 IFO ZEMAX layout of HAM4 is shown in Figure 1.

Figure 1: H1 & L1 HAM4: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump

The H1 and L1 IFO ZEMAX layout of HAM5 is shown in Figure 2.

Figure 2: H1& L1 HAM5: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle

### H2 IFO ZEMAX LAYOUT

The H2 IFO ZEMAX layout of HAM10 is shown in Figure 3.

Figure 3: H2 HAM10: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump

The H2 IFO ZEMAX layout of HAM11 is shown in Figure 4.

Figure 4: H2 HAM11: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle

## BEAM SIZES

### H1/L1 BEAM SIZES IN SIGNAL RECYCLING CAVITY

#### H1/L1 ZEMAX PHYSICAL OPTICS PROPAGATION MODEL

The beam sizes in the signal recycling cavity were calculated using the ZEMAX physical optics program; a Gaussian beam with a 12mm waist located a distance 1835000m away from the ITM HR surface (approximately at the middle of the arm) was propagated down the signal recycling cavity optical train. The ZEMAX layout is shown in Figure 5.

Figure 5: 3D Layout, H1/L1 Physical Optics Propagation

The x (vertical) and y (horizontal) beam profiles at various surfaces within the signal recycling cavity optical train are shown in the following figures.

Figure 6: H1/L1 SR3, Horizontal Beam Profile

Figure 7: H1/L1 SR3, Vertical Beam Profile

Figure 8: : H1/L1 SR2 Scraper Baffle, Horizontal Beam Profile

Figure 9: H1/L1 SR2 Scraper Baffle, Vertical Beam Profile

Figure 10: H1/L1 HAM Scraper Baffle (SR2 AR Baffle), Horizontal Beam Profile

Figure 11: H1/L1 HAM Scraper Baffle (SR2 AR Baffle), Vertical Beam Profile

Figure 12: H1/L1 SRM, Horizontal Beam Profile

Figure 13: H1/L1 SRM, Vertical Beam Profile

### H2 BEAM SIZES IN SIGNAL RECYCLING CAVITY

#### H2 ZEMAX PHYSICAL OPTICS PROPAGATION MODEL

The beam sizes in the signal recycling cavity were calculated using the ZEMAX physical optics program; a Gaussian beam with a 12mm waist located a distance 1835000m away from the ITM HR surface (approximately at the middle of the arm) was propagated down the signal recycling cavity optical train. The ZEMAX layout is shown in Figure 14.

Figure 14: 3D Layout, H2 Physical Optics Propagation

The x (vertical) and y (horizontal) beam profiles at various surfaces within the signal recycling cavity optical train are shown in the following figures.

Figure 15: H2 SR3, Horizontal Beam Profile

Figure 16: H2 SR3, Vertical Beam Profile

Figure 17: : H2 SR2 Scraper Baffle, Horizontal Beam Profile

Figure 18: H2 SR2 Scraper Baffle, Vertical Beam Profile

Figure 19: H2 HAM Scraper Baffle (SR2 AR Baffle), Horizontal Beam Profile

Figure 20: H2 HAM Scraper Baffle (SR2 AR Baffle), Vertical Beam Profile

Figure 21: H2 SRM, Horizontal Beam Profile

Figure 22: H2 SRM, Vertical Beam Profile

# DESCRIPTIONS OF SIGNAL RECYCLING CAVITY BAFFLES

## SR3 HR BAFFLE

A model of the SR3 HR Baffle is shown in Figure 23.

The hole diameter was chosen equal to the SR3 mirror diameter to maximize the extent of the Hartmann beam that reflects from the BS AR surface

Figure 23: SR3 HR Baffle

## SR3 AR BAFFLE

A model of the SR3 AR Baffle is shown in Figure 24. The baffle surface exceeds the dimensions of the SR3 mirror.

Figure 24: SR3 AR Baffle

## SR2 SCRAPER BAFFLE

A model of the SR2 Scraper Baffle is shown in Figure 25. The recycling cavity beams pass through the hole on the right in the figure; the Hartmann pick-off beam passes through the hole in the left. The positions of the holes were determined from the ZEMAX layout.

The 36 mm minimum radius of the left hole in the baffle was determined by a diffraction analysis to cause a negligible vignetting of the Hartmann beam. (TBD see TCS reference); the hole radius was increased to 42mm to allow for misalignment of the baffle. The elliptical size of the right hole in the baffle allows passage of the incident and reflected signal recycling main beam without vignetting causing a signal recycling power loss > 100 ppm.

The results of the FEA model show that the lowest internal mode frequency of the baffle is > 150 Hz TBD.

Figure 25: SR2 Scraper Baffle, H2

## HAM SCRAPER BAFFLE

A model of the HAM Scraper Baffle is shown in Figure 26. The locations of the IFO beams and the Hartmann beam that traverse the HAM Scraper Baffle were determined from the ZEMAX layout.

The 30 mm minimum radius of the hole in the baffle causes a negligible vignetting of the Hartmann beam.

Figure 26: HAM Scraper Baffle

The baffle is mounted directly to the HAM ISI table and must meet the requirement that the lowest internal frequency be > 150 Hz.

The results of the FEA model show that the lowest internal mode frequency of the baffle is approximately 167 Hz, as shown in Figure 27, and meets the design requirement.

Figure 27: Internal Frequencies of HAM Scraper Baffle Assembly

## SRM HR BAFFLE

A model of the SRM HR Baffle is shown in Figure 28. The locations of the IFO beams was determined from the ZEMAX layout.

The hole in the baffle is 25mm diameter, which is larger than the 20mm limiting aperture of the OFI.

Figure 28: SRM HR Baffle

## HARTMANN Beam Dump

A model of the Hartmann Beam Dump is shown in Figure 29.

The Hartmann Beam Dumps catch the 1064nm light that transmits through the first two dichroic  steering mirrors in the Hartmann beam paths.

The results of the FEA model show that the lowest internal mode frequency of the baffle is 325 Hz; see Error! Reference source not found..

Figure 29: Hartmann Beam Dump

Figure 30: FEA Analysis of Hartmann Beam Dump

## BAFFLE HEIGHTS

The heights of the signal recycling cavity baffles above the HAM ISI table and the hole dimensions are shown in Table 1.

## OPTICAL INTERFACES

The locations of the IFO beams and the Hartmann beams that traverse the SR Baffle were determined from the ZEMAX layout, D0901920 H1 Zemax layout, D0902345 H2 Zemax Layout, and D0902216 L1 Zemax layout.

A sequential ZEMAX model was made for the signal recycling cavities of H2, H1, and L1 IFOs, and the physical optics propagation program was used to determine the diffraction beam profiles at the locations of the baffles.

The holes in the SR3 HR baffle, SR2 Scraper baffle, SR2 AR baffle, and SRM HR baffle are larger than the 1E-3 radius of the diffraction beam profile that propagates through the signal recycling cavity optical train and will not vignette the beam appreciably; in addition, the holes are large enough to allow passage of the diffracted Hartmann probe beams from the ITMX and ITMY mirror surfaces; see Table 1.

Table 1: Heights and Sizes of SR Baffles

| IFO | Baffle | 1/e^2 radius | ZEMAX 1E-4 radius | Hartmann beam radius requirement | Baffle hole radius | Height above table |
| --- | --- | --- | --- | --- | --- | --- |
| H2 |  |  |  |  |  |  |
|  | SR3 HR baffle | 54.30 | 117.0 | maximum | 132.5 | 211.0 |
|  | SR2 HR scraper baffle | 7.99 | 18.4 | 36.0 | 42 | 193.2 |
|  | HAM (SR2 AR) scraper baffle | 4.22 | N/A | 30.0 | 30 | 187.4 |
|  | HAM (Hartmann) Scraper baffle | 4.22 | N/A | 30.0 | 30 | 187.4 |
|  | SRM HR baffle | 2.05 | 5.9 |  | 14 | 176.2 |
| H1 |  |  |  |  |  |  |
|  | SR3 HR baffle | 54.30 | 118.6 | 85 | 132.5 | 230.2 |
|  | SR2 HR scraper baffle | 9.59 | 21.3 | 36.0 | 42 | 220.9 |
|  | SR2 AR scraper baffle | 5.06 | N/A | 30 | 30 | 220.0 |
|  | Hartmann Scraper baffle | 5.06 | N/A | 30 | 30 | 220.0 |
|  | SRM HR baffle | 2.05 | 4.5 |  | 14 | 210.9 |
| L1 |  |  |  |  |  |  |
|  | SR3 HR baffle | 54.30 | 118.6 | 85 | 132.5 | 230.2 |
|  | SR2 HR scraper baffle | 9.59 | 21.3 | 36.0 | 42 | 239.7 |
|  | SR2 AR scraper baffle | 5.06 | N/A | 30 | 30 | 232.5 |
|  | Hartmann Scraper baffle | 5.06 | N/A | 30.0 | 30 | 232.5 |
|  | SRM HR baffle | 2.05 | 4.5 |  | 14 | 230.1 |

In every instance, the hole radius is 8mm greater than the 1E-4 radius of signal recycling cavity beam; therefore, the horizontal and vertical tolerance in placement of the baffles is +/- 8mm. This meets the clear aperture requirement.

# SCATTERED LIGHT DISPLACEMENT NOISE

## Scattered Light Requirement

A DARM signal is obtained when the differential arm length is modulated as a result of a gravity wave strain. The DARM signal was calculated in reference, T060073-00 Transfer Functions of Injected Noise, and is defined by the following expression:

Where L is the arm length, hSRD is the minimum SRD gravity wave strain spectral density requirement, P0 is the input laser power into the IFO, and DARM is the signal transfer function.

In a similar manner, an apparent signal (scattered light noise) occurs when a scattered light field with a phase shift is injected into the IFO at some particular location, e.g. through the back of the ETM mirror. The scattered light noise is defined by the following expression:

PSNi is the scattered light power injected into the IFO mode, δSN is the phase shift of the injected field, and SNXXX is the noise transfer function for that particular injection location.

The phase shift spectral density of the injected field due to the motion of the scattering surface is given by

where xs is the spectral density of the longitudinal motion of the scattering surface.

In general, the different scattering sources are not coherent and must be added in quadrature. The requirement for total scattered light displacement noise can be stated with the following inequality:

The SNXXX/DARM scattered light noise transfer function ratios for various injection locations within the IFO are shown in Figure 31: Scattered Light Noise Transfer Functions.

Figure 31: Scattered Light Noise Transfer Functions

### Scattered Light Parameters

The arm cavity power was taken from T070303 with an arm cavity gain of 13000 referenced to the PSL input power of 125 W.

Motion of HEPI @ 200 Hz, m/rt Hz

Motion of HAM table @ 100 Hz, m/rt Hz

solid angle of IFO mode, sr

laser wavelength, m

wave number, m^-1

Transfer function @ 100 Hz, BS from SR

IFO waist size, m

Gaussian power parameter

in recycling cavity

input laser power, W

arm cavity gain

arm cavity power, W

power in power recycling cavity both arms, W

power in recycling cavity arm, W

refl port signal ratio

as port signal ratio

power after SRM, W

reflectivity of BS HR

reflectivity of BS AR

Reflectivity of ITM HR

Reflectivity of ITM AR

transmissivity of SRM HR

power in signal recycling cavity, W

transmissivity of SR2 AR

Reflectivity of dichroic HWSX M1

Reflectivity of dichroic HWSX M2

Reflectivity of HWSX M3

Reflectivity of HWSY M4

Reflectivity of HPX-F1

Reflectivity of HWSY M5

BRDF of HPX-F1 @ 3 deg, sr^-1

Beam Waist after H1 SR3

Beam waist after H1 SR2

Beam Waist after H1 HPYF1

Beam waist after H1 HPXF1

Beam Waist after H2 SR3

Beam waist after H2 SR2

Beam Waist after H2 HPYF1

Beam waist after H2 HPXF1

transmissivity of SR2 HR

### BRDF of Baffle Surfaces

The baffle surfaces are oxidized polished stainless steel, with a measured BRDF < 0.03 sr^-1 @ > 5 deg incidence angle.

### HAM ISI Seismic Motion

The seismic motion of the HAM ISI optical table at LLO and the HAM chamber viewport motions are shown below in Figure 32.

Figure 32: HAM optics table Seismic Motion, m/rtHz

### Naming Convention for Wedged Optics

Figure 33: Wedged Core Optic ghost beam naming convention

Figure 34: BS ghost beam naming convention

### SR3 HR Baffle Scatter

The SR3 HR Baffle catches ghost beams of order GB4 and higher, and the scattered light displacement noise from these beams is negligible.

### SR3 AR Baffle Scatter

The SR3 AR Baffle catches 1) the transmission of the main through the SR3 AR surface and scatters light back toward the BS, and 2) the SR3 GBAR3 ghost beam.

The scattered light displacement noise caused by scattering from the SR3 AR Baffle is calculated below.

#### Transmission of Signal Recycling Cavity Main Beam through SR3 HR

The signal recycling cavity has two counter propagating beams that strike the SR3 HR surface.

power incident on SR3 AR Baffle

(forward and backward beams), W

The beam incident from the BS is scattered by the SR3 AR Baffle back toward the BS, directly into the mode of the IFO.

power scattered from  SR3 AR Baffle toward BS, W

The beam incident from SR2 is scattered by the SR3 AR Baffle back toward SR2, into the mode of the beam waist created by the SR3 mirror curvature.

power scattered from  SR3 AR Baffle toward SR2 W

The total power scattered is given by

power scattered from  SR3 AR Baffle, W

This scattered light from the signal recycling cavity enters the IFO mode through the BS; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### SR3 GBAR3 Ghost Beam

The SR3 GBAR3 ghost beams from the two counter propagating signal recycling cavity beams are caught on the SR3 AR Baffle.

The scattered light displacement noise caused by scattering from the SR3 AR Baffle is calculated below.

power incident on GBAR3 AR Baffle

(forward and backward beams), W

The GBAR3 beam incident from the BS is scattered back toward the BS, directly into the mode of the IFO.

power scattered from  SR3 AR Baffle toward BS, W

The other GBAR3 beam, incident from the SR2, scatters back toward SR2 into the mode of the beam waist created by the SR3 mirror curvature.

power scattered from  SR3 AR Baffle toward SR2, W

The total power scattered is given by:

total power scattered from  SR3 AR Baffle, W

This scattered light from the signal recycling cavity enters the IFO mode through the BS; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### SR3 GBHR3 Ghost Beam

The SR3 GBHR3 ghost beams from the two counter propagating signal recycling cavity beams will hit the mode cleaner tube wall and scatter back toward the signal recycling cavity.

power incident on SR3 GBHR3

(forward and backward beams),  W

The GBHR3 beam incident from the BS is scattered back toward the BS, directly into the mode of the IFO.

power scattered from  SR3 GBHR3 toward BS, W

The other GBHR3 beam, incident from the SR2, scatters back toward SR2 into the mode of the beam waist created by the SR3 mirror curvature.

power scattered from  SR3 GBHR3 toward SR2 W

The total scattered power is given by

total power scattered from SR3 GBHR3

This scattered light from the signal recycling cavity enters the IFO mode through the BS; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

### SR2 Scraper Baffle Scatter

The SR2 scraper baffles on HAM4, and HAM10 traps half of the ghost beams from the ITM, CP, and BS; the other half of the ghost beams is trapped by the PR2 scraper baffles located on HAM3 and HAM9.

The scattered light displacement noise caused by scattering from the SR2 Scraper Baffle is calculated below.

#### ITM Ghosts Beams

The X and Y ITM ghost beams are coherent but may have different phase. For the worst case, we will assume that the fields add in phase.

ITM_GBAR1 H1

Power incident on SR2 Scraper Baffle from both arms, W

both ITM AR1 BD  scattered power into BS

from SR2 Scraper baffle, W

displacement noise @ 100 Hz, m/rtHz

ITM_GBAR3 H1

power incident on SR2 Scraper Baffle from both arms, W

power scattered from  SR2 Scraper Baffle, W

displacement noise @ 100 Hz, m/rtHz

#### BS Ghosts Beam

The beam splitter ghost beams from both arms are almost anti-resonant and the wave fronts overlap; therefore, their coherent sum is reduced by the square of the asymmetry coefficient for common mode field rejection.

BS_GBAR3P H1

power scattered from  SR2 Scraper Baffle, W

displacement noise @ 100 Hz, m/rtHz

#### CP Ghosts Beam

The X and Y CP ghost beams are coherent but may have different phase. For the worst case, we will assume that the fields add in phase.

##### CP_GBAR1 H1

power incident on SR2 Scraper Baffle from both arms, W

power scattered from  SR2 Scraper Baffle, W

displacement noise @ 100 Hz,

m/rtHz

###### CP_GBAR3 H1

power incident on SR2 Scraper Baffle from both arms, W

power scattered from  SR2 Scraper Baffle, W

displacement noise @ 100 Hz, m/rtHz

#### Summary SR2 Scraper Baffle Scatter

Figure 35: SR2 Scraper Baffle Scatter

#### SRM GBAR3 Ghost Beam

The SRM GBAR3 ghost beam is caught on the input baffle of the Output Faraday; it will scatter from the baffle toward the SRM and enter the signal recycling cavity.

power incident on SRM AR Baffle, W

The GBAR3 beam is scattered back toward SRM, into the mode of the beam waist created by the SRM mirror transmission.

power scattered from  SRM AR Baffle, W

The scattered light enters the IFO mode through SRM; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### SRM GBHR3 Ghost Beam

The SRM GBHR3 ghost beam is caught on the Mode Cleaner Tube Baffle; it will scatter from the baffle back toward the SRM and enter the signal recycling cavity.

power of SRM GBHR3,  W

The SRM GBHR3 beam is scattered back toward SRM, into the mode of the beam waist created by transmission through the SRM.

power scattered from  SRM GBHR3 Mode Cleaner Tube Baffle, W

The scattered light enters the IFO mode through SRM; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### Summary SR3, SR2, SRM Ghost Beam Scatter

Figure 36: Summary of SR Ghost Beam Scatter

### H2 Hartmann Y Scatter

The 1064nm power recycling cavity beam from the Y-arm follows the Hartmann Y path: 1) reflection from the BS AR, 2) reflection from dichroic mirror HWSYM1, 3) reflection from dichroic mirror HWSYM2, 4) reflection from HWSYM3, 5) reflection from HWSYM4, 6) reflection from HWPYF1, and 7) reflection from HWSYM5; see Figure 3. The scattered light enters the IFO mode through the ITMy AR surface.

#### Scattered Light Displacement Noise from H2 HWSYM1

The Hartmann Y beam will scatter from the HWSYM1 mirror back toward the ITM AR, into the mode of the beam waist created by the SR3 mirror.

power in signal recycling cavity, W

power incident on HWSY M1, W

power scattered from  HWSY M1, W

The scattered light enters the IFO mode through the ITM AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### Scattered Light Displacement Noise from H2 HWSYM2

The Hartmann Y beam will scatter from the HWSYM2 mirror back toward the ITM AR, into the mode of the beam waist created by the SR3 mirror.

power incident on HWSY M2, W

power scattered from  HWSY M2, W

The scattered light enters the IFO mode through the ITM AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### Scattered Light Displacement Noise from H2 HPY-F1

The Hartmann Y beam will scatter from the HPY-F1mirror back toward the ITM AR, into the mode of the beam waist created by the SR3 mirror.

power incident on HPY-F1, W

power scattered from  HPY-F1, W

The scattered light enters the IFO mode through the ITM AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### H2 Hartmann Y Viewport Scatter

The Hartmann Y beam will scatter from the HAM chamber viewport back toward the ITM AR surface, into the mode of the beam waist created by the HPYF1 mirror.

power incident on Hartmann Y viewport, W

power scattered from  Hartmann y viewport, W

The scattered light enters the IFO mode through the ITM AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### H2 Hartmann Y Viewport Reflection, HAM Chamber Scatter

Part of the Hartmann Y beam will reflect from the HAM chamber viewport and scatter from the chamber wall back toward the ITM AR surface, into the mode of the beam waist created by the HPYF1 mirror.

power incident on Hartmann Y viewport reflected wall, W

power scattered from  Hartmann y viewport reflected wall, W

The scattered light enters the IFO mode through the ITM AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### Summary of H2 Hartmann Y Scatter

Figure 37: Summary of H2 Hartmann Y Surfaces Scatter

### H2 Hartmann X Scatter

The 1064nm signal recycling cavity beam transmitted through the BS from the X-arm follows the Hartmann X path 1) transmission through the SR2 AR, 2) reflection from dichroic mirror HWSXM1, 3) reflection from dichroic mirror HWSXM2, 4) reflection from mirror HWSXM3, 5) reflection from mirror HWSXM4, 6) reflection from HWPXF1, and 7) reflection from HWSXM5, as seen in Figure 3.

The scattered light enters the IFO mode through the BS from the signal recycling cavity side.

The signal power transmitting through the SRM mirror is

The power inside the signal recycling cavity is given by

power in signal recycling cavity, W

#### Scattered Light Displacement Noise from H2 HWSXM1

The Hartmann X beam will scatter from the HWSXM1 mirror back toward the BS, into the mode of the beam waist created by the SR2 mirror.

power incident on HWSX M1, W

power scattered from  HWSX M1, W

The scattered light enters the IFO mode from the signal recycling cavity through the BS AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### Scattered Light Displacement Noise from H2 HWSXM2

The Hartmann X beam will scatter from the HWSXM2 mirror back toward the BS, into the mode of the beam waist created by the SR2 mirror.

power incident on HWSX M2, W

power scattered from  HWSX M2, W

The scattered light enters the IFO mode from the signal recycling cavity through the BS AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### H2 Scattered Light Displacement Noise from HWSXM3

The Hartmann X beam will scatter from the HWSXM2 mirror back toward the BS, into the mode of the beam waist created by the SR2 mirror.

power incident on HWSX M3, W

power scattered from  HWSX M3, W

The scattered light enters the IFO mode from the signal recycling cavity through the BS AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### H2 Scattered Light Displacement Noise from HWSXM4

The Hartmann X beam will scatter from the HWSXM2 mirror back toward the BS, into the mode of the beam waist created by the SR2 mirror.

power incident on HWSX M4, W

power scattered from  HWSX M4, W

The scattered light enters the IFO mode from the signal recycling cavity through the BS AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### H2 Scattered Light Displacement Noise from HPXF1

The Hartmann X beam will scatter from the HWSXM2 mirror back toward the BS, into the mode of the beam waist created by the SR2 mirror.

power incident on HPXF1, W

power scattered from  HPXF1, W

The scattered light enters the IFO mode from the signal recycling cavity through the BS AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### H2 Hartmann X Viewport Scatter

The Hartmann X beam will scatter from the HAM chamber viewport back into the signal recycling cavity, and into the mode of the beam waist created by the HPXF1 mirror.

power incident on Hartmann X viewport, W

power scattered from  Hartmann x viewport, W

The scattered light enters the IFO mode from the signal recycling cavity through the BS AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### H2 Hartmann X Viewport Reflection, HAM Chamber Scatter

Part of the Hartmann X beam will reflect from the HAM chamber viewport and scatter from the chamber wall back into the signal recycling cavity, and into the mode of the beam waist created by the HPXF1 mirror.

power incident on Hartmann X viewport reflected wall, W

power scattered from  Hartmann y viewport reflected wall, W

The scattered light enters the IFO mode from the signal recycling cavity through the BS AR side; the displacement noise is given by

displacement noise @ 100 Hz, m/rtHz

#### Summary of H2 Hartmann X Scatter

Figure 38: Summary of H2 Hartmann X Surfaces Scatter

#### Summary of H2 Hartmann X Viewport Scatter

The scattered light displacement noise from the Hartmann beam viewports is negligible, as shown in Figure 39. Therefore, the Hartmann Viewport Beam dumps will be eliminated.

Figure 39: Summary of H2 Hartmann Viewport Scatter

### H1 & L1 Hartmann Beam Scatter

The scattered light displacement noise calculations for H1, and L1 are similar to those presented for H2. The results of the calculations will be presented in the following.

#### H1 & L1 Hartmann X Arm

The 1064nm power recycling cavity beam from the X-arm follows the Hartmann X path: 1) reflection from the BS AR, 2) reflection from dichroic mirror HWSXM1, 3) reflection from dichroic mirror HWSXM2, 4) reflection from HPXF1, 5) reflection from HWSXM4, and 6) reflection from HWSXM5, as seen in Figure 1. The scattered light enters the IFO mode through the ITM AR surface.

HWSX M1

displacement noise @ 100 Hz, m/rtHz

HWSX M2

displacement noise @ 100 Hz, m/rtHz

HPX-F1

displacement noise @ 100 Hz, m/rtHz

Hartmann X viewport scatter

displacement noise @ 100 Hz, m/rtHz

Hartmann X viewport reflected wall scatter

displacement noise @ 100 Hz, m/rtHz

#### H1 & L1 Hartmann Y Arm

The 1064nm signal recycling cavity beam transmitted through the BS from the Y-arm follows the Hartmann Y path: 1) transmission through the SR2 AR, 2) reflection from dichroic mirror HWSYM1, 3) reflection from dichroic mirror HWSYM2, 4) reflection from mirror HWSYM3, 5) reflection from mirror HWSYM4, 6) reflection from HPYF1, and 7) reflection from HWSYM5, as seen in Figure 1. The scattered light enters the IFO mode through the BS from the signal recycling cavity side.

HWSY M1

displacement noise @ 100 Hz, m/rtHz

The scattered light displacement noise from HWSY M2, HWSY M3, HWSY M4, HPYF1, HWSY M5, Hartmann viewport scatter, and Hartmann viewport reflected wall scatter are negligible because the incident power has been attenuated by the dichroic mirrors and the AR surface of the viewport.

#### Summary of H1 & L1 Hartmann Scatter

Figure 40: Summary of H1 & L1 Hartmann X and Y Scatter

# INTERFACE CONTROL DOCUMENT

The mechanical and optical interfaces of the Manifold/cryopump Baffle and the Mode Cleaner Tube Baffles are described in E1100583 SLC Manifold/Cryopump Baffle Interface Control Document.

.

# Text boxes

SR2 Scraper Baffle

Hartmann Beam Dump (typical)

SRM HR Baffle

SR3 AR Baffle

SR2 Scraper Baffle

HAM Scraper Baffle (SR2 AR Baffle)

Hartmann Scraper Baffle

HAM Scraper Baffle (SR2 AR Baffle)

OFI

OFI

SRM

SR2

SR3

SR2

SR3

SR2

SRM HR Baffle

SR3 AR Baffle

SR3 HR Baffle

Hartmann Scraper Baffle

SR3 HR Baffle

Hartmann Beam Dump (typical)