LIGO Laboratory / LIGO Scientific Collaboration

LIGO- E1100858-V4 	                 LIGO                   November 25th, 2013

L1 BSC 4 BSC-ISI, Pre-integration Testing report,

Phase II

E1100858-V4

Adrien Le Roux, Céline Ramet

Distribution of this document:

Advanced LIGO Project

This is an internal working note

of the LIGO Laboratory

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

Table of contents:

Introduction	4

1.	Phase II- A – Before Install	5

1.	Hardware changes	5

1.	CPS – E1100369	5

2.	GS13 – E1100740	5

3.	L4C – E1100740	5

4.	T240 – E1100740	5

5.	Cables – E1100822	5

6.	Misc	5

2.	Electronic Inventory	6

3.	Models Modifications	6

4.	Mass distribution	7

1.	Seismic	7

2.	Suspension	8

3.	Misc	8

4.	Total	9

5.	Basic functionalities just after installing the BSC-ISI on the test stand	9

1.	Pressure sensors	9

2.	Spectra	10

3.	Actuators-cables resistance	10

4.	Offsets CPS Unlocked vs locked	11

5.	Offset local drive	11

6.	Offset Cartesian drive	12

7.	Range of motion	13

8.	Linearity test	13

6.	Transfer functions and Comparison with measurements done in the staging building.	15

1.	At the end station	15

2.	Comparisons with LHO ETMX	19

3.	Comparisons with measurements in the Staging Building	24

2.	Phase II-B – After Install	29

1.	Hardware changes	29

1.	CPS – E1100369	29

2.	GS13 – E1100740	29

3.	L4C – E1100740	29

4.	T240 – E1100740	29

5.	Cables – E1100822	29

6.	Misc	29

2.	Electronic Inventory	30

3.	Models Modifications	30

4.	Mass distribution	31

1.	Seismic	31

2.	Suspension	32

3.	Misc	32

4.	Total	33

5.	Basic functionalities just after installing the BSC-ISI on the test stand	33

1.	Pressure sensors	33

2.	Spectra	34

3.	Actuators-cables resistance	34

4.	Offsets CPS Unlocked vs locked	35

5.	Offset local drive	35

6.	Offset Cartesian drive	36

7.	Range of motion	37

8.	Linearity test	37

6.	Transfer functions and Comparison with measurements done in the staging building.	39

1.	In Chamber (Dome off)	39

7.	Conclusion Phase II-B – After Install	52

Introduction

The BSC-ISI testing is performed in three phases:

1) BSC-ISI, Pre-integration Testing, Phase I (post-assembly, in the staging building)

2) BSC-ISI, Pre-integration Testing, Phase II: Final tests done before insertion in the chamber
3) BSC-ISI, Integration Phase Testing: Procedure and results related to the commissioning in the chamber.

The ISI-BSC4 was moved from the Staging building to the X End early 2013. Then the ISI was placed on the test stand a few days later.

This document presents results from the series of tests (Phase II) performed on the ISI-BSC4 (ETMX) at the X End station. The tests were done with the ETMX quadruple suspension and the TMS suspension installed in their final version.

First tests started on October 23rd, 2013. The first testing phase (II-a validation before cartridge installation) was completed on October, 2013.

All results are posted on the SVN at:

https://svn.ligo.caltech.edu/svn/seismic/BSC-ISI/L1/ETMX/

The following types of documents can be found in the SVN:

- Data location

- Figures location

# Phase II- A – Before Install

## Hardware changes

### CPS – E1100369

CPS have not been replaced since phase I testing in the staging building.

### GS13 – E1100740

GS13 have not been replaced since phase I testing in the staging building.

### L4C – E1100740

L4C have not been replaced since phase I testing in the staging building.

### T240 – E1100740

T240s have not been replaced since phase I testing in the staging building.

### Cables – E1100822

No cables have been changed since phase I testing in the staging building.

Note: The SRS cables have been added and routed on the ISI.

### Misc

No hardware changes since phase I testing in the staging building.

## Electronic Inventory

This table reports the electronic equipment used in the LVEA.

| Hardware | Ligo reference | S/N |
| --- | --- | --- |
| Interface Chassis Pod 1 | D1002432 | S1203884 |
| Interface Chassis Pod 2 | D1002432 | S1203885 |
| Interface Chassis Pod 3 | D1002432 | S1203886 |
| Anti-aliasing Chassis Pod 1 | D1002693 | S1203106 |
| Anti-aliasing Chassis Pod 2 | D1002693 | S1203107 |
| Anti-aliasing Chassis Pod 3 | D1002693 | S1203109 |
| Binary Input Chassis 1 | D1001726 | S1101306 |
| Binary Input Chassis 2 | D1001726 | S1101307 |
| Binary Output Chassis | D1001728 | S1101333 |
| T240 Interface Pod 1 | D1002694 | S1201405 |
| T240 Interface Pod 2 | D1002694 | S1201406 |
| T240 Interface Pod 3 | D1002694 | S1201407 |
| Anti-image Chassis | D070081 | S0900067 |
| Coil driver Pod 1 | D0902744 | S1103314 |
| Coil driver Pod 2 | D0902744 | S1103336 |
| Coil driver Pod 3 | D092744 | S1103360 |
| Expansion chassis |  | L1seiex |

Table 1 - Electronic inventory

## Models Modifications

No model modifications were done between the beginning and the end of Phase 2a testing.

## Mass distribution

At this point, all the final masses are installed on the BSC-ISI except the Ballast masses on top of the keel. Instead, we have a big leg element (D972213). Those ballast masses will be installed while the BSC is in chamber.

### Seismic

Stage 1

| Stage 1 | HighBay (lbs) | LVEA (lbs) | LVEA (kg) |
| --- | --- | --- | --- |
| Corner 1 | 49.22 | 49.22 | 22.33 |
| Corner 2 | 22.86 | 22.86 | 10.37 |
| Corner 3 | 32.22 | 32.22 | 14.61 |
| Total | 104.3 | 104.3 | 47.31 |

Note: The budget mass didn’t change on Stage 1 between the Highbay and the X End because on this Unit, we installed the Vibration Absorbers in the Highbay and balanced the BSC with them already on.

Stage 2

The seismic masses on BSC 4 are:

- On the side and on the Keel: 			921.7 lbs (=418.08 kg)

- On the Optical Table (6) D1003161:		285.72 lbs (=129.6 kg)

The total of masses on Stage 2 is:			1207.42 lbs (=547.68 kg).

### Suspension

The quad structure and the TMS Structure was weighed to be:

| SUS | Weight (lbs) | Weight (kg) |
| --- | --- | --- |
| Upper structure | 266 | 120.66 |
| Lower structure | 531 | 240.86 |
| Total | 797 | 361.5128 |

| TMS | Weight (lbs) | Weight (kg) |
| --- | --- | --- |
| Total | 456.14 | 206.9 |

### Misc

- 44 lbs = quad sleeve [Betsy’s alog 3621]

- 2 lbs = quad sleeve wedges [estimate]

- 5 lbs = cabling [estimate]

- 2 lbs cable brackets [estimate]

- 28 lbs = Vibration absorbers, quantity 4 [from E1000337-v2: 12.7 kg = 28 lbs]

- 3 lbs = Ring heater + brackets + cables [estimate]

Total Weight for Suspension: 906 lbs = 412 kg

Total Weight for TMS: 456.14 lbs = 206.9 kg

### Total

Nominal mass hanging on stage 0-1 blades (without stage 2): 912Kg – 2010lb

Nominal mass hanging on stage 1-2 blades: 2830Kg – 6239lb

Nominal payload on stage 1: 109Kg – 240lb

Nominal payload on stage 2: 1185Kg – 2612lb

|  |  |  | Staging Bldg | X End |  |
| --- | --- | --- | --- | --- | --- |
|  | Plan | 07/18/2012 | Detail | Overall | Difference |
| Stage 1 (kg) | 108.86 | 47.31 | 47.31 | 0.00 |
| Stage 2 (kg) | Masses | 1183.42 | 1155.53 | 547.68 | 1166.97 | 11.44 |
|  | Suspension | N/A | N/A | 361.51 |  |  |
|  | Miscellaneous | N/A | N/A | 50.88 |  |  |
|  | TMS | N/A | N/A | 206.9 |  |  |
| Total (kg) | 1292.28 | 1200.79 | 1214.28 | 13.49 |

Even if Stage 2 weight difference between the Staging Building and the X End is a little bit over the 10 kg requirement, we’re still going to pass this test because the weight for the quad and the TMS structure are estimated. Overall, the mass budget is fairly consistent with what we had in the Staging Building.

Test result:                                              Passed:   X             Failed:         .   W Waived:   _

## Basic functionalities just after installing the BSC-ISI on the test stand

### Pressure sensors

All pressure sensors are working correctly.

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/
L1_ISI_ETMX_Pressure_Sensors_Check_Calibrated_2013_10_24_084142.mat

|  | Pressure (KPa) |
| --- | --- |
| Sensors | Corner 1 | Corner 2 | Corner 3 |
| ST1-L4C-P | 100.91 | 100.37 | 101.99 |
| ST1-L4C-D | -0.70 | 0.13 | -1.31 |
| ST1-GS13-P | 101.80 | 102.25 | 102.54 |
| ST1-GS13-D | 0.25 | -0.26 | -0.70 |
| ST1-T240-P | 100.75 | 100.95 | 100.85 |

Table 2 - Geophones Pressure sensors

Test result:                                              Passed:   X              Failed:         .   W Waived:   _

### Spectra

Spectra of the instrument can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Spectra/Undamped/

L1_ISI_ETMX_ASD_m_LOC_CPS_T240_L4C_GS13_2013_10_24_120444.mat

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ITMY/Data/Figures/Spectra/Undamped/
L1_ISI_ETMX_ASD_m_LOC_CPS_T240_L4C_GS13_2013_10_24_120444.fig

Figure 1 - Spectra inboard instruments - ISI Unlocked

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Actuators-cables resistance

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/

|  | Stage 1 | Stage 2 |
| --- | --- | --- |
|  | H1 | H2 | H3 | V1 | V2 | V3 | H1 | H2 | H3 | V1 | V2 | V3 |
| Script |  |  |  |  |  |  |  |  |  |  |  |  |

Test result:                                              Passed:                 Failed:         .   W Waived:   X__

### Offsets CPS Unlocked vs locked

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/

- L1_ISI_ETMX_CPS_Read_Back_ISI_UnLocked_2013_10_24_095724.mat

- L1_ISI_ETMX_CPS_Read_Back_ISI_UnLocked_2013_10_24_100154.mat

|  | Table locked | Table unlocked | Difference locked - unlocked |
| --- | --- | --- | --- |
| Sensors | Offset (Mean) | Std deviation | Offset (Mean) | Std deviation | Offset (Mean) | mil |
| ST1 - H1 | 255.80 | 8.28 | 113.57 | 124.73 | 142.23 | 0.17 |
| ST1 - H2 | -39.95 | 5.26 | 288.17 | 102.88 | -328.13 | -0.39 |
| ST1 - H3 | 126.76 | 6.45 | 1259.59 | 143.30 | -1132.83 | -1.35 |
| ST1 - V1 | 219.47 | 5.22 | 30.00 | 107.37 | 189.46 | 0.23 |
| ST1 - V2 | 69.60 | 6.47 | 1025.93 | 133.10 | -956.33 | -1.14 |
| ST1 - V3 | 186.21 | 5.76 | -833.42 | 128.01 | 1019.64 | 1.21 |
| ST2 - H1 | 1038.03 | 102.75 | -1240.21 | 151.05 | 2278.24 | 0.68 |
| ST2 - H2 | 450.40 | 44.86 | -1375.43 | 141.42 | 1825.83 | 0.54 |
| ST2 - H3 | -983.72 | 101.36 | -1406.99 | 181.60 | 423.27 | 0.13 |
| ST2 - V1 | -408.11 | 726.67 | -1375.90 | 261.12 | 967.78 | 0.29 |
| ST2 - V2 | -328.54 | 90.34 | -1637.08 | 307.65 | 1308.54 | 0.39 |
| ST2 - V3 | 313.32 | 480.33 | 1959.48 | 287.11 | -1646.15 | -0.49 |

Table 3 - Locked vs Unlocked Position

Note: The Standard Deviations are a little bit high on the “Table Locked” measurements, especially on Stage 2 V1 and Stage 2 V3.

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Offset local drive

Note: Due to longer cables, offsets measured by CPS for a 7000 count drive are slightly lower than offsets measured in the staging building.

Results of this test can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/

- L1_ISI_ETMX_Offset_Local_Drive_20131025.mat

|  | Sensors |
| --- | --- |
|  |  | ST1 - H1 | ST1 - H2 | ST1 - H3 | ST1 - V1 | ST1 - V2 | ST1 - V3 |
| Actuators | ST1 - H1 | 3701.37 | 1482.45 | 1497.08 | 48.93 | -33.56 | -1.78 |
|  | ST1 - H2 | 1496.44 | 3724.43 | 1516.44 | 52.18 | -50.55 | -44.10 |
|  | ST1 - H3 | 1468.61 | 1479.49 | 3661.69 | 32.40 | -15.05 | 12.65 |
|  | ST1 - V1 | 55.29 | -102.22 | 86.06 | 2927.23 | -494.07 | -476.11 |
|  | ST1 - V2 | 71.04 | 4.51 | -137.19 | -394.34 | 2788.68 | -473.57 |
|  | ST1 - V3 | -127.05 | 57.26 | 78.95 | -413.50 | -453.39 | 2828.51 |

Table 4 - Static Tests – Local to Local - Stage 1

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - H1 | ST2 - H2 | ST2 - H3 | ST2 - V1 | ST2 - V2 | ST2 - V3 |
| Actuators | ST2 - H1 | 2107.61 | 388.27 | 280.63 | -18.52 | -75.28 | -69.35 |
|  | ST2 - H2 | 327.28 | 2103.51 | 341.11 | 9.61 | -1.57 | -46.51 |
|  | ST2 - H3 | 301.56 | 353.75 | 2119.46 | -30.66 | -50.13 | 15.27 |
|  | ST2 - V1 | 53.34 | 129.39 | -149.25 | 2445.87 | 325.62 | 40.76 |
|  | ST2 - V2 | -170.12 | 114.95 | 83.92 | 33.98 | 2459.01 | 336.28 |
|  | ST2 - V3 | 57.22 | -104.97 | 65.03 | 315.18 | -6.71 | 2468.23 |

Table 5 - Static Tests – Local to Local - Stage 2

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Offset Cartesian drive

The test was not performed because it only tests the matrices, which can be changed at any time.

Test result:                                              Passed:   _              Failed:         .   W Waived:   X_

### Range of motion

The range of motion of the table is measured by pushing on the table in a direction collinear to the CPS. The Static tests results can be found on the SVN at:

https://svn.ligo.caltech.edu/svn/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/

- L1_ISI_ETMX_Range_Of_Motion_20131025.mat

| Sensor readout (counts) | Negative drive | Positive drive | Amplitude count | mil |
| --- | --- | --- | --- | --- |
| ST1 - H1 | -16136.9 | 15561.45 | 31698.31 | 37.73608 |
| ST1 - H2 | -15008.2 | 16094.72 | 31102.95 | 37.02732 |
| ST1 - H3 | -14733.4 | 15607.66 | 30341.07 | 36.12032 |
| ST1 - V1 | -12102.3 | 12540.51 | 24642.79 | 29.33665 |
| ST1 - V2 | -10705.7 | 13348.43 | 24054.09 | 28.63582 |
| ST1 - V3 | -12766.5 | 11527.18 | 24293.65 | 28.92101 |
| ST2 - H1 | -9869.56 | 8417.626 | 18287.19 | 5.442616 |
| ST2 - H2 | -9986.07 | 8101.874 | 18087.94 | 5.383315 |
| ST2 - H3 | -10012.2 | 8177.971 | 18190.17 | 5.413741 |
| ST2 - V1 | -11538.3 | 9632.988 | 21171.32 | 6.300988 |
| ST2 - V2 | -11696.5 | 9639.022 | 21335.5 | 6.349852 |
| ST2 - V3 | -8203.01 | 13097.67 | 21300.68 | 6.339489 |

Table 6 - Range of motion - Actuator drive in the LVEA

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Linearity test

The data of the linearity test can be found on the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Linearity_Test/

- L1_ISI_ETMX_Linearity_test_20131025.mat

The figures of the linearity test can be found on the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic\BSC-ISI\H2\BS\Data\Figures\Linearity_Test\

- L1_ISI_ETMX_Linearity_test_20131025.fig

Figure 2 - Linearity test –L1 - BS – In LVEA

|  |  | Slope | Offset | Average slope | Variation from average(%) |
| --- | --- | --- | --- | --- | --- |
| Stage 1 | ST1 - H1 | 0.53259 | -135.3 | 0.5297 | -0.5 |
|  | ST1 - H2 | 0.53324 | 81.5 |  | -0.7 |
|  | ST1 - H3 | 0.52321 | 1018.7 |  | 1.2 |
|  | ST1 - V1 | 0.40990 | 221.1 | 0.4050 | -1.2 |
|  | ST1 - V2 | 0.40019 | 1340.8 |  | 1.2 |
|  | ST1 - V3 | 0.40483 | -632.7 |  | 0.0 |
| Stage 2 | ST2 - H1 | 0.30526 | -758.0 | 0.3031 | -0.7 |
|  | ST2 - H2 | 0.30044 | -951.0 |  | 0.9 |
|  | ST2 - H3 | 0.30362 | -923.0 |  | -0.2 |
|  | ST2 - V1 | 0.35321 | -991.9 | 0.3557 | 0.7 |
|  | ST2 - V2 | 0.35799 | -1065.1 |  | -0.6 |
|  | ST2 - V3 | 0.35597 | 2429.5 |  | -0.1 |

Table 7 - Slope – Offset Linearity test

Test result:                                              Passed:   _X             Failed:         .   W Waived:    _

## Transfer functions and Comparison with measurements done in the staging building.

### At the end station

The parameters for the measurements in the X End are slightly different from those in the staging building. We chose to have weaker excitation but longer averages in an effort to reduce risk for the attached suspension.

At this point, only the tuned mass dampers on the springs and the vibration absorbers on Stage 1 doors are installed (No Viton under the keel masses)

Measurements data can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Measurements/Undamped:

- LLO_ISI_BSC4_Data_L2L_10mHz_100mHz_ST1_ST2_20131028-115737.mat

- LLO_ISI_BSC4_Data_L2L_100mHz_700mHz_ST1_ST2_20131026-104726.mat

- LLO_ISI_BSC4_Data_L2L_700mHz_10Hz_ST1_ST2_20131025-210845.mat

- LLO_ISI_BSC4_Data_L2L_10Hz_100Hz_ST1_ST2_20131025-174154.mat

- LLO_ISI_BSC4_Data_L2L_100Hz_500Hz_ST1_ST2_20131025-155703.mat

- LLO_ISI_BSC4_Data_L2L_500Hz_1000Hz_ST1_ST2_20131025-143236.mat

Data after processing can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Simulations/Undamped

- LLO_ISI_BSC4_TF_L2L_Raw_10mHz_1000Hz_2013_10_28.mat

The transfer functions can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Figures/Transfer_Functions/Measurements/Undamped/

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_CPS_2013_10_28.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_L4C_2013_10_28.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_T240_2013_10_28.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST2_ACT_to_ST2_CPS_2013_10_28.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST2_ACT_to_ST2_GS13_2013_10_28.fig

Note 1:  The transfer functions are measured from the Output filters bank excitation point to the input (IN1) of the input filters bank. The transfer functions presented below are raw transfer functions without any electronic compensation.

Note 2: The L4Cs are out of phase (should be -90 before 1Hz). A minus sign is added in the calibration filters that convert count to nm/s.

Note 3: On the ST1-ACT-H to ST1-CPS-H transfer functions, we can see the first resonances of the LVEA test stand at 21.1 Hz, 23.4Hz and 33.3Hz (matches within a few Hz our BSC 3 results).

Note 4: We had to retake the low frequency data (10mHz to 100mHz) because the watchdog for the T240 tripped over the weekend. As we were re setting it, we noticed that we had a high gain filter on those T240 explaining why it tripped so we disengaged it. That explains the difference of gain on Figure 5 between 10-100mHz and the rest of the Transfer Function. We also lowered the number of averages while we were retaking these measurements in order to be able to finish the report and get it approved which explains the difference in quality between 10-100mHz and the other frequencies.

Note 5: While we were retaking the measurements on the 10 to 100mHz frequencies, the watchdog tripped but we reset it as soon as we noticed it was tripped. This explains why on Figure 6, on Stage 2 H3 we can see a slightly lower response at low frequency (<10mHz).

Figure 3 - TF ST1 ACT to ST1 CPS

Figure 4 - TF ST1 ACT to ST1 L4C

Figure 5 - TF ST1 ACT to ST1 T240

Figure 6 - TF ST2 ACT to ST2 CPS

Figure 7 - TF ST2 ACT to ST2 GS13

### Comparisons with LHO ETMX

The script used to compare transfer function can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Scripts/Control_Scripts

- Comparison_TF_L2L_LLO_ISI_BSC4.m

The figure that shows the comparison between the transfer functions of L1 & H1 ETMX are located in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Figures/Transfer_Functions/Comparisons/L2L

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST1_ACT_H_to_ST1_CPS_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST1_ACT_V_to_ST1_CPS_V_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST1_ACT_H_to_ST1_L4C_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST1_ACT_V_to_ST1_L4C_V_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST2_ACT_H_to_ST2_CPS_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST2_ACT_V_to_ST2_CPS_V_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST2_ACT_H_to_ST2_GS13_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_Comparison_TF_L2L_ST2_ACT_V_to_ST2_GS13_V_20130405_vs_20121216.fig

Figure 8 - Transfer functions comparison - ST1 ACT to ST1 CPS

Figure 9 - Transfer functions comparison - ST1 ACT to ST1 L4C

Figure 10 - Transfer functions comparison - ST2 ACT to ST2 CPS

Figure 11 - Transfer functions comparison – ST2 ACT to ST2 GS13

Test result:                                              Passed:                 Failed:         .   W Waived:   X_

### Comparisons with measurements in the Staging Building

The script used to compare transfer function can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Scripts/Control_Scripts

- Comparison_TF_L2L_LLO_ISI_BSC4.m

The figure that shows the comparison of L1 BSC 4 Transfer Functions before and after the install of the Quad and TMS, are located in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Figures/Transfer_Functions/Comparisons/L2L

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST1_ACT_H_to_ST1_CPS_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST1_ACT_H_to_ST1_L4C_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST1_ACT_V_to_ST1_CPS_V_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST1_ACT_V_to_ST1_L4C_V_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST2_ACT_H_to_ST2_CPS_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST2_ACT_H_to_ST2_GS13_H_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST2_ACT_V_to_ST2_CPS_V_20130405_vs_20121216.fig

- L1_ISI_BSC4_TestStand_X-End_with_BSC3_Comparison_TF_L2L_ST2_ACT_V_to_ST2_GS13_V_20130405_vs_20121216.fig

Figure 12 - Transfer functions comparison - ST1 ACT to ST1 CPS

Figure 13 - Transfer functions comparison - ST1 ACT to ST1 L4C

Figure 14 - Transfer functions comparison - ST2 ACT to ST2 CPS

Figure 15 - Transfer functions comparison – ST2 ACT to ST2 GS13

Test result:                                              Passed:                 Failed:         .   W Waived:   X_

# Phase II-B – After Install

## Hardware changes

### CPS – E1100369

CPS have not been replaced since phase I testing in the staging building.

### GS13 – E1100740

GS13 have not been replaced since phase I testing in the staging building.

### L4C – E1100740

L4C have not been replaced since phase I testing in the staging building.

### T240 – E1100740

T240s have not been replaced since phase I testing in the staging building.

### Cables – E1100822

No cables have been changed since phase I testing in the staging building.

### Misc

No hardware changes since phase I testing in the staging building.

## Electronic Inventory

This table reports the electronic equipment used in the LVEA.

| Hardware | Ligo reference | S/N |
| --- | --- | --- |
| Interface Chassis Pod 1 | D1002432 | S1203884 |
| Interface Chassis Pod 2 | D1002432 | S1203885 |
| Interface Chassis Pod 3 | D1002432 | S1203886 |
| Anti-aliasing Chassis Pod 1 | D1002693 | S1203106 |
| Anti-aliasing Chassis Pod 2 | D1002693 | S1203107 |
| Anti-aliasing Chassis Pod 3 | D1002693 | S1203109 |
| Binary Input Chassis 1 | D1001726 | S1101306 |
| Binary Input Chassis 2 | D1001726 | S1101307 |
| Binary Output Chassis | D1001728 | S1101333 |
| T240 Interface Pod 1 | D1002694 | S1201405 |
| T240 Interface Pod 2 | D1002694 | S1201406 |
| T240 Interface Pod 3 | D1002694 | S1201407 |
| Anti-image Chassis | D070081 | S0900067 |
| Coil driver Pod 1 | D0902744 | S1103314 |
| Coil driver Pod 2 | D0902744 | S1103336 |
| Coil driver Pod 3 | D092744 | S1103360 |
| Expansion chassis |  | L1seiex |

Table 8 - Electronic inventory

Note: No changes.

## Models Modifications

No model modifications were done between the beginning and the end of Phase 2a testing.

## Mass distribution

At this point, all the final masses are installed on the BSC-ISI.

### Seismic

Stage 1

| Stage 1 | HighBay (lbs) | LVEA Test Stand (lbs) | LVEA Chamber (lbs) | LVEA Chamber (kg) |
| --- | --- | --- | --- | --- |
| Corner 1 | 49.22 | 49.22 | 46.72 | 21.19 |
| Corner 2 | 22.86 | 22.86 | 24.86 | 11.28 |
| Corner 3 | 32.22 | 32.22 | 31.72 | 14.39 |
| Total | 104.3 | 104.3 | 103.30 | 46.86 |

Note: The budget mass on Stage 1 changed a little bit between the Test Stand and in Chamber, it is probably due to some cablings that have been re-routed.

Stage 2

The seismic masses on BSC 4 are:

- On the side and on the Keel: 			933 lbs (=423.20 kg)

- On the Optical Table (6) D1003161:		285.72 lbs (=129.6 kg)

The total of masses on Stage 2 is:			1218.72 lbs (=552.8 kg).

### Suspension

The quad structure and the TMS Structure was weighed to be:

| SUS | Weight (lbs) | Weight (kg) |
| --- | --- | --- |
| Upper structure | 266 | 120.66 |
| Lower structure | 531 | 240.86 |
| Total | 797 | 361.5128 |

| TMS | Weight (lbs) | Weight (kg) |
| --- | --- | --- |
| Total | 456.14 | 206.9 |

### Misc

- 44 lbs = quad sleeve [Betsy’s alog 3621]

- 2 lbs = quad sleeve wedges [estimate]

- 5 lbs = cabling [estimate]

- 2 lbs cable brackets [estimate]

- 28 lbs = Vibration absorbers, quantity 4 [from E1000337-v2: 12.7 kg = 28 lbs]

- 3 lbs = Ring heater + brackets + cables [estimate]

Total Weight for Suspension: 906 lbs = 412 kg

Total Weight for TMS: 456.14 lbs = 206.9 kg

### Total

Nominal mass hanging on stage 0-1 blades (without stage 2): 912Kg – 2010lb

Nominal mass hanging on stage 1-2 blades: 2830Kg – 6239lb

Nominal payload on stage 1: 109Kg – 240lb

Nominal payload on stage 2: 1185Kg – 2612lb

|  |  |  | Staging Bldg | X End | X End (Chamber) |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Plan | 07/18/2012 | Detail | Overall | Detail | Overall | Difference |
| Stage 1 (kg) | 108.86 | 47.31 | 47.31 | 46.86 | -0.45 |
| Stage 2 (kg) | Masses | 1183.42 | 1155.53 | 547.68 | 1166.97 | 552.80 | 1172.09 | 5.12 |
|  | Suspension | N/A | N/A | 361.51 |  | 361.51 |  |  |
|  | Miscellaneous | N/A | N/A | 50.88 |  | 50.88 |  |  |
|  | TMS | N/A | N/A | 206.9 |  | 206.9 |  |  |
| Total (kg) | 1292.28 | 1200.79 | 1214.28 | 1218.95 | 4.67 |

The weight difference between the Test Stand and the In Chamber Mass Budget is under the 10 kg requirement. The weight for the quad and the TMS structure are estimated. Overall, the mass budget is consistent with what we had in the Staging Building.

Test result:                                              Passed:   X             Failed:         .   W Waived:   _

## Basic functionalities just after installing the BSC-ISI on the test stand

### Pressure sensors

All pressure sensors are working correctly.

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/
L1_ISI_ETMX_Pressure_Sensors_Check_Calibrated_2020_11_11_3 5:3:.mat

|  | Pressure (KPa) |
| --- | --- |
| Sensors | Corner 1 | Corner 2 | Corner 3 |
| ST1-L4C-P | 100.77 | 100.20 | 102.01 |
| ST1-L4C-D | -0.57 | 0.20 | -1.33 |
| ST1-GS13-P | 101.72 | 102.19 | 102.46 |
| ST1-GS13-D | 0.22 | -0.30 | -0.76 |
| ST1-T240-P | 100.54 | 100.66 | 100.74 |

Table 9 - Geophones Pressure sensors

Test result:                                              Passed:   X              Failed:         .   W Waived:   _

### Spectra

Spectra of the instrument can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Spectra/Undamped/

L1_ISI_ETMX_ASD_m_LOC_CPS_T240_L4C_GS13_2013_11_13_160436.mat

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ITMY/Data/Figures/Spectra/Undamped/
L1_ISI_ETMX_ASD_m_LOC_CPS_T240_L4C_GS13_2013_11_13_160436.fig

Figure 16 - Spectra inboard instruments - ISI Unlocked

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Actuators-cables resistance

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/ L1_ISI_ETMX_Actuators_Resistance_20131112T102441.mat

|  | Stage 1 | Stage 2 |
| --- | --- | --- |
|  | H1 | H2 | H3 | V1 | V2 | V3 | H1 | H2 | H3 | V1 | V2 | V3 |
| Script | 6.65 | 6.79 | 6.94 | 6.70 | 6.89 | 6.71 | 10.39 | 10.60 | 10.83 | 10.47 | 10.50 | 10.53 |

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Offsets CPS Unlocked vs locked

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/

- L1_ISI_ETMX_CPS_Read_Back_ISI_Locked_2013_11_13_154209.mat

- L1_ISI_ETMX_CPS_Read_Back_ISI_UnLocked_2013_11_13_154804.mat

|  | Table locked | Table unlocked | Difference locked - unlocked |
| --- | --- | --- | --- |
| Sensors | Offset (Mean) | Std deviation | Offset (Mean) | Std deviation | Offset (Mean) | mil |
| ST1 - H1 | -126.90 | 3.94 | -478.19 | 53.35 | 351.29 | 0.42 |
| ST1 - H2 | 29.25 | 4.27 | -1433.28 | 187.56 | 1462.53 | 1.74 |
| ST1 - H3 | -271.37 | 4.05 | -679.61 | 99.82 | 408.24 | 0.49 |
| ST1 - V1 | 129.49 | 5.10 | 189.55 | 110.58 | -60.06 | -0.07 |
| ST1 - V2 | -91.21 | 8.52 | -1291.51 | 69.55 | 1200.30 | 1.43 |
| ST1 - V3 | 280.67 | 6.24 | 253.75 | 106.65 | 26.92 | 0.03 |
| ST2 - H1 | 988.94 | 8.33 | -190.83 | 163.03 | 1179.78 | 0.35 |
| ST2 - H2 | -702.24 | 11.57 | -2007.25 | 230.40 | 1305.01 | 0.39 |
| ST2 - H3 | -1176.33 | 19.86 | -1753.94 | 68.32 | 577.60 | 0.17 |
| ST2 - V1 | -233.46 | 17.25 | -1249.38 | 242.67 | 1015.92 | 0.30 |
| ST2 - V2 | 126.95 | 15.82 | -510.76 | 161.26 | 637.70 | 0.19 |
| ST2 - V3 | -1154.53 | 19.85 | -318.12 | 216.05 | -836.41 | -0.25 |

Table 10 - Locked vs Unlocked Position

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Offset local drive

Note: Due to longer cables, offsets measured by CPS for a 7000 count drive are slightly lower than offsets measured in the staging building.

Results of this test can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/

- L1_ISI_ETMX_Offset_Local_Drive_20131112.mat

|  | Sensors |
| --- | --- |
|  |  | ST1 - H1 | ST1 - H2 | ST1 - H3 | ST1 - V1 | ST1 - V2 | ST1 - V3 |
| Actuators | ST1 - H1 | 3943.87 | 1599.22 | 1590.61 | -31.08 | -15.00 | 26.18 |
|  | ST1 - H2 | 1584.30 | 3969.92 | 1605.17 | 3.16 | -10.78 | 1.08 |
|  | ST1 - H3 | 1557.03 | 1576.15 | 3870.52 | -36.84 | 6.48 | 14.04 |
|  | ST1 - V1 | 8.38 | -128.47 | 70.39 | 2965.50 | -500.15 | -446.42 |
|  | ST1 - V2 | 67.33 | 11.20 | -135.44 | -451.42 | 2956.52 | -493.36 |
|  | ST1 - V3 | -116.69 | 84.93 | 48.19 | -453.71 | -471.60 | 3011.11 |

Table 11 - Static Tests – Local to Local - Stage 1

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - H1 | ST2 - H2 | ST2 - H3 | ST2 - V1 | ST2 - V2 | ST2 - V3 |
| Actuators | ST2 - H1 | 2202.20 | 331.22 | 337.90 | 9.01 | -8.52 | -18.83 |
|  | ST2 - H2 | 311.54 | 2211.21 | 329.80 | 8.38 | -28.38 | -16.66 |
|  | ST2 - H3 | 349.95 | 334.23 | 2215.81 | 27.00 | -13.33 | -7.23 |
|  | ST2 - V1 | 71.37 | 106.48 | -151.34 | 3131.97 | 316.20 | 45.22 |
|  | ST2 - V2 | -163.52 | 75.84 | 88.94 | 24.24 | 2594.10 | 328.84 |
|  | ST2 - V3 | 106.25 | -148.87 | 54.49 | 446.25 | 12.29 | 2592.81 |

Table 12 - Static Tests – Local to Local - Stage 2

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Offset Cartesian drive

The test was not performed because it only tests the matrices, which can be changed at any time.

Test result:                                              Passed:   _              Failed:         .   W Waived:   X_

### Range of motion

The range of motion of the table is measured by pushing on the table in a direction collinear to the CPS. The Static tests results can be found on the SVN at:

https://svn.ligo.caltech.edu/svn/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Static_Tests/

- L1_ISI_ETMX_Range_Of_Motion_20131114.mat

| Sensor readout (counts) | Negative drive | Positive drive | Amplitude count | mil |
| --- | --- | --- | --- | --- |
| ST1 - H1 | -16337.6 | 15347.3 | 31684.9 | 37.7 |
| ST1 - H2 | -15441.0 | 15558.5 | 30999.5 | 36.9 |
| ST1 - H3 | -15342.9 | 15952.1 | 31295.0 | 37.3 |
| ST1 - V1 | -12814.8 | 13297.3 | 26112.2 | 31.1 |
| ST1 - V2 | -14052.3 | 11664.9 | 25717.2 | 30.6 |
| ST1 - V3 | -12497.1 | 13356.9 | 25854.0 | 30.8 |
| ST2 - H1 | -9814.7 | 9292.3 | 19107.0 | 5.7 |
| ST2 - H2 | -11541.5 | 7443.2 | 18984.6 | 5.7 |
| ST2 - H3 | -11313.2 | 7682.6 | 18995.7 | 5.7 |
| ST2 - V1 | -11711.4 | 10043.1 | 21754.5 | 6.5 |
| ST2 - V2 | -11246.7 | 10991.4 | 22238.1 | 6.6 |
| ST2 - V3 | -11103.3 | 11155.4 | 22258.7 | 6.6 |

Table 13 - Range of motion - Actuator drive in the LVEA

Test result:                                              Passed:   X              Failed:         .   W Waived:   __

### Linearity test

The data of the linearity test can be found on the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Linearity_Test/

- L1_ISI_ETMX_Linearity_test_20131114.mat

The figures of the linearity test can be found on the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic\BSC-ISI\H2\BS\Data\Figures\Linearity_Test\

- L1_ISI_ETMX_Linearity_test_20131114.fig

Figure 17 - Linearity test –L1 - BS – In LVEA

|  |  | Slope | Offset | Average slope | Variation from average(%) |
| --- | --- | --- | --- | --- | --- |
| Stage 1 | ST1 - H1 | 0.56723 | -458.7 | 0.5635 | -0.66 |
|  | ST1 - H2 | 0.56788 | -1476.9 |  | -0.77 |
|  | ST1 - H3 | 0.55547 | -662.9 |  | 1.43 |
|  | ST1 - V1 | 0.43374 | 258.0 | 0.4306 | -0.73 |
|  | ST1 - V2 | 0.42761 | -1200.8 |  | 0.69 |
|  | ST1 - V3 | 0.43042 | 428.5 |  | 0.04 |
| Stage 2 | ST2 - H1 | 0.31916 | -248.1 | 0.3175 | -0.51 |
|  | ST2 - H2 | 0.31658 | -2049.8 |  | 0.30 |
|  | ST2 - H3 | 0.31683 | -1834.2 |  | 0.22 |
|  | ST2 - V1 | 0.36355 | -914.0 | 0.3687 | 1.38 |
|  | ST2 - V2 | 0.37058 | -174.6 |  | -0.52 |
|  | ST2 - V3 | 0.37183 | 46.6 |  | -0.86 |

Table 14 - Slope – Offset Linearity test

Test result:                                              Passed:   _X             Failed:         .   W Waived:    _

## Transfer functions and Comparison with measurements done on H1 BSC9 ETMX.

### In Chamber Quad Locked (Dome off)

The parameters for the measurements in the X End are slightly different from those in the staging building. We chose to have weaker excitation but longer averages in an effort to reduce risk for the attached suspension.

Note: the following transfer functions have been taken with the ISI in Chamber, with the dome off, the TMS Structure Unlocked but the Quad locked. The suspension team was busy welding ETMY at the time and we had some time to test ETMX so we decided to go ahead and do the transfer functions. This will eventually allow us to put the dome back on ETMX before Thanksgiving.

At this point, all the tuned mass dampers are on (on Stage 0-1 springs, the vibration absorbers on Stage 1 doors & Viton under the keel masses).

Measurements data can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Measurements/Undamped:

- LLO_ISI_BSC4_Data_L2L_10mHz_100mHz_ST1_ST2_20131116-091020.mat

- LLO_ISI_BSC4_Data_L2L_100mHz_700mHz_ST1_ST2_20131116-052642.mat

- LLO_ISI_BSC4_Data_L2L_700mHz_10Hz_ST1_ST2_20131115-210713.mat

- LLO_ISI_BSC4_Data_L2L_10Hz_100Hz_ST1_ST2_20131115-185936.mat

- LLO_ISI_BSC4_Data_L2L_100Hz_500Hz_ST1_ST2_20131115-173404.mat

- LLO_ISI_BSC4_Data_L2L_500Hz_1000Hz_ST1_ST2_20131115-162447.mat

Data after processing can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Simulations/Undamped

- LLO_ISI_BSC4_TF_L2L_Raw_10mHz_1000Hz_2013_11_16.mat

The transfer functions can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Figures/Transfer_Functions/Measurements/Undamped/

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_CPS_2013_11_16.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_L4C_2013_11_16.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_T240_2013_11_16.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST2_ACT_to_ST2_CPS_2013_11_16.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST2_ACT_to_ST2_GS13_2013_11_16.fig

Note 1:  The transfer functions are measured from the Output filters bank excitation point to the input (IN1) of the input filters bank. The transfer functions presented below are raw transfer functions without any electronic compensation.

Note 2: The L4Cs are out of phase (should be -90 before 1Hz). A minus sign is added in the calibration filters that convert count to nm/s.

Figure 18 - TF ST1 ACT to ST1 CPS

Figure 19 - TF ST1 ACT to ST1 L4C

Figure 20 - TF ST1 ACT to ST1 T240

Figure 21 - TF ST2 ACT to ST2 CPS

Figure 22 - TF ST2 ACT to ST2 GS13

Figure 23: H1 BSC9 ETMX TF ST2 ACT to ST2 GS13 (Quad & TMS Locked)

### In Chamber Quad Unlocked (Dome off)

Note: the following transfer functions have been taken with the ISI in Chamber, with the dome off, the TMS Structure Unlocked but the Quad unlocked.

At this point, all the tuned mass dampers are on (on Stage 0-1 springs, the vibration absorbers on Stage 1 doors & Viton under the keel masses).

Measurements data can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Measurements/Undamped:

- LLO_ISI_BSC4_Data_L2L_10mHz_100mHz_ST1_ST2_20131123-090401.mat

- LLO_ISI_BSC4_Data_L2L_100mHz_700mHz_ST1_ST2_20131123-034107.mat

- LLO_ISI_BSC4_Data_L2L_700mHz_10Hz_ST1_ST2_20131122-220223.mat

- LLO_ISI_BSC4_Data_L2L_10Hz_100Hz_ST1_ST2_20131122-185521.mat

- LLO_ISI_BSC4_Data_L2L_100Hz_500Hz_ST1_ST2_20131122-172030.mat

- LLO_ISI_BSC4_Data_L2L_500Hz_1000Hz_ST1_ST2_20131122-160402.mat

Data after processing can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Simulations/Undamped

- L1_ISI_ETMX_TF_L2L_Raw_2013_11_22.mat

The transfer functions can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Figures/Transfer_Functions/Measurements/Undamped/

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_CPS_2013_11_22.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_L4C_2013_11_22.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST1_ACT_to_ST1_T240_2013_11_22.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST2_ACT_to_ST2_CPS_2013_11_22.fig

- L1_ISI_ETMX_TF_L2L_Raw_from_ST2_ACT_to_ST2_GS13_2013_11_22.fig

Note 1: The transfer functions are measured from the Output filters bank excitation point to the input (IN1) of the input filters bank. The transfer functions presented below are raw transfer functions without any electronic compensation.

Note 2: The L4Cs are out of phase (should be -90 before 1Hz). A minus sign is added in the calibration filters that convert count to nm/s.

Figure 24 - TF ST1 ACT to ST1 CPS

Figure 25 - TF ST1 ACT to ST1 L4C

Figure 26 - TF ST1 ACT to ST1 T240

Figure 27 - TF ST2 ACT to ST2 CPS

Figure 28 - TF ST2 ACT to ST2 GS13

Note: We can notice on this last Figure that the resonances that we had on the TFs with the Quad Locked around 20Hz are gone.

### Comparisons with H1 BSC 9 ETMX

Note: the following transfer functions have been taken with the ISI in Chamber, with the dome off, the TMS Structure Unlocked but the Quad unlocked.

At this point, all the tuned mass dampers are on (on Stage 0-1 springs, the vibration absorbers on Stage 1 doors & Viton under the keel masses).

Measurements data can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Measurements/Undamped:

- LLO_ISI_BSC4_Data_L2L_10mHz_100mHz_ST1_ST2_20131123-090401.mat

- LLO_ISI_BSC4_Data_L2L_100mHz_700mHz_ST1_ST2_20131123-034107.mat

- LLO_ISI_BSC4_Data_L2L_700mHz_10Hz_ST1_ST2_20131122-220223.mat

- LLO_ISI_BSC4_Data_L2L_10Hz_100Hz_ST1_ST2_20131122-185521.mat

- LLO_ISI_BSC4_Data_L2L_100Hz_500Hz_ST1_ST2_20131122-172030.mat

- LLO_ISI_BSC4_Data_L2L_500Hz_1000Hz_ST1_ST2_20131122-160402.mat

Data after processing can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Transfer_Functions/Simulations/Undamped

- L1_ISI_ETMX_TF_L2L_Raw_2013_11_22.mat

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/H1/ ETMX/Data/Transfer_Functions/Simulations/Undamped

- H1_ISI_ETMX_TF_L2L_Raw_2013_09_21.mat

The transfer functions can be found in the SVN at:

https://svn.ligo.caltech.edu/svncommon/SeiSVN/seismic/BSC-ISI/L1/ETMX/Data/Figures/Transfer_Functions/Comparisons/L2L/

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST1_ACT_H_to_ST1_CPS_H_20131122_vs_20130921.fig

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST1_ACT_H_to_ST1_L4C_H_20131122_vs_20130921.fig

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST1_ACT_V_to_ST1_CPS_V_20131122_vs_20130921.fig

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST1_ACT_V_to_ST1_L4C_V_20131122_vs_20130921.fig

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST2_ACT_H_to_ST2_CPS_H_20131122_vs_20130921.fig

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST2_ACT_H_to_ST2_GS13_H_20131122_vs_20130921.fig

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST2_ACT_V_to_ST2_CPS_V_20131122_vs_20130921.fig

- L1_ISI_BSC4_InChamber_X-End_with_H1-BSC4-ETMX_Comparison_TF_L2L_ST2_ACT_V_to_ST2_GS13_V_20131122_vs_20130921.fig

Note 1: The transfer functions are measured from the Output filters bank excitation point to the input (IN1) of the input filters bank. The transfer functions presented below are raw transfer functions without any electronic compensation.

Note 2: The L4Cs are out of phase (should be -90 before 1Hz). A minus sign is added in the calibration filters that convert count to nm/s.

Figure 29 – TF ST1 H ACT to ST1 H CPS comparisons between L1 BSC4 & H1 BSC9

Figure 30 - TF ST1 V ACT to ST1 V CPS comparisons between L1 BSC4 & H1 BSC9

Figure 31 - TF ST1 H ACT to ST1 H L4C comparisons between L1 BSC4 & H1 BSC9

Figure 32 - TF ST1 V ACT to ST1 V L4C comparisons between L1 BSC4 & H1 BSC9

Figure 33 - TF ST2 H ACT to ST2 H CPS comparisons between L1 BSC4 & H1 BSC9

Figure 34: TF ST2 V ACT to ST2 V CPS comparisons between L1 BSC4 & H1 BSC9

Figure 35: TF ST2 H ACT to ST2 H GS13 comparisons between L1 BSC4 & H1 BSC9

Figure 36: TF ST2 V ACT to ST2 V GS13 comparisons between L1 BSC4 & H1 BSC9

Note: We can notice on this last Figure that the resonances that we had on the TFs with the Quad Locked around 20Hz are gone for the L1 BSC4 ETMX (Quad Unlocked) but are there for BSC9 (these TFs were taken at Handford with the Quad and TMS Locked)..

Test result:                                              Passed:   X              Failed:         .   W Waived:   _

## Conclusion Phase II-B – After Install

All results appear satisfying. The last set of Transfer Functions has been taken with the Quad UnLocked, and we have been able to confirm that the resonance at ~20Hz on Figure 22 - TF ST2 ACT to ST2 GS13 (see Figure 23: H1 BSC9 ETMX TF ST2 ACT to ST2 GS13 (Quad & TMS Locked) were due to the Locked Quad.

We can also notice that at higher frequencies (above 100Hz) we lose coherence. This might be due to the fact that we lowered the excitation for the transfer functions or due to the extra noise coming from the clean room right above the BSC.

If this Unit can be approved before Tuesday, November 26th 2013, we would be able to put the dome back on BSC 4 before Thanksgiving, and we would retake some more data.

Test result:                                              Passed:   X              Failed:         .   W Waived:   _