Cryogenic Silicon
Fabry-Perot Cavities:
Laser Stabilization with sub-Hertz Linewidth
Matthew Arran, University of Cambridge
Mentors: Rana Adhikari, David Yeaton-Massey

---
Summary
- Introduction
- Methodology
- Prior progress
- Analysis
- Results

---
Background
Introduction
- Laser frequency noise
- External reference cavities
- Noise sources:
  - Seismic noise
  - Shot noise
  - Thermal noise
    - Brownian
    - Thermoelastic
    - Thermorefractive

---
Introduction
Aim
- Work with silicon cavity at cryogenic temperatures
- Reduce Brownian noise:
  - By fluctuation-dissipation theorem[1]:
- Reduce seismic noise:
  - Require high quality factor Q at low temperature
  - Silicon has Q ~ 108 at around 100K
- Control thermoelastic noise:
  - CTE of Silicon has zeros at 18K & 123K[2]
S_x(f)=- {{4 k_b T} over {%omega}} Im[H(%omega)]
[1] K. Numata, A. Kemery, J. Camp ,
“Thermal-Noise Limit in the Frequency Stabilization of Lasers with Rigid Cavities”
Phys. Rev. Lett. 93 (2004)
[2] P. B. Karlmann, K. J. Klein, P. G. Halverson, R. D. Peters, M. B. Levine et al.
 “Linear Thermal Expansion Measurements of Single Crystal Silicon for Validation of Interferometer Based Cryogenic Dilatometer”
 AIP Conf. Proc. 824, 35 (2006)

---
Applications
Introduction
[3]
- Precision of atomic clocks
  - NIST-F1 uncertainty 3×10-16
  - Optical atomic clocks promise O(10-17)
- Gravitational wave observation
  - Thermal noise limiting after standard quantum limit[4]
[4] S. J. Waldman
“The Advanced LIGO Gravitational Wave Detector”
[3] NIST
“The Advanced LIGO Gravitational Wave Detector”

---
Optical system
Methodology
- Laser PDH locked to reference cavity
- Initially single cavity
  - Use spectrum analyzer for initial result
- Later work possible with two cavities
  - Measure beat frequency to analyse noise
[5]
[5] Image from D. Yeaton-Massey

---
Thermal system
Methodology
- Experimental chamber evacuated to 10-5 torr
- Cavity cooled to 123K
- Use of radiation shields
- Fine temperature control
  - High precision sensors
  - Resistive heaters
  - Temperature controller

---
Prior progress
Prior progress
- Optical system
  - Tabletop optics in place
- Cryostat
  - Designed
  - Manufactured
  - Pressure tested
- Experimental chamber
  - Parts manufactured
  - Attachments designed
  - Assembly tested
[Insert picture of optics]

---
Project aims
Prior progress
- Test cryostat cooldown
  - Prepare cryostat
- Analyse thermal system
  - Propagation of temperature perturbations
  - Effect of heaters
  - Communication with control system

---
System schematic
Analysis

---
Analytic approach
Analysis
θ0
- Construct differential equations
- Linearise about equilibrium, with
- Derive small-perturbation transfer functions
- Determine and substitute in parameter values
  - Two methods used
""{d}over{dt} (C_1 %theta_1)=%alpha_1 (%theta_0-%theta_1) +%beta_1(%theta_0^4-%theta_1^4)+%alpha_{2}(%theta_{2}-%theta_1) +%beta_{2}(%theta_{2}^4-%theta_1^4)+P_1 newline ""{d}over{dt} (C_2 %theta_2)=%alpha_2 (%theta_1-%theta_2) +%beta_2(%theta_1^4-%theta_2^4)+%alpha_{3}(%theta_{3}-%theta_2) +%beta_{3}(%theta_{3}^4-%theta_2^4)+P_2 newline ""{d}over{dt} (C_3 %theta_3)=%alpha_3 (%theta_2-%theta_3) +%beta_3(%theta_2^4-%theta_3^4)+P_3
θ3
θ2
θ1
%theta_i = {hat{%theta}}_i + %delta_i ", " P_i = {hat{P}}_i + %pi_i
""dot{%delta}_i={1}over{%GAMMA_i} left[ J_{i-1} %delta_{i-1} - (I_i + J_i) %delta_i + I_{i+1} %delta_{i+1} + %pi_i +O(%delta^2) right] newline "for" newline ""I_i = {hat{%alpha}}_i +a_i left( {hat{%theta}}_{i}-{hat{%theta}}_{i-1} right)+4 {hat{%beta}}_i {hat{%theta}}_{i}^3+b_i left( {hat{%theta}}_{i}^4-{hat{%theta}}_{i-1}^4 right) newline ""J_i = {hat{%alpha}}_{i+1} +a'_{i+1} left( {hat{%theta}}_{i}-{hat{%theta}}_{i+1} right) +4 {hat{%beta}}_{i+1} {hat{%theta}}_{i}^3+b'_{i+1} left( {hat{%theta}}_{i}^4-{hat{%theta}}_{i+1}^4 right) newline ""%GAMMA_i = {hat{C}}_i+c_i {hat{%theta}}_i

---
1. Fit D.E.s to cooldown
Analysis
- Cool cold plate to 77.4K
- Use known heat capacities
- Assume αi , βi constant
- Choose values to best fit D.E. solution to data

---
2. Fit T.F.s to step responses
Analysis
- Analytically-derived transfer functions have form:
- Step outer shield temperature
- Choose values A, B, C, μ1, μ2 to best fit step responses to data
{{tilde{%delta}}_2 (s)}over{{tilde{%delta}}_0 (s)}={a(s+b)}over{(s- %mu_1)(s- %mu_2)}={A}over{s - %mu_1} + {B}over{s- %mu_2} newline {{tilde{%delta}}_3 (s)}over{{tilde{%delta}}_0 (s)}={c}over{(s- %mu_1)(s- %mu_2)}={C}over{s - %mu_1} - {C}over{s- %mu_2}

---
Predictive ability
Results
Error in predictions by method 1.
Error in predictions by method 2.

---
Estimated transfer functions
Results
Zeros:	-1.4×10-5
-1.9×10-6
Poles:	-2.5×10-5
-7.0×10-6
-1.4×10-6
Zeros:	-2.5×10-6 -1.6×10-6
Poles:	-1.4×10-5 -1.2×10-5
-1.9×10-6 -1.4×10-6
Poles:	-1.4×10-5 -1.2×10-5
-1.9×10-6 -1.4×10-6
Method 1.
Method 2.
Magnitude of a zero
Magnitude of a pole

---
Poles and zeros
	Cold plate to Outer radiation shield	Outer shield to / Inner shield			Outer shield to / Dummy cavity
		1st method	2nd method	% diff	1st method	2nd method	% diff
Poles:	-2.5×10-5	-1.4×10-5	-1.2×10-5	14%	-1.4×10-5	-1.2×10-5	14%
	-7.0×10-6	-1.9×10-6	-1.4×10-6	26%	-1.9×10-6	-1.4×10-6	26%
	-1.4×10-6
Zeros:	-1.4×10-5	-2.5×10-6	-1.6×10-6	36%
	-1.9×10-6

---
Acknowledgements
David Yeaton-Massey
Rana Adhikari
LIGO
SFP, FASA offices
NSF