## Slide 1
S.Gras LVC meeting, Bethesda 2013
Progress on Acoustic Mode Damper design
Slawek Gras, 2013

## Slide 2
High power interferometer
Courtesy of G. Harry
S.Gras LVC meeting, Bethesda 2013

## Slide 3
Courtesy of R. Adhikari
Parametric Instability
Two processes present in the loop:
1. Test mass mechanical mode scatters fundamental mode (pump) into the higher order mode
2. After round trip scattered mode returns to the test mass and couples via radiation pressure into the mechanical mode
Parametric Instability as
a feedback loop:
Feed back loop gain (R) describes the dynamic of the system:
- Gain > 1 energy is pumped in to the test mass -> positive feed back - > Parametric Instability
- Gain < 0 energy is extracted from the test mass -> negative feed back-> TM cooling process
S.Gras LVC meeting, Bethesda 2013

## Slide 4
PI in Advanced LIGO
Initial results! Possibly overestimated statistics due to the small population.
Nevertheless, parametric instability cannot be ignored.
Unstable modes can occur in the frequency range 10- 90 kHz.
S.Gras LVC meeting, Bethesda 2013

## Slide 5
Parametric gain
Optical power in the arm cavities
~ 830 kW
Test mass
Q-factor
~ 1e+7
Overlapping parameter
(spatial matching)
< 0.01
Detuning parameter
(frequency matching)
~ 0
lower power ?
different
TM topology, coating?
doesn’t solve the problem
lower Q?
Yes, we think we can
but... can help
S.Gras LVC meeting, Bethesda 2013

## Slide 6
Let’s stick something lossy to the test masses
Danger: adding lossy element to the test mass can cause thermal noise elevetaion of the detectot.
Objectives:
1) Damping in the frequency range 10-90 kHz.
2) Minimum 10 -fold Q-factor reduction .
3) Negligible thermal noise degradation in 10 – 1000 Hz,
negligible = < 1% detector strain degradation.
What if we can control the loss value in the frequency domain?
-> minimizes effect on thermal noise in the detection band.
S.Gras LVC meeting, Bethesda 2013

## Slide 7
The loss factor η of the system can be visualized as a weighted of the loss factors of the parts with stored energies as weighted constants.
A highly dissipative element cannot contribute significantly to the total loss factor if it does not participate considerably in the total strain energy.
If a damper is in the form of a resonator, high E can be obtained despite of high loss factor of the damper -> better damping performance.
Damping mechanism
By adding a lossy element to the test mass , the effective loss factor of the test mass + lossy element can be increased.
On the other hand, thermal noise is proportional to W - the averaged energy dissipation. Therefore is required to keep η as low as possible at 10 – 1000 Hz.
S.Gras LVC meeting, Bethesda 2013

## Slide 8
Reaction mass
Electrical conductive epoxy
Epoxy
PZT/Piezo crystal
Base
TEST MASS
R
(+C,L)
Heat
RI2
Acoustic mode damper (AMD)
S.Gras LVC meeting, Bethesda 2013

## Slide 9
6 resonant AMD modes available to extract energy from test mass: 12 kHz – 65 kHz
2 x Flag-poles
2 x antiFlag-poles
Compression
Rotation
AMD resonances
Fx-mode
Fy-mode
aFx-mode
aFy-mode
C-mode
R-mode
S.Gras LVC meeting, Bethesda 2013

## Slide 10
σ
σ
σ
σ
σ
σ
compression
bending
shear
Active direction of piezo material
Mode 33
Mode 31
Mode 15
electrode
~
C
R,I,C
piezo
external
impedence
Careful design of electronic circuit allows controlling piezo element mechanical properties to the desired values.
S.Gras LVC meeting, Bethesda 2013

## Slide 11
low R
high R
low k
high k
Piezo element loss factor
S.Gras LVC meeting, Bethesda 2013
k – electromechanical coupling coefficient,
R - resistor

## Slide 12
Thermal noise
Finite element modeling is used for thermal noise analysis.
Epoxy
AMD
S.Gras LVC meeting, Bethesda 2013

## Slide 13
Epoxy area
Epoxy thickness = 4μm
Top mass area = 3x3 mm^2
Small epoxy area is more dissipative.
S.Gras LVC meeting, Bethesda 2013

## Slide 14
Epoxy thickness
1) Epoxy thickness scales linearly with energy dissipation.
2) Inertia effect has significant impact on energy dissipation.
S.Gras LVC meeting, Bethesda 2013

## Slide 15
2.0 mm
2.5 mm
3.0 mm
3.0 mm
2.0 mm
Thermal noise analysis
Piezo element dimenssions:
Test Mass: ITM,
Piezo manufacturer: Physics Instruments,
Q-factor: 2200,
k15 = 0.63,
R = 250 kΩ,
Polarization: perpendicular to the laser beam
Base diameter: 120 mm
Reaction mass: 1g
AMD location: 130 mm from the front face
No of AMDs: 1 AMD per TM
Specification:
S.Gras LVC meeting, Bethesda 2013

## Slide 16
Shear AMD
at
0.055%
If 2 AMDs per TM
expected degradation is ~1.0%
Max degradation in the range 10 – 1000 Hz.
S.Gras LVC meeting, Bethesda 2013

## Slide 17
1- epoxy TM-base (0.04)
2- epoxy base-piezo (0.04)
3- epoxy piezo-RM (0.04)
4- epoxy RM-Resistor (0.04)
5- Base (1e-7)
6- RM (1e-4)
7- Resistor (0.1)
8- Piezo (4.3e-3 at 300Hz)
AMD loss budget at 300 Hz
dominant
TN source
S.Gras LVC meeting, Bethesda 2013
-

## Slide 18
Compression AMD
Max degradation in the range 10 – 1000 Hz.
Orientation of polarization
S.Gras LVC meeting, Bethesda 2013

## Slide 19
Advanced LIGO noise curve + AMD noise
S.Gras LVC meeting, Bethesda 2013

## Slide 20
Conclusions
1) Analysied AMD configuration shows acceptable thermal noise level not exceeding 1% of the strain degradation
2) Dominant source of thermal noise is from epoxy layer between AMD base and piezo element,
3) Better choce of epoxy can further reduce influance of AMD on thermal noise,
4) High Q-factor shear piezo cermics is the best candidate for AMD,
5) AMD damping preformance analysis is required for final conclusion on AMD application for PI control.
S.Gras LVC meeting, Bethesda 2013