## Slide 1: Modeling the Calibrated Response of the Advanced Ligo Detectors
Luke Burks
2013 LIGO Caltech SURF
Mentors: Alan Weinstein, Jameson Rollins
Final Presentation

## Slide 2: Project Goals
Reproduce the GW strain with noise signal as accurately as possible from the error (eD) and control (sD) signals.
Our Project: Construct R-1, the Inverse Response Function

## Slide 3
Simulink Model provided by Rana Adhikari
Essentially we treated the existing model as a black box. We put in waves, and signals came out. Formulas for the strain were explained in the previous presentation. These formulas are adapted to Simulink in the block.

## Slide 4: Inside The inverse Response Block
As in the formulas, the error and control signals are combined with the inverse sensing and actuation functions as per:
h = e + As .
The sensing and actuation functions take the form of transfer functions and thus act as operators on the two signals.

## Slide 5: Two points of interest
The control signal is delayed due to the Digital Filters, so a compensating delay had to be input to properly set the phase of the two signals before they are combined.
The control signal also becomes inverted with respect to the error signal, so the strain formula becomes: h = e – (-As)

## Slide 6: Addition of two sine waves

## Slide 7: Comparison of strain reconstructions in the frequency domain

## Slide 8: Comparison of Input and output Strain in the time domain
The reconstruction differs from the input strain by less than 1 or 2 percent in the lower frequencies of the LIGO band.

## Slide 9: Varying delays according to frequency
Optimal delay times vary by frequency, resulting in large deviations at either high or low frequencies for a fixed delay. This could potentially be solved by using fixed delays and additional poles and zeros to stabilize the system.
Frequency | 50 | 100 | 200 | 300 | 400 | 500 | 600 | 800 | 1000
Delay time | 2.015e-8 | 2.015e-8 | 2e-8 | 2e-8 | 2e-8 | 2.5e-8 | 0 | 4e-8 | 5e-8
Percent Error | .017% | .15% | .6% | .34% | 1% | .15% | .2% | .3% | .6%

## Slide 10
Delays currently lose effectiveness at higher frequencies than 1000 Hz.

## Slide 11: Conclusion
We have developed a calibration block in Simulink to reconstruct h(t) from the simulated output of the aLIGO detectors.
The resulting response agrees fairly well with the frequency-domain inverse response function, but more work is needed to improve the agreement, especially at high frequencies.

## Slide 12
Further improvements on high frequency strain reconstruction are needed.
Use the output to track changes in the optical gain and potentially measure variation in the cavity pole.
The next phase of this project is to input calibration lines into the model, demodulate at those frequencies, and use the output to track changes in the optical gain, cavity pole, etc.
The next step would be to take this model and put it into the front end Real-time Code Generator (RCG) at the 40 meter laboratory at Caltech.
The model will then be implemented at LLO and LHO
Future Work

## Slide 13: Acknowledgements
Thanks to:
Professor Alan Weinstein
Jameson Rollins
2013 Caltech LIGO SURF
Rana Adhikari
Jeff Kissel