## Slide 1: LQR Linear Quadratic Regulator
A state space optimal control technique
Brett Shapiro

## Slide 2: Summary
LQR description
LQR derivation
  Double pendulum test mass control example
LQR observer formulation
  Quad pendulum damping observer example
Augmenting the plant for more complexity
  Example: Frequency domain LQR

## Slide 3: References
Reference 1: Modern Control Engineering, 4th Ed. Katsuhiko Ogata. 2002, Prentice Hall.
Reference 2: Linear Optimal Control Systems. Huibert Kwakernaak, Raphael Sivan. 1972, Wiley-Interscience. Online access at http://www.ieeecss.org/publications/classic-books
Reference 3: T1300301 – LQR in the frequency domain

## Slide 4: What is it?
An automated algorithm for finding optimal feedback for a linear system in state space form.
Initial state
Final state
State trajectory
1 DOF pendulum example
LQR determines the feedback law to minimize the size of the state vector in the least time with the least control effort.
Note, a state of [0,0] may be generalized to any arbitrary point.

## Slide 5: System Description
System block diagram
Assumptions:
We have knowledge of all states
2) The system is completely controllable. This means that given infinite actuator range we can [ref 1, pgs 779-780, 829-832]
  drive the system from one arbitrary state to another in finite time
  or, equivalently
  Set all closed loop poles to arbitrary values
Matrix dimensions for n states and m control inputs
LQR feedback gain

## Slide 6: Identifying the Goal - the Cost Function with competing interests
We want to make the size of really small.
But…also want to the size of to be really small,
to minimize noise, keep the actuators in range, avoid exciting higher order dynamics, etc.
And, we want this to be true for all time. So we make the total cost:
But, we might care about the size of some states and actuators more than others. So we generalize the cost with some weighting matrices: and
System block diagram

## Slide 7: Other LQR Cost Function Forms
Other forms you may see for the cost function
‘Infinite time horizon’. The simplest, and most common form. The one we use here. Ref [1].
‘Finite time horizon’. More general form. Used in the most rigorous LQR derivations. Results in a time variant feedback law, i.e. K = K(t). Ref [2].
You may also see this form, which is used by Matlab and also frequency domain versions of LQR.
In all cases, the weighting matrices are assumed to have these properties

## Slide 8: Minimizing the Cost Function: Two Derivation Approaches
Calculus of variations – the super gory rigorous method.
See reference 2, Chap 3. Includes special cases, including stochastic noise.
Linear algebra – more concise. Get’s the point across with some hand-waving. See Reference 1, pages 897-899.

## Slide 9: Minimizing the Cost Function
Plug in feedback relation
Factor out x
Then make the following substitution where . The time derivative allows us to brings the system dynamics into the cost function.
(1)
(2)
(3)
(4)

## Slide 10: Minimizing the Cost Function
Then substitute in the system dynamics
Canceling the x’s
Splitting into ‘square roots’ , , and rearranging
It can be shown that minimization of with respect to requires the minimization of
(5)
(6)
(7)
(8)
(9)

## Slide 11: Minimizing the Cost Function
But, since
This minimization is solved when
Which give us a relation between the feedback matrix and
Plugging this back into Eq. (7) (just after we substituted in the system dynamics)
(10)
(11)
(12)
(13)
Gives us the so called ‘Algebraic Riccati Equation’ (ARE), which we can solve for to get P for the complete solution. The ARE is generally solved for numerically. Only some very simple cases can be solved analytically.

## Slide 12: Example 1 – Double Pendulum Test Mass Control
Courtesy Gabriele Vajente
Problem:
design a controller to position the test mass using the two actuators
the test mass actuator has 1/10 the range of the top mass.
See MATLAB Example 1

## Slide 13: Example 1 – Double Pendulum Test Mass Control
We are interested in controlling the test mass position using the two actuators to compensate for suspension point motion.

## Slide 14: Example 1 – Double Pendulum Test Mass Control
For the states, just weight the test mass displacement
We try putting 10 times the weight on the test mass actuator since it has 10 times less range. Not necessarily an obvious relation to actuator range.
We will also include in R a scalar tuning factor λ.
State space equation
Cost function

## Slide 15: Example 1 – Double Pendulum Test Mass Control
% State space matrices
...
system = ss(A,B,C,D);
% LQR weighting matrices
Q = diag([0 1 0 0]);
lambda = 1e-13;
R = lambda*diag([1 10]);
% LQR feedback matrix
K = lqr(A,Bu,Q,R);
% closed loop state space matrices
A_closed_loop = A-B*K;
C_closed_loop = [C;K];
D_closed_loop = zeros(size(A,1),size(C_closed_loop,2))
system_closed_loop = ss(A_closed_loop,B,C_closed_loop,D_closed_loop)

## Slide 16: Example 1 – Double Pendulum Test Mass Control

## Slide 17: Example 1 – Double Pendulum Test Mass Control

## Slide 18: Example 1 – Double Pendulum Test Mass Control
λ
λ

## Slide 19: Example 1 – Double Pendulum Test Mass Control
How does the RMS test mass displacement change with λ?

## Slide 20: Example 1 – Double Pendulum Test Mass Control
λ
λ
If this dashed line is the requirement, we need λ < 1e-18

## Slide 21: Observer Design with LQR
Recall from yesterday, a system of the form
has an observer of the form
where is the estimated state.
The observer error is then,

## Slide 22: Control/Observer Separation Principal
For control feedback using the estimated state, the system state space is
Augmenting this plant with the state estimation error
We get the full closed loop system/compensator state space as
Because this matrix is block-triangular, the eigenvalues (poles) simple the combined set of the eigenvalues of (A-BK) and (A-LC). Thus, the poles of the control and estimator design are independent. So, one can design each piece individually, and be confident of where the closed loop poles will be.

## Slide 23: Observer – Controller Duality
Observer error
Control error
Note that the poles of are the same as its transpose
Thus, we can think of the observer feedback design as the ‘control’ design of the fictitious system
Control design
Observer design
Control-Observer Duals

## Slide 24: Observer LQR design
So, we can use LQR to chose how the estimation error evolves
% LQR observer feedback matrix
L_transpose = lqr(transpose(A),transpose(C),Qe,Re);
L = transpose(L_transpose);
Recall that
Where the dynamics are the same as e.
Qe weights the estimation error
Re weights the feedback of the noisy measured output
Matlab code

## Slide 25: Example 2 – quad damping
quad
-gain*derivative
Top mass
displacement
Test mass displacement
Top mass
input
Test mass displacement
Top mass velocity estimate
quad
-gain
Top mass displacement
Top mass
input
Estimator
LT = lqr(AT,CT,Qe,Re)
Reference case, pure velocity feedback with no estimation
Test case, velocity feedback using state estimation
See MATLAB
Example 2

## Slide 26: Example 2 – quad damping
22 kg
22 kg
40 kg
40 kg
We only consider the single degree of freedom along the laser beam axis for each stage (longitudinal motion). Thus, we have 8 states with 4 displacements and 4 velocities
We only care about estimating the top mass velocity. Thus,
We then scan for desirable values for the scalar
when we have this pure velocity feedback law

## Slide 27: Example 2 – quad damping
We can see what Re values give us convenient trade-offs between noise and damping

## Slide 28: Example 2 – quad damping
Scanning test mass noise and damping time performance for
10 Hz test mass seismic motion reference line
Test mass 10 Hz OSEM noise induced motion
Test mass ringdown time from seismic impulse

## Slide 29: Example 2 – quad damping

## Slide 30: Adding complexity – plant augmentation
One of LQR’s limitations is that the controller has no more complexity than the plant. Consequently, the controller design has finite degrees of freedom.
If we augment the plant with some fictitious states, we can achieve some more design degrees of freedom.

## Slide 31: Example – double pendulum plant augmentation
Problem: we want to lock a cavity with this double pendulum
there is very large seismic noise around the microseism
The test mass actuator has limited range, but is most effective at high frequencies
See [3]

## Slide 32: Example – double pendulum plant augmentation
Choose a low pass weighting function for the test mass displacement
Choose a high and low pass weighting function for the top and bottom forces respectively
frequency
magnitude
frequency
magnitude
frequency
magnitude

## Slide 33: Combine the state spaces of the plant and weighting filters
For a system state space
Note: the Matlab functions zp2ss or tf2ss will take you from the frequency domain to state space matrices. This makes it easy to design weights with poles and zeros while still augmenting the state space.
See the details in T1300301 [3]
Weight function for system state
Weight function for control inputs
Augmented A matrix

## Slide 34: Combine the state spaces of the plant and weighting filters
We then solve the LQR problem of the augmented state space
with the following cost function
where
Augmented B matrix
Augmented state vector

## Slide 35: T1300301 Example

## Slide 36: T1300301 Example
Cavity closed loop error chosen be the same for both standard and frequency weighted LQR

## Slide 37: T1300301 Example
The top mass actuation is also approximately the same

## Slide 38: T1300301 Example
The frequency weighted approach is successful at reducing the test mass drive without compromising the error signal

## Slide 39: Conclusions
LQR Benefits
  Optimal solution to control problem
  Automated (and very fast) method to design
  Always stable with a good model
  The controllers are typically robust
LQR Limitations
  Only has as much complexity as the plant
    This can be overcome by augmenting the plant
  Identifying the best weighting matrices is an art

## Slide 40: Backups

## Slide 41: Intro to Observers/Estimators
A state observer estimates the state of a system based on the system measurements.
  Useful if not all states are known, and/or they are measured with noisy sensors
  The measurements can involve states and/or inputs
  The system must be observable
  Observability (dual of controllable) means that the full state can be reconstructed from the outputs in finite time (recall, controllability is the ability to drive the system to any state in finite time)
Ref 1, Chapter 12-5.