## Slide 1: White Light Cavity Ideas and General Sensitivity Limits
Haixing Miao
Summarizing researches by several LSC groups
GWADW 2015, Alaska
University of Birmingham
G1500730

## Slide 2
Mizuno Limit
Shot-noise-limited sensitivity and signal recycling
A limit on peak sensitivity and bandwidth
Approaches for Surpassing Mizuno Limit
Peak-sensitivity-oriented: external/internal squeezing
Bandwidth-oriented: white-light-cavity ideas
An overview of key issues for future upgrades
Fundamental Quantum Limit
A limit beyond the Standard Quantum Limit and Mizuno Limit
Some implications for configuration studies in future
0
Outline
GWADW 2015, Alaska

## Slide 3
Mizuno Limit
Shot-noise-limited sensitivity and signal recycling
A limit on peak sensitivity and bandwidth
Approaches for Surpassing Mizuno Limit
Peak-sensitivity-oriented: external/internal squeezing
Bandwidth-oriented: white-light-cavity ideas
An overview of key issues for future upgrades
Fundamental Quantum Limit
A limit beyond the Standard Quantum Limit and Mizuno Limit
Some implications for configuration studies in future
Outline
GWADW 2015, Alaska
1

## Slide 4
Mizuno Limit
GWADW 2015, Alaska
2
Shot-noise-limited sensitivity and signal recycling:
Given different
SRM
reflectivity

## Slide 5
Mizuno Limit
GWADW 2015, Alaska
2
Shot-noise-limited sensitivity and signal recycling:
A limit on peak sensitivity and bandwidth product:
Given different
SRM
reflectivity
Order-of-magnitude:

## Slide 6
Mizuno Limit
GWADW 2015, Alaska
2
Shot-noise-limited sensitivity and signal recycling:
A limit on peak sensitivity and bandwidth product:
Given different
SRM
reflectivity
More precisely:
Order-of-magnitude:
Only depends
on power and
arm length.

## Slide 7
Mizuno Limit
Shot-noise-limited sensitivity and signal recycling
A limit on peak sensitivity and bandwidth
Approaches for Surpassing Mizuno Limit
Peak-sensitivity-oriented: external/internal squeezing
Bandwidth-oriented: white-light-cavity ideas
An overview of key issues for future upgrades
Fundamental Quantum Limit
A limit beyond the Standard Quantum Limit and Mizuno Limit
Some implications for configuration studies in future
Outline
GWADW 2015, Alaska
3

## Slide 8
Approaches for Surpassing Mizuno Limit
GWADW 2015, Alaska
4
Peak-sensitivity oriented: external squeezing
Challenge: optical loss of injection path
Max Mizuno
beating factor:
Faraday

## Slide 9
Approaches for Surpassing Mizuno Limit
GWADW 2015, Alaska
5
Peak-sensitivity oriented: internal squeezing
Challenge : optical loss of the nonlinear crystal
Max Mizuno
beating factor:
Reference: Mikhail Korobko & Roman Schnabel et al., in preparation

## Slide 10
Approaches for Surpassing Mizuno Limit
GWADW 2015, Alaska
6
Bandwidth-oriented: white-light-cavity ideas
Case I:
Advantage: Long coherence time and tunable
Challenges: (1) Wavelength compatibility (frequency conversion) (2) Additional quantum noise (currently under study)
Principle: Negative dispersion to compensate propagation phase
Reference: Zhou et al., arXiv:1410.6877; Yiqiu Ma et al. arXiv:1501.01349

## Slide 11
Approaches for Surpassing Mizuno Limit
GWADW 2015, Alaska
7
Bandwidth-oriented: white-light-cavity ideas
Mikhailov’s group
Shahriar’s group
Phase
Phase

## Slide 12
Approaches for Surpassing Mizuno Limit
GWADW 2015, Alaska
8
Bandwidth-oriented: white-light-cavity ideas
Mikhailov’s group
Shahriar’s group
Phase
Phase
Working
wavelengths
transitions in
alkali atom
(780, 795, 590,
852, 895 nm)

## Slide 13
Approaches for Surpassing Mizuno Limit
GWADW 2015, Alaska
9
Bandwidth-oriented: white-light-cavity ideas
An example using optomechanics:
Case II:
Challenge:
thermal noise from mechanical oscillator (optomechanics)

## Slide 14
Approaches for Surpassing Mizuno Limit
GWADW 2015, Alaska
9
Bandwidth-oriented: white-light-cavity ideas
An example using optomechanics:
Case II:
Challenge:
thermal noise from mechanical oscillator (optomechanics)
Reference: Miao et al., LIGO DCC: P1400255

## Slide 15
Overview of key challenges for upgrades
GWADW 2015, Alaska
10
Peak-sensitivity-oriented: external/internal squeezing
Bandwidth-oriented: white-light-cavity ideas
Advantage: fully understood and ready to implement
Challenge:
optical loss in injection path (external squeezing) or
in nonlinear crystal (internal squeezing).
Advantage: long coherence time and tunable
Challenges and readiness:
Atomic-based:
(1) Compatibility of wavelength (using frequency conversion).
(2) A complete quantum noise analysis (currently under way).
Readiness: around 5-10 years according to Shahriar and Mikhailov.
Optomechanics-based:
(1) Thermal noise in the optomechanical oscillator.
(2) Additional feedback control scheme.
Readiness: conditional on progress in optomechanics.

## Slide 16
Mizuno Limit
Shot-noise-limited sensitivity and signal recycling
A limit on peak sensitivity and bandwidth
Approaches for Surpassing Mizuno Limit
Peak-sensitivity-oriented: external/internal squeezing
Bandwidth-oriented: white-light-cavity ideas
An overview of key issues for future upgrades
Fundamental Quantum Limit
A limit beyond the Standard Quantum Limit and Mizuno Limit
Some implications for configuration studies in future
Outline
GWADW 2015, Alaska
11

## Slide 17
Fundamental Quantum limit
GWADW 2015, Alaska
12
Tuned signal recycling: Standard Quantum Limit
A tradeoff between the radiation pressure noise and shot noise
Cancelling radiation pressure noise: Mizuno Limit
Using squeezing or white-light cavities: Next Limit?
A tradeoff between the peak sensitivity and detector bandwidth

## Slide 18
Fundamental Quantum limit
GWADW 2015, Alaska
12
Tuned signal recycling: Standard Quantum Limit
A tradeoff between the radiation pressure noise and shot noise
Cancelling radiation pressure noise: Mizuno Limit
Using squeezing or white-light cavities: Next Limit?
A tradeoff between the peak sensitivity and detector bandwidth
(Initial quantum state of detector)
(Interaction)
(Final state to
be measured)

## Slide 19
Fundamental Quantum limit
GWADW 2015, Alaska
13
GW detectors as force measurement devices:

## Slide 20
Fundamental Quantum limit
GWADW 2015, Alaska
13
GW detectors as force measurement devices:
For any interferometer configuration:
(Displacement spectrum)

## Slide 21
Fundamental Quantum limit
GWADW 2015, Alaska
13
GW detectors as force measurement devices:
For any interferometer configuration:
(Displacement spectrum)
(Force)
Strong back action force (high energy) is necessary for high SNR.
Energetic Quantum Limit
References: [1] Braginsky et al., arXiv: 9907057 (gr-qc); [2]Tsang et al. PRL 106, 090401 (2011); [3] Yiqiu Ma et al. (in preparation)

## Slide 22
Fundamental Quantum limit
GWADW 2015, Alaska
14
Applied to tuned configurations (no optical spring):

## Slide 23
Fundamental Quantum limit
GWADW 2015, Alaska
14
With matching filtering:
Applied to tuned configurations (no optical spring):

## Slide 24
Fundamental Quantum limit
GWADW 2015, Alaska
14
With matching filtering:
Applied to tuned configurations (no optical spring):
Leading to a generalized Mizuno limit [ ]:
Upper sensitivity bound for all schemes with squeezing and WLC.
(variance of power fluctuation)

## Slide 25
Fundamental Quantum limit
GWADW 2015, Alaska
15
For any interferometer configuration:
Implications:
Approach 2: increasing mechanical response
Approach 1: increasing the back action
Higher power and more squeezing (external/internal)
Modifying test-mass dynamics using optical spring (optical bar)
Note: proper filtering schemes are needed to approach such SNR
(Speedmeter, frequency-dependent readout, intra-cavity filtering)

## Slide 26
Fundamental Quantum limit
GWADW 2015, Alaska
16
For any interferometer configuration:
Implications:
increasing the back action & mechanical response
Two interesting examples combining these two aspects:
Mingchuan Zhou & Shahriar et al. arXiv:1410.6877
Farid Khalili & Kentaro et al.

## Slide 27
Mizuno Limit
Shot-noise-limited sensitivity and signal recycling
A limit on peak sensitivity and bandwidth
Approaches for Surpassing Mizuno Limit
Peak-sensitivity-oriented: external/internal squeezing
Bandwidth-oriented: white-light-cavity ideas
An overview of key issues for future upgrades
Fundamental Quantum Limit
A limit beyond the Standard Quantum Limit and Mizuno Limit
Some implications for configuration studies in future
The End
GWADW 2015, Alaska
17