## Slide 1: Control system in Gravitational Wave Detectors
Koji Arai (新井宏二) – LIGO Laboratory / Caltech
GW mini-school: Beijing Normal University 2016/9/15~18
LIGO-G1601928-v1
引力波

## Slide 2: Introduction ~ Control?
Gravitational wave detection Laser displacement sensor Requires linear displacement detection
Control for measurement Laser interferometer = nonlinear device Feedback control => linearization

## Slide 3: Introduction ~ Control?
What is the feedback control?
  A scheme to monitor and modify output(s) of a system by changing the input(s) depending on the output(s)
Examples
  Shower temperature
  Car driving
  Tight rope walking
Imagine what happens
  If the response is too slow?
  If the response is too fast?
  Air conditioning
  Bike riding
  Inverted bar on a hand

## Slide 4: Introduction ~ Control?
Block diagram: Elements of a feedback loop
  Stabilized
  motion
  Disturbance
  Error
  signal
  Sensor
  Servo
  Filter
  Actuator
  Feedback
  signal
  m or m/Hz1/2
  m or m/Hz1/2
  V or V/Hz1/2
  V or V/Hz1/2
  V/m
  V/V
  m/V
  Transducer
  Filter

## Slide 5: Introduction ~ Control?
Sensor: Transducer for displacement-to-voltage conversion
If the sensor is completely linear (and has or no frequency dependence)
We don’t need feedback control!

## Slide 6: Introduction ~ Control?
In reality: Sensors, laser interferometers in particular, are nonlinear!
Enclose the operating point in the linear region => The system recovers linearity
Was the displacement modified by the feedback? => Precise knowledge of the control system
for signal reconstruction

## Slide 7: Introduction ~ Control?
Elements of a feedback loop
disturbance
error signal
sensor
servo filter
feedback
signal
actuator
Open loop transfer function
stabilized disturbance

## Slide 8: Introduction ~ Control?
When G is small:
disturbance
error signal
sensor
servo filter
feedback
signal
actuator
Open loop transfer function
stabilized disturbance

## Slide 9: Introduction ~ Control?
When G is big: e.g. G = 10, 100, or 1000
dx
dxs= dx/(1+G) = 0.09 dx, 0.01 dx, 0.001 dx
Verr= dx H /(1+G)
Vfb = G/(1+G) /A dx
= 0.91 dx/A, 0.99 dx/A, 0.999 dx/A
0.91 dx, 0.99 dx,
0.999 dx
Actuator range
Filter frequency response / loop stability
Residual error
vs
Sensor linear range

## Slide 10: Introduction ~ Control?
When the openloop gain G is >>1, the error signal gets suppressed
“Wow! our sensor signal became smaller!”
  Is our system more sensitive now? => No
  Then, can we still measure gravitational waves even if the error signal is almost zero? => Yes

## Slide 11: Introduction ~ Control?
Important difference between
  “Feedback control for stabilization” and “Feedback control for measurement”
  Feedback control changes the stabilized motion but reconstructed Disturbance is not modified by the loop* (*if everything is linear)
  Stabilized
  motion
  Disturbance
  Error
  signal
  Sensor
  Servo
  Filter
  Actuator
  Feedback
  signal

## Slide 12: Linear systems and their stability

## Slide 13: Linear systems and their stability
A deterministic and time-invariant system: H
The system H is LTI (linear & time-invariant) when
We can deal with such a system using Laplace transform (or almost equivalently Fourier Transform)
H
  System Input
  x(t)
  System Output
  y(t)

## Slide 14: Linear systems and their stability
Time domain vs Laplace (or Fourier) frequency domain
http://en.wikipedia.org/wiki/Linear_system
http://en.wikipedia.org/wiki/LTI_system_theory
Impulse response
transfer function

## Slide 15: Linear systems and their stability
It is easy to convert from an ordinary differential equation to a transfer function
e.g. Damped oscillator
  Laplace Transform
  Fourier Transform

## Slide 16: Linear systems and their stability
e.g. Damped oscillator
Bode diagram
  log-log
  log-lin

## Slide 17: Linear systems and their stability
e.g. RC filter
cut-off freq
w = 1/(R*C)

## Slide 18: Linear systems and their stability
In most cases, a system TF can be expressed as:
The roots of the numerator are called as “zeros” and the roots of the denominator are called as “poles”
Zeros (szi) and poles (spi) are real numbers (single zeros/poles) or pairs of complex conjugates (complex zeros/poles)

## Slide 19: Linear systems and their stability
Poles rule the stability of the system! H(s) can be rewritten as
Each term imposes exponential time impulse response
Therefore, if there is ANY pole with the response of the system diverges

## Slide 20: Linear systems and their stability
Poles rule the stability of the system!
http://nupet.daelt.ct.utfpr.edu.br/_ontomos/paginas/AMESim4.2.0/demo/Misc/la/SecondOrder/SecondOrder.htm
  Re(s)
  Im(s)
  Unstable
  response

## Slide 21: Linear systems and their stability
Requirement: All the roots for 1+G should be
in the left hand side of Laplace plane
  dx
  dxs = dx/(1+G)
  Open loop TF:
  G = H F A
  Closed loop TF:
  GCL = 1/(1+G)
  (!)
Now we eventually came back to this diagram

## Slide 22: Linear systems and their stability
Remarks
Requirement:
All the roots for 1+G should be in the left hand side of Laplace plane
  This does not mean all H, F, A needs to be stable. e.g. Unstable mechanical system A can be stabilized by a control loop. (cf. An inverted Rod)
  We usually play with F to tune the result. It is awkward to evaluate the stability of 1/(1+G) every time. There is a way to tell the stability only from G
  Nyquist’s stability criterion
  Open loop TF:
  G = H F A
  Closed loop TF:
  GCL = 1/(1+G)

## Slide 23: Linear systems and their stability
Nyquist stability criterion
  Plot openloop gain G in a complex plane (i.e. Nyquist diagram)
  If the locus of G(f) from f=0 to ∞, goes to 0 looking at the point (-1 + 0 i) at the left side => Stable
  If the locus sees the point (-1+o i) at the right side => Unstable
  Unity gain frequency fUGF : for |G(fUGF)| = 1
  Phase margin θ : θ = Arg(G(fUGF))
  Gain margin g: g = 1/|G(f0)| where Arg(G(f0)) = -π

## Slide 24: Linear systems and their stability
Phase Margin / Gain Margin in Bode diagram
  Most of the case, a bode diagram of G is enough to see the stability
  Nearly
  unstable
  Gain Margin
  4.3dB@420kHz
  -180deg
  Phase Margin
  48deg
  Unity Gain Freq
  (176kHz)
  A rough standard of a stable servo loop:
  Phase Margin > 40deg
  Gain Margin > 10dB

## Slide 25: Linear systems and their stability
Building blocks (“zpk” representation)
  Single pole
  Single zero
  A pair of complex poles
  A pair of complex zeros
  Gain

## Slide 26: Linear systems and their stability
Relationship between pole/zero locations and w0&Q
To be compared with

## Slide 27: Linear systems and their stability

## Slide 28: Linear systems and their stability
Summary
  Classical control theory
  Design locations of poles and zeros
  Stability: tuning of open loop transfer function is important

## Slide 29: Control system components in GW detectors

## Slide 30: Control systems
Elements of a feedback loop (again)
  Sensor
  Servo
  Filter
  Actuator

## Slide 31: Interferometer control system
Local control vs global control

## Slide 32: Local Sensors
L Carbone, Class. Quantum Grav. 29 (2012) 115005
Shadow sensor (relative displacement sensor)
  aLIGO: Birmingham Optical Sensor and Electro-Magnetic actuator (BOSEM)
Linear Variable Differential Transducer (relative disp. sensor)
Optical Lever (relative angular sensor)
  A B
  C D
  SUM = A+B+C+D
  X = A–B+C-D
  Y = A+B-C-D

## Slide 33: Local Sensors
Accelerometers (Inertial sensor)
  Piezo Accelerometer
  Servo Accelerometer

## Slide 34: Local Sensors
Servo Accelerometer (Inertial sensor)
  Above the resonant freq: Limited by the sensor noise
  Below the resonant freq: Steep rise of the noise as the mass does not move in relative to the ground => Low resonant freq is beneficial
  1 pm/sqrtHz
A. Bertolini et al, Nuclear Instruments and Methods in Physics Research A 564 (2006) 579–586
  Positive
  spring
  Negative
  spring

## Slide 35: Acutuators
Mechanical actuators
  Coil Magnet actuator
  Electro Static Driver (ESD)
  Piezo (PZT) actuator

## Slide 36: Acutuators
Optical actuators
  Acousto-Optic Modulator
  Electro-Optic Modulator
  Laser Frequency actuator
    Thermal actuator
    Fast piezo actuator
    External EOM
  LiNbO3 crystal

## Slide 37: Analog servo vs digital servo
Comparison of the control room in the analog and digital eras
  TAMA300 (2001)
  aLIGO (2014)