## Slide 1: Gravitational Waves Detected: The physics behind the detection, The physics we detected
Séminaire Poincaré
3 December 2016
David Shoemaker
For the LIGO and Virgo Scientific Collaborations
Credits
Measurement results: LIGO/Virgo Collaborations,
PRL 116, 061102 (2016); http://arxiv.org/abs/1606.04856
Simulations: SXS Collaboration; LIGO Laboratory
Localization: S. Fairhurst arXiv:1205.6611v1
Photographs: LIGO Laboratory; MIT; Caltech

## Slide 2
2
2
Virgo and LIGO
LIGO
Hanford,
Livingston
Virgo
KAGRA
2018
…and Observed with the initial detectors 2005-2011, and saw no signals
(and some interesting non-detections)
Virgo and LIGO built new observatories in the 90’s

## Slide 3: Advanced Detectors: a qualitative difference
While observing with initial detectors, parallel R&D led to better concepts
Design for 10x better sensitivity
Initial Reach
Advanced Reach
  We measure amplitude, so signal falls as 1/r
1000x more candidates

## Slide 4: What is our measurement technique?
Enhanced Michelson interferometers
  LIGO, Virgo, and GEO600 use variations
Passing GWs modulate the distance between the end test mass and the beam splitter
The interferometer acts as a transducer, turning GWs into photocurrent proportional to the strain amplitude
Arms are short compared to our GW wavelengths, so longer arms make bigger signals  multi-km installations
Arm length limited by taxpayer noise….
Magnitude of h at Earth:
  Largest signals h ~ 10-21
  (1 hair / Alpha Centauri)
  For L = 1 m, ΔL= 10-21 m
  For L = 4km, ΔL= 4x10-18 m

## Slide 5: Measuring ΔL= 4x10-18 m Readout
Shot noise – ability to resolve a fringe shift due to a GW (counting statistics)
Zum gegenwärtigen Stand des Strahlungsproblems, A. Einstein, 1909
Fringe Resolution at high frequencies improves as as (laser power)1/2

## Slide 6: Measuring ΔL= 4x10-18 m Readout
Shot noise – ability to resolve a fringe shift due to a GW (counting statistics)
Radiation Pressure noise – Point of diminishing returns when buffeting of test mass by photons increases low-frequency noise – use heavy test masses!
‘Standard Quantum Limit’

## Slide 7: Standard Quantum Limit
For a simple model of the instrument, one can choose the frequency of the best compromise between the two effects
Figures: Miao

## Slide 8: Detuned signal recycling (SR)
5
One interpretation: optical spring effect
[1] A. Buonanno and Y. Chen. Signal recycled laser-interferometer gravitational-wave detectors as optical springs, PRD 65, 042001 (2002). Slide: H. Miao
Signal recycling mirror (SRM)
In fact, in Advanced LIGO the signal recycling mirror couples phase and amplitude, and there is pondermotive squeezing of the light

## Slide 9: Measuring ΔL= 4x10-18 m Readout
Advanced LIGO is expected to operate in this pondermotive regime with its 200W laser, 40 kg test masses
…not yet, though (only see shot noise to date)

## Slide 10: Measuring ΔL= 4x10-18 m Internal motion
Thermal noise – kT of energy per mechanical mode
Über die von der molekularkinetischen Theorie der Wärmegeforderte Bewegung von in ruhenden Flüssigkeiten suspendierten Teilchen, A. Einstein, 1905
Simple Harmonic Oscillator:
Distributed in frequency according to real part of impedance

## Slide 11: Measuring ΔL= 4x10-18 m Internal motion
Thermal noise – kT of energy per mechanical mode
  This is the integral under the curve of motion…
Fluctuation-dissipation theorem gives motion as a function of frequency
Low mechanical loss materials gather this motion into a narrow peak at resonant frequencies
  Lower noise above and below the peak

## Slide 12: Measuring ΔL= 4x10-18 m Internal motion
In Advanced LIGO, the optical coating is the dominant loss
Fused silica components have losses of order 10-6 – 10-8
Sputtered optical coatings have losses of order 10-4
And the lossy coating is the interface to the laser beam
This is the dominant limit in the critical 10-200 Hz band
A focus of research!

## Slide 13: Measuring ΔL= 4x10-18 m Forces on test mass
Seismic noise – must prevent masking of GWs, enable practical control systems
(did Einstein work on seismic motion…?)
Motion from waves on coasts…and people moving around
GW band: 10 Hz and above – direct effect of masking
Control Band: below 10 Hz – forces needed to hold optics on resonance and aligned
aLIGO uses active servo-controlled platforms, multiple pendulums

## Slide 14: Measuring ΔL= 4x10-18 m Forces on test mass
Ultimate limit on the lowest frequency detectors on- or under-ground:
Newtownian background – wandering net gravity vector; a limit in the 10-20 Hz band
Images: J. Harms

## Slide 15: Measuring ΔL= 4x10-18 m Forces on test mass
Advanced LIGO (and Virgo) expect to be limited by this noise source –
  After all technical noise sources beaten down
  At low optical power (no radiation pressure noise)
  In the 10-30 Hz range
We would love to be limited only by this noise source!
Images: J. Harms

## Slide 16: Then there are the technical noise sources….

## Slide 17: Sensitivity for first Observing run
Initial LIGO
O1 aLIGO
Design aLIGO
Broadband,
Factor ~3 improvement
At ~40 Hz, Factor ~100 improvement

## Slide 18: 1.3 Billion years after the Black Holes merged.. (and multicellular life started on earth…) 100 years after Einstein predicted gravitational waves… 50 years after Rai Weiss invented the detectors... 20 years after the NSF, MIT, and Caltech Founded LIGO... 10 years after Advanced LIGO got the ok... 6 months after starting detector tuning... Two days after we started observing...
Notes: And then...after this 1.3-billion-year history,
Two days after we started observing...

## Slide 19: The first signal
On September 14, 2015 at 09:50:45 UTC the two detectors of the Laser Interferometer Gravitational-Wave Observatory observed a transient gravitational-wave signal
 1/10 second 

## Slide 20: We measure h(t) – think ‘strip chart recorder’
The output of the detector is the (signed) strain as a function of time
Earlier measurements of the pulsar period decay (Taylor/Hulse/Weisberg) measured energy loss from the binary system – a beautiful experiment
  radiation of gravitational waves confirmed to remarkable precision for 0pn
LIGO can actually measure the change in distance between our own test masses, due to a passing space-time ripple
  More ‘direct’ (in some sense)
  Much richer information!

## Slide 21
Time trace from Hanford, high- and low-pass filtered to make signal more evident. Signal in-band for ~0.2 secs. Amplitude ~1x10-21

## Slide 22
Time trace from Hanford and Livingston; Hanford inverted (observatory orientation is 180),
and shifted by 7.1 msec
(the observatories are separated by 10 msec time of flight). Source is in an annulus in the Southern hemisphere.

## Slide 23
Best fit waveform, assuming Einstein’s GR, using numerical relativity calculations, and putting in the same high/low pass filtering (so no long sinusoidal precursor). Same fit matches both observatories.

## Slide 24
Real time-series data,
minus best fit GR waveform:
Shows only noise in residual.
Absolutely astonishing.

## Slide 25
Spectrogram of high/low pass filtered data shows characteristic ‘chirp’ form.

## Slide 29: One event…was it real?

## Slide 30: Our second signal, 26 December 2015 – the SNR we thought we would be working with

## Slide 31: Our 2+1 signals to date

## Slide 32: Black holes seen to date

## Slide 33: Gravitational-wave astrophysics

## Slide 34: Spins of component BH
Would like to make inferences about origins based on spin
For all but one, no statistical deviation from zero spin (face-on, so not a good measure
For one component of GW151226, spin of 0.2 – so probably not the result of a merger ( primordial BH?)

## Slide 35
35
35
The advanced GW detector network
Advanced
LIGO
Hanford,
Livingston
2015
Advanced
Virgo
2016
LIGO-India
2022
KAGRA
2018

## Slide 36: What does the future hold?

## Slide 37: First Detection Sensitivity/configuration: 2 detectors, 1/3 goal sensitivity ~3 signals in 4 months of observation
37
Notes: P0900125-v8

## Slide 38
2017 Sensitivity/configuration:
3 detectors (add Virgo), ~1/2 goal sensitivity ~2-3 signals per month of observation
Notes: P0900125-v8

## Slide 39
2018-19 Sensitivity/configuration:
3 detectors, full goal sensitivity ~1 signal per day
Notes: P0900125-v8

## Slide 40
2022 Sensitivity/configuration:
5 detectors (add India and Japan)
far improved source localization
~60% in 10 sq deg
2022
Notes: P0900125-v8

## Slide 41: aLIGO operating at full power
ZUCKER

## Slide 42: aLIGO with the addition of frequency-dependent squeezing and lowered optical coating thermal noise
BNS reach: 510 Mpc
BBH reach: 3700 Mpc (z = 1.1)
QNM SNR ~35
(for an event like GW150914)
ZUCKER
A+

## Slide 43: A+
An incremental upgrade to aLIGO
leverages existing technology and infrastructure, with
  minimal new investment,
  moderate risk, and
  modest interruption in observing
Target: factor of 1.7* increase in range over aLIGO
About a factor of 5 greater event rate
Stepping stone to future 3G detector technologies
Link to future GW astrophysics and cosmology
Could be observing within < 6.5 years (mid-2022)
  (with FY’19 or earlier funding)
“Scientific breakeven” within 1/2 year of operation
Incremental cost: a small fraction of aLIGO
  Formulating proposal to NSF now
*BBH 20/20 M: 1.64x
*BNS 1.4/1.4 M: 1.85x
ZUCKER

## Slide 44: LIGO Voyager: exploit existing facilities
Refs: https://dcc.ligo.org/LIGO-T1400226, https://dcc.ligo.org/LIGO-T1200031, https://dcc.ligo.org/LIGO-T1200099
BNS Range = 740 Mpc
Si optics, > 100 kg
Si or AlGaAs coatings
‘mildly’ Cryogenic
λ~2 µm, 300 W
BNS R < 800 Mpc
BBH z < 5 (@10 M)
QNM SNR ~80
~$ ½ aLIGO
aLIGO
Voyager
ZUCKER

## Slide 45
US Concept: Make Advanced LIGO 10x longer,
10x more sensitive
Signal grows with length – not most noise sources
Thermal noise, radiation pressure, seismic, Newtonian unchanged
Coating thermal noise improves faster than linearly with length
40km surface Observatory ‘toy’ baseline
  can still find sites, earthmoving feasible; costs another limit…
Concept offers sensitivity without new measurement challenges; could start at room temperature, modest laser power, etc.
 | Adv. LIGO | 40 km LIGO
Arm length | 4 km | 40 km
Beam radius | 6.2 cm | 11.6 cm
Measured squeezing | none | 5 dB
Filter cavity length | none | 1 km
Suspension length | 0.6 m | 1 m
Signal recycling mirror trans. | 20% | 10%
Arm cavity circulating power | 775 kW | 
Arm cavity finesse | 446 | 
Total light storage time | 200 ms | 2 s
Sigg et. al

## Slide 46: Further Future Improvements: The 3rd generation
European Concept: Einstein Telescope
Significant design study undertaken for both Facility and Instruments
Underground construction proposed to reduce Newtonian Background
  (and be compatible with densely-populated Europe)
Triangle – LISA-like – with 10km arms
Multiple instruments in a ‘Xylophone’ configuration
  Allows technical challenges for low- and high-frequency to be separated
Designed to accommodate a range of detector topologies and mechanical realizations
  Including squeezing and cryogenics

## Slide 47: Einstein Telescope, Cosmic Explorer ‘Green field’ multi-generation Observatories ~G$/G€
John Miller, T1500491;
P1400147; ET-0106C-10
BNS
NSBH
BBH
POP3?
CE
Sigg et. al
SNR in QNM ~600

## Slide 48: 3rd Generation
When could this new wave of ground instruments come into play?
Appears 15 years from t=0 is a feasible baseline
  Initial LIGO: 1989 proposal, and at design sensitivity 2005
  Advanced LIGO: 1999 White Paper, GW150914 in 2015
Modulo funding, could envision…
  Einstein Telescope in the early 2030’s
  Cosmic Explorer in the mid-2030s
Should hope – and strive and plan – to have great instruments ready to ‘catch’ the end phase of binaries seen in LISA (ref. Sesana)
Crucial for all these endeavors: to grow the scientific community planning on exploiting these instruments far beyond the GR/GW enclave
  Costs are like TMT – needs a comparable audience

## Slide 49: ...and a detector in Space: LISA
AEI Max Planck
Once you are there, vacuum is inexpensive – make very long arms
  Very high signal-to-noise – precision tests of gravitation
Can observe much larger masses
  Galaxies with black holes of a million solar masses coalescing
Analogous to adding Radio Astronomy to Optical Astronomy

## Slide 50: LISA
Notion of a space-based interferometric detector dates from 1974
  Rai Weiss and Peter Bender
Basically a timing measurement between test masses in space
Take advantage of vacuum in space: make very long arms
  h = ΔL/L ; L can be ~109 m, making ΔL ~10-12 m (not LIGO’s 10-19)
  Also moves best sensitivity to milliHz region – explores much more massive objects
Triangular configuration
Sums and differences around the triangle
  Allows both polarizations of the gravitational waves to be measured
  Provides signals to remove laser frequency noise
Earth-trailing orbit provides scan of the sky, provides sky localization

## Slide 51: LISA Pathfinder test mission, now underway: interferometry between two LISA test masses

## Slide 52: LISA Sensitivity, with current Pathfinder Performance
A. Petiteau 2016

## Slide 53: LISA
ESA-led mission; NASA minority partner
ESA-NASA discussions on program elements
EU-US community (re-)forming joint collaboration
Phase A imminent; mission adoption possible in 2020
Launch date nominally 2034; may bring in to ~2030
…and then great science:
Blue: Simulated signal for inspiral of two 5x105 Black Holes inspiraling at z=5
Red: LISA Pathfinder interferometer performance

## Slide 54
Notes: So, that is my story of a cosmic cataclysmic rendez-vous: from 1.3 billion years ago with black holes coalescing in space when life was just forming on Earth, through the medium our favorite scientist Einstein – who looks in this photo as though he knew exactly how this was going to play out-- , and to a magic moment on September 14th 2015 when all the parts fell together to make this once-in-a-lifetime discovery possible.