## Slide 1
D. Shoemaker
for the LISA Consortium
GWADW
11 May 2018
Based on materials from Martin Hewitson and other LISA Colleagues
LIGO DCC G1800974

## Slide 2: Contents
Mission constraints and design
LISA Pathfinder Heritage
The path to launch
Science from Kelly, John

## Slide 3: GW Spectrum
http://rhcole.com/apps/GWplotter/
small
big
huge
10 M☉
106 M☉
>109 M☉

## Slide 4: The LISA Concept
Probe the change in proper time between pairs of free-falling test masses caused by GWs
Free-falling test masses are housed in drag-free spacecraft separated by a few million km
Proper time is inferred by the time of flight of photons exchanged between the satellites
We have multiple transponder links from which we can form Michelson-like signals

## Slide 5: A constellation of three satellites
60 million km to earth
(~3 minutes)

## Slide 6: The measurement concept
test-mass to test-mass measurement is synthesised from:
  test-mass to SC
  SC to SC
  SC to test-mass
2 W broadcast, 10-10 W received
Combine 6 links on ground
Time Delay Interferometry

## Slide 7: Process of setting requirements
Determine practical (cost, space readiness) limits for sensing system and spacecraft key parameters:
  Laser power
  Telescope size
  Photodetector and phasemeter performance
  Lifetime, mass, ESA cost cap
Use detailed models to calculate sensitivity in high-frequency regime
Use LISA Pathfinder results to define low-frequency sensitivity
Feed to Science Team; use detailed models to calculate what can be seen with that instrument
  Sanity check: Is this a great mission? Yes!
‘Flow down’ from Science to the mission specifications

## Slide 8: LISA limiting noise sources

## Slide 9: Science Objectives
Science case is composed from a number of Science Objectives (SO)
Each SO is broken up into Science Investigations (SI)
From each SI we derive Measurement Requirements (MR)

## Slide 10: Sensitivity Envelope

## Slide 11: LISA Pathfinder
Test most of the LISA performance budget
  all relevant local test mass disturbance forces
  local interferometry
And much of the critical technology
  drag-free control
  test mass charge control
  gravitational balancing
  SC environment control (thermal, magnetic)

## Slide 12: The LPF test
LPF tests this
Can we put test masses in quiet enough free-fall?

## Slide 13: LPF Concept
Free-falling test mass
Drag-free satellite
Suspended witness mass
Suspension
Drag-free

## Slide 14: LPF Realization
Motion
Sensors
Magnetic Coils
Heaters
UV Lamps
Motion
Actuators

## Slide 15: What do we know now?
Interferometer sensing noise
100x better than on ground
Brownian force noise due to residual gas around test masses
actuation noise, radiation pressure, etc + 50% something unknown

## Slide 16: Acceleration noise in LISA
LPF
extrapolation
estimates from LPF
Un-modelled noise to reflect uncertainty in LPF measurement

## Slide 17: Optical Metrology Noise in LISA
Bottom up approach of best estimates
Added:
  a little margin for un-modelled phase noise effects
  relaxation to low frequency to ease testing

## Slide 18: Full observatory break-down
LPF-like TM force noise limits at low frequency
OMS Noise limits above few mHz

## Slide 19: LISA Selected for ESA’s L3 mission slot
https://arxiv.org/abs/1702.00786
www.lisamission.org

## Slide 20: Payload concept (per S/C)
2 LPF Gravitational Reference Sensors
  TM, EH, FEE, caging mechanism, discharge system
2 Optical Benches
  imaging of received light, local and science IFOs, back-link/phase reference
2 Telescopes and mounting structures
Telescope breathing mechanism
Images courtesy of Airbus D&S GmbH,
Friedrichshafen

## Slide 21: Payload concept (per S/C)
Consortium Provided
Probably
NASA Provided

## Slide 22: S/C after Phase 0
Telescopes
Cold-gas
Tanks
Solar Array
Star
Cameras
Cold-gas
Thrusters
Transfer
Thruster

## Slide 23: Data Processing
Calibration
Preprocessing
TDI Processing
Astrophysics DA
Source Catalogues

## Slide 24: Raising alerts
Rich science available in joint EM+GW observations of events
MOC
SOC
DPC
Depacketising
Preprocessing
TDI
low-latency
analysis
Issue Alert
Generate Alert

## Slide 25: An alert example
Edge case:
Total mass 106 M☉
z = 2
most of the SNR from merger and ring down in the last hours

## Slide 26: Detection and localisation
need SNR > 10 for detection
need SNR > 50 for good source localisation
Sources more massive and/or closer give
earlier detection
earlier and/or more accurate localisation

## Slide 27: High SNR!
Blue: Simulated signal for inspiral of two 5x105 Black Holes inspiraling at z=5
Red: LISA Pathfinder interferometer performance

## Slide 28: The challenge of LISA data analysis
Multiple signals are always present in the LISA data
Need to disentangle all those signals to extract information about the sources
Mock LISA Data Challenges
  international community working on the problem

## Slide 29: Mission: Organization
ESA is the lead organization
  €1.05Bn Euro for launch, spacecraft
LISA Consortium is an umbrella for instrument, data, and science community
  European nation LISA Consortium members to deliver instrument to ESA
NASA a ~20% partner
  Probable contributions: Telescopes, Lasers, Charge Management, Colloidal Thrusters, Phasemeter parts
  Goddard, JPL; ‘Nasa LISA Study Team’

## Slide 30
Kelly Holley-Bockelmann, Chair
k.holley@vanderbilt.edu
NASA LISA Study Team

## Slide 31
NASA LISA
Study Team
Science Team
independent scientists
Jillian Bellovary | CUNY, Queensborough
Pete Bender | University of Colorado
Emanuele Berti | University of Mississippi
Warren Brown | Harvard-Smithsonian Center for Astrophysics
Robert Caldwell | Dartmouth College
Neil Cornish | Montana State University
Mike Eracleous | Penn State University
Craig Hogan | Fermilab
Kelly Holley-Bockelmann | Vanderbilt
Brittany Kamai | CalTech
Joey Key-Shapiro | University of Washington, Bothel
Shane Larson | Northwestern
Sean McWilliams | West Virginia Unversity
Guido Mueller | University of Florida
Priya Natarajan | Yale
David Shoemaker | MIT
Deirdre Shoemaker | Georgia Tech
Tuck Stebbins | University of Colorado

## Slide 32
NASA LISA
Study Team
Core Team
folks paid by NASA
John Baker | NASA Goddard Space Flight Center
Jordan Camp | NASA Goddard Space Flight Center
John Conklin | University of Florida
Curt Cutler | NASA Jet Propulsion Laboratory
Ryan DeRosa | NASA Goddard Space Flight Center
William Klipstein | NASA Jet Propulsion Laboratory
Tyson Littenberg | NASA Marshall Space Flight Center
Jeff Livas | NASA Goddard Space Flight Center
Kirk McKenzie | NASA Jet Propulsion Laboratory
Michele Vallisneri | NASA Jet Propulsion Laboratory
John Ziemer | NASA Jet Propulsion Laboratory

## Slide 33
NASA LISA
Study Team
Ex-Officio and Observers
people with power
Ira Thorpe | NASA Goddard Space Flight Center
Ann Hornschemeier | NASA Goddard Space Flight Center
Rita Sambruna | NASA Headquarters
Terri Brandt | NASA PCOS Program Office
Paul McNamara (ESA Observer) | European Space Technology Centre
Martin Hewitson (Euro-Community Observer) | Albert Einstein Institut/ Leibniz Universität Hannover

## Slide 34
Key NLST
Reasons
for Existing:
The US 2020 Decadal Survey
‘Advoreach’ (advocacy+ outreach)
Placing well in the 2020 US Astronomy Decadal Survey will protect LISA from budget cuts, cost overruns, the winds of change…
To get the most science out of LISA, we need to build capacity in the new field of gravitational wave astronomy. This requires a huge, formal, and persistent effort to train scientists at all levels, from senior faculty to undergraduates.

## Slide 35: Path to launch
2017
2018
2019
2020
Mission
Phase 0
Payload
Phase 0
Proposal
Selection
Competitive Industrial Phase A studies
2024
Mission
Definition
Review
Mission
Consolidation
Review
Mission
Selection
Review
2026
2028
2032
2030
2034
Mission
Adoption
Implementation Phase (B2/C/D)
Launch

## Slide 36: Post launch
2034
2036
2040
2046
Transfer & Commissioning
Operations
Mission Extension
Launch

## Slide 37: Summary
LISA L3 proposal has been selected!
Scramble now to
  Deliver required documentation for industrial contractors
  Develop hardware designs to required readiness
Refining Science, developing analysis techniques
Developing community
In US, focused effort to inform Decadal Survey
Launch scheduled for 2034;
…Possible as early as 2028