## Slide 1: Gravitational wave detection with laser interferometers
Koji Arai – LIGO Laboratory / Caltech
LIGO-G1801277-v1

## Slide 2: Gravity = Spacetime curvature
Albert Einstein: General Relativity
spacetime curvature
energy density
(e.g. mass)
Credit: Caltech/MIT/LIGO Lab

## Slide 3: Gravitational waves
Small perturbation of the spacetime
Ripples in specetime
flat spacetime
perturbation
wave equation
spacetime metric
Image credit: LIGO/T. Pyle
Notes: Gmunu definition / Einstein tensor = function of g / EM wave / ds^2 =

## Slide 4: Two modes of gravitational waves
Quadrupole strain pattern
flat spacetime
perturbation
wave equation
spacetime metric
Notes: Gmunu definition / Einstein tensor = function of g / EM wave / ds^2 =

## Slide 5: GW Detection
Two free-falling masses
Free fall? Free mass?
  => Equivance principle

## Slide 6: GW Detection
Optically measure strain between free masses
  GWs do not appear in the local motions
  The effect appears in the optical distance between the masses
GW
L->L (1+h/2)

## Slide 7: GW Detection
Measure strain between free masses
  GW does not appear in the local motion
  Changes optical distance between the masses
Longer the baseline, the bigger change
  (displacement dx) = (Strain h) x (baseline L)
GW
L->L (1+h/2)

## Slide 8: GW Detection
Q: What happens if
  The mirrors are not free-falling
  The distance is measured with a tape measure with infinite precision
GW
L

## Slide 9: GW detection with a laser interferometer
Michelson-type interferometer
  With suspended mirrors
Laser
Beamsplitter
End Mirror
End Mirror
Photodetector

## Slide 10: GW detection with a laser interferometer
Q: Why is the Michelson interferometer suitable for GW detection?
Laser
Beamsplitter
End Mirror
End Mirror
Photodetector

## Slide 11: GW detection with a laser interferometer
Michelson interferometer =
Optical phase meter sensitive to differential arm displacement
  The effect of GWs have the nature of differential strain
  Insensitive to the wavelength (=frequency) change of the laser
  Laser interferometry allows us to read the phase of the light
  Laser beams can be propagated long distance without power loss

## Slide 12: GW detection with a laser interferometer
Path length
change
GW strain
Arm length
h
L
Michelson-type interferometer
  With suspended mirrors
Differential path length change
  Intensity change at the output
The longer the arms, the better!
-> dx

## Slide 13: GW detection with a laser interferometer
Q: Why are the mirrors suspended?
Laser
Beamsplitter
End Mirror
End Mirror
Photodetector

## Slide 14: GW detection with a laser interferometer
Why are the mirrors suspended?
Above the resonant (pendulum) frequency,
a suspended mirror behaves as a free mass
At least in horizontal directions.
Notes: &m \ddot{x} = - \frac{m g}{l} x + F_{\rm ext}\\
({\rm F.T.}) \Rightarrow &- \omega^2 \tilde{x} = - \omega_0^2 \tilde{x} + \tilde{F}_{\rm ext}/m\\
&\,\,\,\,\,\,(\omega_0 = \sqrt{g/l})\\
\Rightarrow &\frac{\tilde{x}}{\tilde{F}_{\rm ext}} = \frac{1}{m (\omega_0^2-\omega^2)}

## Slide 15: GW detection with a laser interferometer
Plane light wave & propagation
  In a scaler model, the light field of a laser beam can be assumed as plane waves.

## Slide 16: Michelson interferometer
Electric field in a Michelson interferometer

## Slide 17: Michelson interferometer
Light intensity at the output port
  Difference of the electric fields from the arms
  Output intensity is sensitive
  to the differential phase

## Slide 18: Michelson interferometer
Frequency response of the Michelson to GWs
Jean-Yves Vinet,et al
Phys. Rev. D 38, 433 (1988)
Frequency response
of the Michelson interferometer
Ω: optical angular frequency, λOPT laser wavelength
ω: angular frequency of GW, λGW wavelength of GW

## Slide 19: Michelson interferometer
Frequency response of the Michelson to GWs
DC Response
longer -> larger
Cut off freq
longer -> lower
Notch freq
f = n c / (2 L)
  Michelson arm length optimized for 1kHz GW -> 75km, too long! => Fabry-Perot cavity

## Slide 20: Comparison: Michelson sensitivity and GW amplitudes
Michelson sensitivity (4km 1W ): h ≈ 1.3×10-20 /√Hz
Not enough at all!! What to do? (talk about it later)
From Phys. Rev. X 6, 041015

## Slide 21: Antenna pattern of a Michelson interferometer
Q: How does a Michelson interferometer reacts
to GWs coming from various directions?
Laser
Beamsplitter
End Mirror
End Mirror
Photodetector

## Slide 22: Antenna pattern of a Michelson interferometer
Q: How does a Michelson interferometer reacts
to GWs coming from various directions?
Laser
Beamsplitter
End Mirror
End Mirror
Photodetector

## Slide 23: Antenna pattern of a Michelson interferometer
Response of the interferometer to GWs
with + and x polarizations from various directions
+ x sqrt(“+”2 +“x”2)
Directivity is very mild
 Need multiple detectors for source identification

## Slide 24: Antenna pattern of a Michelson interferometer
Source identification with multiple detectors
Use difference of the signal arrival time to triangulate the source direction
Two detectors are not enough Need three or more.
dt
GW

## Slide 25: Advanced topics
Angular & frequency response of an arbitrary optical path
  Draw an arbitrary optical path. What is the angular and frequency response of such a path?
  Can we use numerical “optimization” for certain criteria? e.g. better sky coverage, directive beaming, for certain source frequency, etc…
GW
GW
GW

## Slide 26: Advanced topics
Angular and frequency response of LISA
  R. Schilling, Class. Quantum Grav. 14 (1997) 1513-1519
Arm length 2.5Gm

## Slide 27: Fabry-Perot Michelson Interferometer
Arms are too short
Use Fabry-Perot cavities in the arms to store the light longer
Basic form of the modern interferometer GW detector

## Slide 28: Fabry-Perot Michelson Interferometer
In the past, a delay line arm was considered (easier to understand)
A FP arm is similar but use a single optical path

## Slide 29: Fabry-Perot optical resonator
Storing light in an optical cavity
  Field equations
Very fast phase response

## Slide 30: Fabry-Perot optical resonator
Storing light in an optical cavity
Finesse
DC Response
amplification
Cutoff freq “Cavity pole”
  1. FP increases stored power in the arm
  2. FP increases accumulation time of the signal
  => Above the roll-off, increasing F does not improve the response

## Slide 31: Dual recycling
Even more mirrors for more light and signals
Advanced LIGO
Dual-Recycled Fabry-Perot Michelson Interferometer
Signal extraction mirror
Power recycling mirror
These recycling mirrors allows us to control the power increase in the arm and the signal storage time independently

## Slide 32: GW telescope?
A continuous signal stream from an interferometer
Find GW signals in the sea of noise
  Detector noises produce fake detections
Reduce noises!
  Obs. distance is inv-proportional to noise level
  x10 better => x10 farther => x1000 more galaxies

## Slide 33: GW telescope?
Noises & the signal
Noise = Background

## Slide 34: Actual GW detector
High
Power Laser
Mode
Cleaner
Recycling
Mirrors
4km FP arm cavities
Signal
Readout
Scheme
Data Storage
Data Analysis
Analog Electronics
Digital Control
Seismic Attenuation
Vacuum Envelope
Mirror Suspension
(Quad Pendulum)
Mirror & Coating
Fused Silica fiber

## Slide 35: Technologies of the GW detectors
3 elements of a laser GW detector
  Mechanics
  Optics
  Electronics

## Slide 36: Technologies of the GW detectors
3 elements of a GW detector
  Mechanics
  Optics
  Electronics

## Slide 37: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Design

## Slide 38: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Current sensitivity
h= 8x10-24 /rtHz

## Slide 39: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Noise budget
h= 2x10-23 /rtHz

## Slide 40: Summary
Interferometric GW detector
  GWs: Spacetime strain with quadrupole patterns
  Laser interferometry: Michelson type interferometer
  Multiple detectors: Triangulation for source identification
  Optical resonators: Fabry-Perot cavity and recycling
  Technologies: All for noise reduction