## Slide 1: Noises in gravitational wave detectors
Koji Arai – LIGO Laboratory / Caltech
LIGO-G1801355-v1

## Slide 2: Detector output signal
h(t) = differential arm strain signal
Single time series data

## Slide 3: Signal vs Noise
Waveform of GW signals
Continuous
Compact Binary Coalescence
Burst (unpredictable w.f.)
Stochastic

## Slide 4: Signal vs Noise
Waveform of GW signals
Continuous
Compact Binary Coalescence
Burst (unpredictable w.f.)
Stochastic
vs noises
Line noise
Transient noise
Scattered light noise
broadband noise

## Slide 5: Characterization of time-series data
Transient noise
Amplitude
Line noise
Scattered light noise
broadband noise
?
?
???
Notes: x_{\rm RMS} = \sqrt{\frac{1}{T} \int_{T_1}^{T_2} \left[x(t)\right]^2 dt}

## Slide 6: Characterization of time-series data
Transient noise
RMS (Root Mean Square)
Line noise
Scattered light noise
broadband noise
? ->RSS
Notes: x_{\rm RMS} = \sqrt{\frac{1}{T} \int_{T_1}^{T_2} \left[x(t)\right]^2 dt}

## Slide 7: Characterization of time-series data
Same RMS (~0.2), but they look different
Waveform 1
Waveform 2
Notes: x_{\rm RMS} = \sqrt{\frac{1}{T} \int_{T_1}^{T_2} \left[x(t)\right]^2 dt}

## Slide 8: Freq domain: Power Spectral Density
Double sided PSD (-Infinity < f < Infinity)
Single sided PSD (0 <= f < Infinity) [xunit2 / Hz]
Linearized PSD: [xunit/ sqrtHz]

## Slide 9: Characterization of time-series data
Same RMS (~0.2), but they look different
Waveform 1
Waveform 2
Frequency Domain
Notes: x_{\rm RMS} = \sqrt{\frac{1}{T} \int_{T_1}^{T_2} \left[x(t)\right]^2 dt}

## Slide 10: PSD <-> RMS
Parseval’s Theorem for signal RMS and PSD
Root Mean of x(t): average signal power density (per sec)
(cf. variance, std deviation)
PSD Sx(f):
power density per frequency (per sec)

## Slide 11: PSD <-> RMS
Same RMS (~0.2), but they look different
Waveform 1: RMS~0.18
Waveform 2: RMS~0.18
Frequency Domain
150Hz
150Hz
Sqrt(0.0142 * 150)
=~0.17
Notes: x_{\rm RMS} = \sqrt{\frac{1}{T} \int_{T_1}^{T_2} \left[x(t)\right]^2 dt}

## Slide 12: Time series, PSD, and RMS
Example
PSD [fm/sqrtHz] in log-log scale,
PSD [fm/sqrtHz] in log-lin scale
RMS [fm] ~ 50fm = 0.05pm
Time series [pm]
Notes: x_{\rm RMS}(f) = \sqrt{\int_f^{\infty} S_x(f) df}

## Slide 13: Time domain vs frequency domain
Time domain vs frequency domain
Noise
Reduction
Time domain: transient noises Frequency domain: stationary noises

## Slide 14: Time domain vs frequency domain
Transient noise *
Line noise *
Scattered
light noise *
Broadband
noise
Notes: x_{\rm RMS} = \sqrt{\frac{1}{T} \int_{T_1}^{T_2} \left[x(t)\right]^2 dt}

## Slide 15: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Current sensitivity
h= 8x10-24 /rtHz
RMS?

## Slide 16: Actual GW detector
High
Power Laser
Mode
Cleaner
Recycling
Mirrors
4km FP arm cavities
Signal
Readout
Scheme
Data Storage
Data Analysis
Analog Electronics
Digital Control
Seismic Attenuation
Vacuum Envelope
Mirror Suspension
(Quad Pendulum)
Mirror & Coating
Fused Silica fiber

## Slide 17: Components of the interferometer
3 elements of a GW detector
  Mechanics
  Optics
  Electronics

## Slide 18: Components of the interferometer
3 elements of a GW detector
  Mechanics
  Optics
  Electronics

## Slide 19: Noise categories
3 fundamentals of the GW detector
Mechanics -> Displacement noises
Optics -> Optical noises
Electronics -> Electrical noises
Optical
Optical
Displacement
Displacement
Electrical
Electrical
Electrical

## Slide 20: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Design

## Slide 21: Noise coupling to the GW channel
Noise coupling
model
Make the noise (dx) small
Make the coupling (𝜀) small
It is simple... isn’t it?
Noise
Coupling
GW channel
GW

## Slide 22: Noise coupling to the GW channel
Noise source measurement
Use a sensor that is specifically sensitive to dx.
This measurement itself is often difficult.
Noise
Sensor
Sensor
Output

## Slide 23: Noise coupling to the GW channel
Coupling measurement
dH = 𝜀 dN.
The system should be designed to allow the excitation.
Noise
Coupling
GW channel
Noise Excitation

## Slide 24: Noise coupling to the GW channel
Noise budget
Artificial Excitation
GW channel
Noise measurement

## Slide 25: Sensitivity and noise
Sensitivity (=noise level) of Advanced LIGO
Noise budget
h= 2x10-23 /rtHz

## Slide 26: Displacement noises

## Slide 27: Displacement noise
Mechanical displacement sensed by a laser interferometer
The longer the arm length, the smaller the strain noise
  Seismic noise
  Thermal noise
  Newtonian Gravity noise

## Slide 28: Displacement noise
Seismic noise
  Even when there is no noticeable earth quake…
http://link.aps.org/doi/10.1103/RevModPhys.86.121 (http://arxiv.org/abs/1305.5188)
Target disp. noise
10-20m/rtHz

## Slide 29: Displacement noise
Vibration isolation ~ utilize a harmonic oscillator
  A harmonic oscillator provides vibration isolation above its resonant frequency
w0=1Hz
|x/X|~1/1000@30Hz

## Slide 30: Displacement noise
aLIGO vibration isolation
Hydraulic active isolation / Invacuum Active Isolation Platforms / Multiple Pendulum

## Slide 31: Displacement noise
http://link.aps.org/doi/10.1103/RevModPhys.86.121 (http://arxiv.org/abs/1305.5188)

## Slide 32: Displacement noise
Thermal noise:
System in thermal equilibrium
  the system can dissipate its energy to the heat bath
  the system is thermally excited by thermal fluctuation
  The level of thermal excitation can be evaluated using the energy dissipation of the system (e.g. friction, resistance) “Fluctuation Dissipation Theorem”

## Slide 33: Displacement noise
Equipartition Theorem
In thermal equilibrium, each d.o.f. has the energy of
Johnson noise

## Slide 34: Displacement noise
Mechanical resonance
Quality factor Q
High Q => most of the kBT/2 energy contained in the resonant freq => Lower thermal motion at off-resonance
High Q
Low Q

## Slide 35: Displacement noise
Mirror substrate thermal noise
  Brownian motion Mechanical loss associated with the internal friction Thermally excited body modes Optical coating (higher mech. loss) will be limiting noise source in aLIGO
  Thermo elastic noise Elastic strain & thermal expansion coefficient => cause heat distribution & flow in the substrate Temperature fluctuation causes mirror displacement
  Thermo-refractive noise Temp. fluctuation causes fluctuation of refractive index
We don’t need to
know Z(w)!

## Slide 36: Displacement noise
Suspension thermal noise
  Brownian motion Mechanical loss of the suspension fiber Thermally excited pendulum modes
  Thermo elastic noise Elastic strain of the fiber & thermal expansion coefficient => cause heat distribution & flow in the fiber Temperature fluctuation causes mirror motion
We don’t need to
know Z(w)!
<- Monolithic suspension
for high pendulum Q

## Slide 37: Displacement noise
Newtonian Gravity noise
  Mass density fluctuations around the test masses => test mass motion via gravitational coupling
  Dominant source of Newtonian noise = Seismic surface wave
  Mitigation 1) Going to quiet place (underground) 2) Feedforward subtraction 3) Passive reduction by shaping local topography
NN
aLIGO
sensitivity
J Driggers, et al, PRD 86, 102001 (2012)
J Harms, et al, Class. Quantum Grav. 31 185011 (2014)

## Slide 38: Optical noises

## Slide 39: Optical noises
Noises that contaminate the readout signal
  Quantum noises (shot noise, radiation pressure noise)
  Laser technical noises (frequency/intensity noise)
  Modulation noises
  Scattered light noise
Optical
Optical

## Slide 40: Optical noises
Quantum noises: Shot noise
  Noise due to photon counting statistics
  N detected photon => standard deviation √N
  Increasing the incident power Pin, => The shot noise is increased by √Pin => The signal amplitude is increased by Pin
  In total, the signal-to-noise ratio is improved by

## Slide 41: Optical noises
Quantum noises ~ Radiation pressure noise
  Photon number fluctuation in the arm cavity => Fluctuation of the back action force
  Quantum noise of the input laser => Common noise for two arms => cancelled and does not appear in the signal
  Vacuum fluctuation injected from the dark port => Differentially power fluctuation => Cause the noise in the GW signal

## Slide 42: Optical noises
Quantum noises
  Standard Quantum Limit (SQL)
- Trade-off Between Shot Noise and Radiation-Pressure Noise
- Uncertainty of the test mass position due to observation

## Slide 43: Optical noises
Laser frequency noise
  Laser wavelength (λ = c / ν) = reference for the displacement measurement
  Optical phase 𝜙 = 2 pi ν L / c d𝜙 = 2 pi / c (L dν + ν dL) <= indistinguishable
  dL/L target 10-24 => dν = 10-24 x 300 THz (1064nmYAG laser) = 3 x 10-10 Hz/rtHz

## Slide 44: Optical noises
Laser frequency noise
  Target: dνeff = 3 x 10-10 Hz/rtHz
  Laser stability dν = 10~100 Hz/rtHz @100Hz
3-stage cascaded laser frequency stabilization
iLIGO
  Michelson’s differential sensitivity provides Frequency noise cancellation of 1/100~1/1000 “Common Mode Rejection”

## Slide 45: Optical noises
Laser intensity noise
  Relative Intensity Noise (RIN): dP/P
  Sensor output V = P x => dV = P dx + x dP <= indistinguishable
  Requirement: RIN = 10-9 1/√Hz xofs=10e-12 (DC Readout) => dx=1e-20 m/√Hz

## Slide 46: Optical noises
Laser intensity noise ~ intensity stabiliaztion
  Requirement: RIN = 10-9 1/√Hz
  2-stage cascaded intensity stabilization control
  Challenge: requires 300mA of photodetection
  Shot noise limited RIN
  In-vacuum 8-branch Photodiode array
P. Kwee et al, Optics Express 20 10617-10634 (2012)

## Slide 47: Optical noises
Scattered light noise
  Scattered light recouples to the interferometer beam with an arbitrary phase => causes amplitude and phase fluctuation
  Two effects: 1. Small motion regime: linear coupling of the phase fluctuation 2. Large motion regime: low freq large motion of the scattering object => upconversion via fringe wrapping
  Mitigation
    Reduce scattered light
    Vibration isolation of the scattering object

## Slide 48: Electrical noises

## Slide 49: General rules for electrical noises
Low noise amplification at the beginning
Give necessary gain as early as possible
Don’t attenuate (and amplify again)
Gain G1
Gain G2
input noise: v1
input noise: v2
output noise: v1 G1
output noise Vout:
Sqrt[(v1 G1 G2)2+(V2 G2) 2]
Input equivalent noise
Vout / (G1 G2)
= Sqrt[v12+(v2/G1) 2]
Signal
Lessons
  The input referred noise is determined by v1
  It won’t become better by the later stages
  If G1 is big enough, we can ignore the noise of later stages

## Slide 50: Digitization (Quantization) noise
Analog signals (~+/-10V) -> Digital signal
  Digitized to a discrete N bit integer number
  Quantization causes a white noise e.g. +/-10V 16bit => Δ = 0.3mV => Vn ~ 100 μV/sqrtHz cf. Input noise of a typical analog circuit 10nV/sqrtHz
http://www.analog.com/static/imported-files/tutorials/MT-229.pdf
quantization
quantization error

## Slide 51: Digitization (Quantization) noise
Whitening
  Amplify a signal in the freq band where the signal is weak
Dewhitening
  Amplify a signal in the freq band where the signal is weak

## Slide 52: Noise in photodetectors
Photodiodes
  PIN photodiodes (InGaAs for near IR, Si for visible)
    Good linearity
    Low noise
    High Quantum Efficiency (>90%)
InGaAs Quadrant PD
(𝜙3mm)
InGaAs PD (𝜙1mm)
P-layer
I-layer
N-layer
Anode
Cathode
“Photodiode Amplifiers”, J. Graeme (McGrawHill 1995)
Photocurrent

## Slide 53: Noise in photodetectors
input referred noise current
Noise in photodiodes
  Photodiode equivalent circuit
    Shunt Capacitance RD (~100MΩ) Usually not a problem
    Junction Capacitance CD (1pF~1nF)
    Series Resistance RS (1Ω~100Ω)
  The diode aperture size needs to be ~mm => Cd tends to be big.
  2mm InGaAs PD: Rs~10Ω, Cd~100pF => i_Rs = 20 pA/sqrtHz @100MHz
  (equivalent to the shot noise of 1mA light ~ 1.3mW@1064nm)

## Slide 54: Summary

## Slide 55: Summary
Summary
  There are such large number of noises
  They are quite omnidisciplinary
  Only one untamed noise can ruin GW detection
  GW detection will be achieved by
    Careful design / knowledge / experience
    Logical, but inspirational trouble shooting
  Noise “hunting”
    Systematic approach: noise budget