## Slide 1: LVK and LHO status
Georgia Mansell
On behalf of LIGO lab and the entire LVK (!)

## Slide 2: About me!
Post doc at LIGO Hanford and MIT since 2018
PhD at Australian National University in squeezed light
Undergrad at Adelaide University
My work focuses on gravitational-wave detector instrumentation
  Commissioning the aLIGO detectors in the run up to observing runs
This talk will have an instrumentation focus!!

## Slide 3: Overview
Recent collaboration publications
Frequency dependent squeezing!
Status of LIGO, Virgo, Kagra
New faces and farewells at LHO
LHO site status
Pre-O4 commissioning summary
LIGO-Virgo-Kagra collaboration overview
LIGO Hanford observatory overview

## Slide 4: Status of the LVK
ETMY cleaning at Kagra – klog 17271

## Slide 5: LVK update – recent publications
Publication list with handy science summaries https://pnp.ligo.org/ppcomm/Papers.html
Today! NSBH announcement
  Two NSBH events found in the O3 data
  GW200105
    Signal seen in 2 detectors, lower significance
    8.9 M☉ + 1.9 M☉
    900 million years ago!
  GW200115
    Triple detector discovery, high significance
    5.7 M☉ + 1.5 M☉
    1 billion years ago!

## Slide 6: Status of LVK
Covid restrictions are lifting, and we’re preparing for O4!
O4 scheduled start date >July 2022
  Aim: aLIGO 160 – 190 Mpc, AdV 90 – 120 Mpc, KAGRA 25 – 130 Mpc
Frequency-dependent squeezing install at LIGO and Virgo sites
  Major facility upgrade!
  New optics
  Elaborate additional controls
Many many other upgrades at each site!

## Slide 7: Frequency-dependent squeezing in a nutshell
In O3 both the LIGO and Virgo detectors injected squeezed light
This made quantum noise better at high frequency and worse at low frequency
Tse, 2019, Phys. Rev. Lett. 123, 231107
Side note!
1/3

## Slide 8: Frequency-dependent squeezing in a nutshell
For O4 we want broadband improvement – frequency dependent squeezing
To achieve this, we need to reflect our squeezed beam off a high-finesse optical cavity before sending it into the interferometer
Isogai, G1500727
Side note!
2/3

## Slide 9
Eddie Sanchez
G1900621
Both LIGO and Virgo are installing 300 m long filter cavities!
FC1
FC2
Y arm
Side note!
3/3
X arm

## Slide 10: Status of LIGO
O4 sensitivity improvement plans
  Improved stray light control (important <200Hz)
  New higher power laser amplifier
  Point absorber-free test masses
A+ project (O5, maybe ready by O4?)
  High efficiency Faraday isolators
  Adaptive mode matching at anti-symmetric port
  Frequency-dependent squeezing!
GariLynn Billingsley, G1800345
155um

## Slide 11: Status of Virgo
Slide from Giovanni Losurdo
G2100580

## Slide 12: Status of Virgo
Slide from Giovanni Losurdo
G2100580

## Slide 13
Slide from Yuta Michimura
G2100394

## Slide 14: Status of LHO
Photo: Chandra Romel

## Slide 15: Who’s who at LHO
New faces 
Cory Grimmer – Site safety
Nidhi Patel – Operator
Craig Cahillane – Postdoc
Mitchell Robinson - Instrument Assembly Technician
Aurora Shaffer (c/o TJ Shaffer)
Neal Grabeel (c/o Sheila Dwyer)
Cory Grimmer
Craig Cahillane
Nidhi Patel

## Slide 16: Who’s who at LHO
Some departures 
Hugh Radkins (seismic engineer) retired
Jeff Bartlett (operator) retired
Niko Lecoeuche (operator) now at UBC
Hugh Radkins
Niko Lecoeuche

## Slide 17: Site status – it’s complicated!

## Slide 18: Site status (1/3)
Photo: Keita Kawabe
LIGO exploration center (LExC) is under construction
  New outreach center at Hanford – see discussion led by Amber at 4pm!

## Slide 19: Site status - SQZ
Frequency-dependent squeezing
  Massive facilities undertaking!
  Two new HAMs to hold filter cavity optics
  New FC “end station” – the HAM shack
  New 300 m beam tube
Anticipate install of squeezer, FC optics in August– October 2021

## Slide 20: Site status - SQZ
New paths on the squeezer platform to route beam to and from filter cavity

## Slide 21: Site status - PSL
New amplifier = more power out of the pre-stabilized laser
Visual progress! Complete table re-alignment
June 9 – LHO alog 59172
June 21 – LHO alog 59251

## Slide 22: Site status – going in chamber
Many other vacuum incursions in the works!
Replaced ITMY in December 2020
Installing new stray-light baffles
Upgrading thermal compensation system
Moving the squeezer to a fresh HAM
New output Faraday isolator install
Travis Sadecki and Sebastien Biscans with new ITMY

## Slide 23: Pre-O4 mini commissioning period
In March/April 2021 we had a commissioning period*
Good news: new ITMY has no significant point absorbers!
  Reduced scatter coupling
  Angular controls became more stable and reasonable
  Powering up was easier! Reached 47W requested from PSL
Bad news: mystery noise (20-80Hz band) was consistent with O3
*vacuum envelope pumped down, commissioners “get” the interferometer, we work on acquiring lock and reaching low-noise configuration

## Slide 25: Conclusion
All hands on deck as we push towards O4 (and O5!)
Ambitious target sensitivity (160-190 Mpc for aLIGO), but we have some ideas of how to get there
Exciting upgrades to many systems
Expect more BBHs, BNSs, NSBHs in 2022!

## Slide 27: Frequency-dependent squeezing in a nutshell
Shot noise is caused by the quantum nature of light
Heisenberg uncertainty principal relates the amplitude and phase uncertainty
ΔA Δφ ≥ 1
Squeezing is reducing the noise in one quadrature at the expense of the other
Squeezing is produced in a nonlinear crystal

## Slide 28: Frequency-dependent squeezing in a nutshell
Shot noise is associated with phase quadrature
Radiation pressure noise is associated with amplitude quadrature
ΔA
Δφ

## Slide 29: Frequency-dependent squeezing in a nutshell
In O3 we injected phase squeezing only – improved shot noise but made radiation pressure noise worse!