## Slide 1
LIGO Converter Design Basic Features
Daniel Sigg and Marc Pirello
LIGO Hanford Observatory
Some Meeting Februray, 2023

## Slide 2: Converter R&D Direction
Long R&D Goal:
  Buy or make a PCIe board that could replace the common mode servos
  Something like FPGA & 4 Inputs & 2 Outputs & >1MHz sampling
  All signal processing for servo network in FPGA
  Integration with our RTCDS, strive for a similar feel as much as possible
  FPGA filters which try to emulate current filter module, use foton for design
  Data acquisition and excitation channels through PCIe
Short term need:
  Replace failing 18-bit DAC (GS 20-bit DAC very expensive, i.e., ~$7000 for 8 channels)
  Design a prototype 16-32 channel DAC board
32 channel ADC board?
Direct RF down-conversion using ADCs with GHz sampling?
  Requires phase locked RF demodulation/modulation signals

## Slide 3: Status
DAC Daughter Board
  Partially successful (issues with power supply)
  FPGA code to send sine waves to DAC completed and tested
  FPGA code for IIR filters completed and simulated
  FPGA code to interface PCIe completed (not tested, but mostly copied from Xilinx)
    Front-end driver required!
  Analog notch filter for testing completed
  Some promising noise measurements but incomplete
  DC accuracy not able to assess
DAC Prototype Design
  Mostly done
  Design checks ongoing

## Slide 4: Schedule
DAC Board
  Prototype by March (design is close to ready)
  Testing April- July
  First article by August/September (if needed)
ADC Board
  Design starting soon-ish
  Prototype by August
  Testing September-November
  First article by December (if needed)
Fast Servo Board: Start design next year
Costs:
  Each prototype/1st article run: $5000-$7000
  Required this year: $15k to $25k
  Estimated final costs: ~$1200-$1800 in quantity of 100 (16/32 channels)

## Slide 5: Front-End Chassis
Timing Board
Backplane
Adapter Board
Converter
AA/AI
Data
Sampling Clock
Watchdog
PCIe

## Slide 6: Clocking Improvements
Use timing distribution signal as input clock
  Local 226 Hz VCXO is locked to input clock
  Converter knows GPS time
Allows for time stamped data transfers
  Watchdog: Outputs can be stopped when no valid data is received
No special startup synchronization procedure required
  Converter is always synchronized to GPS (currently clock must start at 1sec boundary)
Clock rate is set by the converter and not by the timing board
  Only 2n Hz conversion rates available, so

## Slide 7: Signal Processing Support
Board will use a modern FPGA (e.g., Artix-7/Artix Ultrascale)
  Support for PCIe 2.1/3.0
  Support for 4x possible (current Adnaco boards only supports V2.1 at 1x)
FPGA is large enough to support high precision IIR Filters
  Up and down sampling filters in FPGA
  No requirement to increase IOP rate beyond required rate for servos
  Could implement down-conversion as well
Converter runs at optimal rate
  Usually faster than required sampling rate
Include support for sampling rate > transfer rate
  Multiple samples per channel per DMA transfer
DMA is double buffered to reduce IOP timing constraints

## Slide 8: Converter Technology
First prototype is 32 channel DAC
  Price estimate ~$1500/card in quantities of 100 (~$2000/card in qty 10)
  Channel bonding possible to improve SNR, i.e., 16 channel or 8 channel
Uses SD-Technology
  Tend to have better linearity than other technologies
  Preferred by audiophiles (10Hz to >20kHz)
Delays
  Old SD-converters implemented FIR filters for up-sampling which introduced long delays
  New SD-converters allow to implement filters externally → use IIR filters on FPGA
  New SD-converters are much faster, so sample delays matter much less
Improvement output stage of SD-DACs
  Much lower resistance in current drive reduces flicker noise
  Full differential design improves DC accuracy, but is it good enough?