## Slide 1: Present and Future Terrestrial GW Detectors
David Shoemaker
MIT Kavli Institute – LIGO Laboratory
Slides from many CE and LIGO Collaborators!
4 October 2023
G2301273
Vanderbilt Lunar MMA

## Slide 2: The Gravitational Wave Spectrum
10-9 Hz
10-4 Hz
100 Hz
103 Hz
Relic radiation
Cosmic Strings
Supermassive BH Binaries
BH and NS Binaries
Extreme Mass Ratio
Inspirals
Supernovae
Spinning NS
10-16 Hz
Pulsar timing
Space detectors
Terrestrial interferometers

## Slide 3: The Gravitational Wave Spectrum
10-9 Hz
10-4 Hz
100 Hz
103 Hz
Relic radiation
Cosmic Strings
Supermassive BH Binaries
BH and NS Binaries
Extreme Mass Ratio
Inspirals
Supernovae
Spinning NS
10-16 Hz
Pulsar timing
Space detectors
Terrestrial interferometers

## Slide 4: The Gravitational Wave Spectrum
10-9 Hz
10-4 Hz
100 Hz
103 Hz
Relic radiation
Cosmic Strings
Supermassive BH Binaries
BH and NS Binaries
Extreme Mass Ratio
Inspirals
Supernovae
Spinning NS
10-16 Hz
Pulsar timing
Space detectors
Terrestrial interferometers

## Slide 5: Why are terrestrial detectors limited to f > ~1 Hz?
Passing GW shortens the light path for one arm, lengthens for the other – and then vice-versa ΔL = hGW · L
Interference at the Beam splitter turns this into a light intensity variation, and a photodiode into an electrical signal
Resolution of the readout limited by quantum effects
Physical motion of the mirrors due to local forces masks the minuscule changes in light path due to GWs

## Slide 6: Newtonian background due to seismic environment
In principle, can eliminate all direct mechanical coupling
Can not shield against the wandering net gravity vector
Images: J. Harms
Images: J. Harms

## Slide 7: Newtonian background creates a wall at a few Hz
Newtonian Background falls as ~ 1/f 5
Can reduce somewhat by moving underground
  ET vs CE – more later on these two
Can reduce somewhat with arrays of seismometers and subtraction of effect
Forbiddingly large for ~3Hz and lower
Ultimate limit on the lowest frequency detectors on- or under-ground
And thus the largest BH masses detectable
Harms et al. 2022
Evans et al. 2023

## Slide 8: Practical limitations for Terrestrial Detectors
Arm length L – currently in short-antenna limit; path-length shift ΔL from a given strain grows with interferometer arm length. Maximize L !
  ΔL = hGW · L
  LIGO 4km, Virgo and KAGRA 3km
Optical resolution – limited by photon Poisson counting statistics; maximize laser power P
…but too much power, and the radiation pressure causes mirror motion which masks the GW
Optimal power – naïve quantum limit
  Working with ~50-100 W

## Slide 9: Practical limitations for Terrestrial Detectors
Arm length L – currently in short-antenna limit; path-length shift ΔL from a given strain grows with interferometer arm length. Maximize L !
  ΔL = hGW · L
  LIGO 4km, Virgo and KAGRA 3km
Optical resolution – limited by photon Poisson counting statistics; maximize laser power P
…but too much power, and the radiation pressure causes mirror motion which masks the GW
Optimal power – naïve quantum limit
  Working with ~50-100 W
Tomorrow

## Slide 10: Good enough to start the new observational discipline of Gravitational Wave Astronomy
What have we seen so far?

## Slide 11: The ground-based gravitational-wave world-wide network in 2023
A third LIGO detector in India funded
(Operational late 2020s)

## Slide 12
Gravitational Wave Physics & Astrophysics

## Slide 13
Observations
Image : Carl Knox (OzGrav, Swinburne University of Technology)
Slide: S. Fairhurst

## Slide 14
Image : Carl Knox (OzGrav, Swinburne University of Technology)
Slide: S. Fairhurst
GW150914: First Detection
Abbott et al, “Observation of Gravitational Waves from a Binary Black Hole Merger”, 2016

## Slide 15
Image : Carl Knox (OzGrav, Swinburne University of Technology)
GW170817: Neutron Stars and Multi-messenger Observation
From Abbott et al, “Multi-Messenger Observations of a Binary Neutron Star Merger ”, 2017
Slide: S. Fairhurst

## Slide 16
Image : Carl Knox (OzGrav, Swinburne University of Technology)
GW170817: Neutron Stars and Multi-messenger Observation
From Abbott et al, “Multi-Messenger Observations of a Binary Neutron Star Merger ”, 2017
Slide: S. Fairhurst

## Slide 17
GW190412: Unequal mass binary
One of the black holes ~4 times heavier than the other
Slide: S. Fairhurst

## Slide 18
GW200105 and GW200115: Observation of Neutron Star Black Hole Mergers
First unambiguous observation of NS-BH system
Slide: S. Fairhurst

## Slide 19
Observations
Image : Carl Knox (OzGrav, Swinburne University of Technology)
Slide: S. Fairhurst
GW190521: A Black Hole in the
Pair Instability Mass Gap
Evidence for a hierarchical merger?
Or perhaps dynamical capture?
156 Msun
66 Msun
95 Msun

## Slide 20
O1: Gravitational waves from astrophysical sources can be measured.
O1: Binary black hole (BBH) systems exist.
O2: Binary neutron stars (BNS) are progenitors of short gamma ray bursts.
O2: BNS mergers produce kilonovae, which produce heavy elements.
O2: The speed of gravitational waves equals the speed of light.
O2: The Hubble-Lemaître constant can be measured using EM-bright GW ‘sirens’.
O2 – O3: The Hubble-Lemaître constant can be measured using dark GW ‘sirens’.
O3: Black holes with masses in the (pulsational) pair instability gap exist.
O3: Black hole – neutron star systems exist.
O3: Compact objects exist in the 2 – 3 M⦿ mass range.
O1-O3: Astrophysical black holes are Kerr black holes
O1 – O3: General relativity is valid in the high curvature, high field regime.
O1 – O3: Intermediate black holes and stellar mass black holes with mass > 20 M⦿ exist.
LIGO-Virgo Fundamental Results 2015-2021: What Ground-
Based Gravitational Wave Detections Have Taught Us
GW150914
GW170817/
GRB170817A
SSS17A

## Slide 21: Sensitivity improvements boost signal rate
rreach ∝ 1/hsensitivity
Volume of space accessible – and sources –grows as ~(sensitivity)3
There are gaps for the upgrades… but so far we make up for it

## Slide 22: Sensitivity improvements boost signal rate
rreach ∝ 1/hsensitivity
Volume of space accessible – and sources –grows as ~(sensitivity)3
There are gaps for the upgrades… but so far we make up for it

## Slide 23: O4 started 24 May 2023
Significant delay from original planning – COVID primary cause
Starting without Virgo due to technical problems; joining soon
KAGRA still commissioning, with plans to join late in the run

## Slide 24: O4 started 24 May 2023
Events 2-3/week, range of likely binary systems represented
No EM/particle coincidences to date (and very poor localization…)
Eagerly awaiting Virgo!

## Slide 25: Notional Plans for the current 4km observatories – 2x improvements
Best guess for LIGO
Virgo similar
Gives improving performance and continuous operation to ~2040
~160 Mpc
~275 Mpc
~600 Mpc

## Slide 26: What could we do with 10x better GW detectors?
Greater sensitivity will enable a qualitative growth in the number of observed sources (10x sensitivity  few 105 sources per year)
It also increases the resolution of waveforms, enabling more stringent tests of GR and more detailed models of the coalescences
Wider bandwidth can expose Neutron star coalescence and thus dynamics of dense matter

## Slide 27: Black Holes and Neutron Stars throughout cosmic time
The best understood source of gravitational wave emissions are compact binary systems.
Can build a detector able see all binaries in a broad range of masses

## Slide 28: Even better detectors would deliver more science. How to build a such a 10x better detector? Make it 10x longer  10x larger signal ΔL = hGW · L

## Slide 29: Noise due to stochastic forces is independent of armlength
The Newtonian Background is the same for 4 or 40km, but the signal is 10x larger
Also unchanged:
  Thermal noise motion (pendulum, substrate, coating)
  Magnetic and electrostatic dynamic forces
…Up to L = 1/2 λGW – giving an optimal length for a given signal
ΔL = h L

## Slide 30: Sensing noises scale with arm length at various powers of 1/L – all get better
30
Shot Noise
while maintaining bandwidth
Radiation Pressure Noise
while maintaining bandwidth
Coating Thermal Noise
loss angle dependence
Residual Gas Noise
facility limit

## Slide 31: The Infrastructure for a realistic implementation
A sufficient length L of the arms is needed to bring the GW-induced strain to a measurable level (4km  40km)
Sensing laser light must travel in an excellent vacuum (10-9 Torr)
The vacuum system diameter must accommodate a diffraction limited beam over 4 or 40km (~1 m Diameter)
The vacuum system must be straight, level, and protected from the human and natural environment (earthmoving, concrete bed, aligned to several mm over 4 or 40km, and protected by a concrete cover)
Corner and end buildings with particulate, temperature control; staff buildings; outreach/public science building (~10,000 m2)

## Slide 32
LIGO Hanford Observatory
Present LIGO Observatory sites
L = 4km
LIGO Livingston Observatory

## Slide 33
Image: Eddie Anaya (Cal State Fullerton)
Image: Eddie Anaya (Cal State Fullerton)
Image: Eddie Anaya (Cal State Fullerton)
Image: Eddie Anaya (Cal State Fullerton)
Image: Eddie Anaya (Cal State Fullerton)
cosmicexplorer.org
cosmicexplorer.org
US contribution to the next-gen Network (with Einstein Telescope – European project)
LIGO-like concept for a single interferometer per site, on Earth’s surface
CE is a larger, and more technically advanced version of LIGO: baseline of two widely separated observatories, 40km and 20km arms

## Slide 34: CE Detector Design
LIGO is starting to plan upgrades to the LIGO 4km detectors for the ‘Post-O5’ epoch – ~2029 to the start of CE observing (optimistically 2035)
  Room temperature, 1 micron light, fused silica optics, sputtered optical coatings, frequency dependent squeezed light..
Initial CE detectors will use techniques of this LIGO Post-O5 upgrade
Low risk – no significant advances in the detector are needed
  Some work on bigger masses, suspensions, lower-loss optics
(Later CE upgrades can include all insights from CE, ET, quantum sensing…)

## Slide 35: CE Infrastructure
Baseline of 40km and 20km observatories
  20km = 1/2 λGW is ideal for observing ~2kHz endgame of neutron-star mergers
  40km is optimized for absolute ‘reach’ to enable all in-scope binaries to be observed
Sites separated by a continental baseline for position information
  Hope that ET in Europe will be built; expect that data will be shared
Working on less expensive vacuum systems (dominates the cost)
Single interferometric detector per site
Earth’s surface construction
  Bad: increased coupling to surface ‘seismic’ noise, and thus Newtonian background – limits low-frequency sensitivity (~7Hz compared to ~5 Hz for ET)
  Good: less expensive than tunneling; no complexity of underground work; future modifications of interferometer layout easier (no new caverns)
Geographically suitable sites can be found in the US (and Canada, Australia…)

## Slide 36
The history of the land will play a pivotal role in this project.
We have the opportunity, and obligation, to work with Indigenous Peoples
We will build synergistic relationships and respect their land, their culture, and their sovereignty.
http://native-land.ca/
If you are not aware of issues surrounding TMT, please read arXiv:2001.00970 .

## Slide 37: CE Status
Conceptual Design is now underway
CE Funding approved for this phase
  International contributions (in-kind) – UK, Canada, Australia, Germany
Goal: observatories by mid-2030’s

## Slide 38: European Vision for the next generation: Einstein Telescope
ET Design: underground, triangular, 3 detectors consisting of two interferometers each (high frequency + low frequency ‘xylophone’)
  Cryogenic test masses, longer wavelengths for LF operation
  Underground infrastructure designed for future upgrades
Possible sites:
  Euregio Meuse-Rhine
  Sardinia, Italy
  (possibly) Saxony, Germany
Current envisioned timeframe:
  Construction to begin in 2026
  Science operations to begin in 2035
Status:
  ET is a fully recognized European Project on European Strategy Forum for Research Infrastructures (ESFRI) Roadmap  a key step in getting the project funding lined up.
  ET Project Organization and relevant Boards have been established
  ET Pathfinder facility in Maastricht, Netherlands under construction
  Site evaluation well underway

## Slide 39: Reach of present and future instruments
Credit: ESO/NAOJ
Cosmic Explorer
and
Einstein Telescope
LIGO
~2033
LIGO
today
Slide: Kevin Kuns

## Slide 40: The last page (at last!)
Ground-based GW observation works, and LIGO, Virgo, and KAGRA observing together
There are lots of sources yet to be observed
Scaling laws show the technical feasibility of better detectors
The US Concept, Cosmic Explorer
  Two sites, one 40km, one 20km
  Surface construction, LIGO Technology
The European Concept, Einstein Telescope
  Underground triangle multiple-interferometer approach
  Pushes detector technology with high power, low temperatures
Both eager to participate in Multi-Messenger Astrophysics
The future is bright for gravitational-wave astronomy!

## Slide 41: Thank you!

## Slide 42: Gravitational Wave Properties
GW generation:
lowest order radiation is quadrupole
quadrupole moment
metric perturbation
Two masses m in a circular orbit at a distance r create a periodic strain h in space
Binary Coalescence of two compact objects
fgw = 2 x forbital
Distance r
Speed c
m
m
About once a week,
a wave passes with this characteristic strain:

## Slide 43: Gravitational Wave Properties
GW generation:
lowest order radiation is quadrupole
quadrupole moment
metric perturbation
Two masses m in a circular orbit at a distance r create a periodic strain h in space
Binary Coalescence of two compact objects
fgw = 2 x forbital
Distance r
Speed c
m
m
About once a week,
a wave passes with this characteristic strain:
A change in distance from here to Alpha Centauri
(4 light-years distant)
of the thickness of a human hair
(10 microns)

## Slide 44: Stretching and squeezing of space-time
Amplitude of the gravitational wave strain is h = ΔL/L
ΔL = h L
Big L makes ΔL easier to measure; current detectors have L = 4 km, so from our two-mass example
ΔL ~10-21 x ~103 = ~ 10-18 m
L
ΔL

## Slide 45: Stretching and squeezing of space-time
Amplitude of the gravitational wave strain is h = ΔL/L
ΔL = h L
Big L makes ΔL easier to measure; current detectors have L = 4 km, so from our two-mass example
~10-21 x ~103 = ~ 10-18 m
L
ΔL

## Slide 46: The binary neutron star signal, with and without the interferometer noise

## Slide 47: 40km CE
Kuns

## Slide 48: Why 40km?
Broadly speaking, the sensitivity of these instruments improves with length
The bandwidth is, however, limited to roughly so making a detector longer than 40km would compromise its access to interesting astrophysics (i.e., post-merger signals and supernovae).

## Slide 49: What can CE do?
arXiv 1902.09485
BNS
BBH
IMBH

## Slide 50: Noise improvements: reducing quantum noise
Increasing the laser power in the arms
  O1,O2 (100kW)  O3 (200kW)  goal is 400 kW for O4
Not easy!
  You need a high power laser first..
  Mirror radii must remain within a few meters of the ~2 kilometer nominal value
  Control issues: angular control and parametric instabilities
  ``Point absorbers”
Applied Optics Vol. 60, Issue 13 pp. 4047-4063 (2021)
Applied Optics Vol. 60, Issue 13 pp. 4047-4063 (2021)
Applied Optics Vol. 60, Issue 13 pp. 4047-4063 (2021)
Applied Optics Vol. 60, Issue 13 pp. 4047-4063 (2021)
Applied Optics Vol. 60, Issue 13 pp. 4047-4063 (2021)
Applied Optics Vol. 60, Issue 13 pp. 4047-4063 (2021)
Applied Optics Vol. 60, Issue 13 pp. 4047-4063 (2021)
  Complementary approach: squeezed states of vacuum

## Slide 51
LASER
Phase
IFO Signal
Amplitude
When average amplitude is zero, the variance remains
Heisenberg uncertainty principle, quadratures associated with amplitude and phase
They enter the interferometer from all the open ports of the interferometer, but the ones which matter are the one entering from the anti-symmetric port!
X1
X2
∆X1 ∆X2 ≥1
Zero-point energy
(vacuum) fluctuations

## Slide 52: Replace regular vacuum with squeezed vacuum
LASER
Squeezed Field
Phase
Amplitude
Reduce quantum noise by injecting squeezed vacuum: less uncertainty in one of the two quadratures
Heisenberg uncertainty principle: if the noise gets smaller in one quadrature, it gets bigger in the other one
One can choose the relative orientation between the squeezed vacuum and the interferometer signal (squeeze angle)
Squeezing is made by creating pairs of photons using an optical parametric oscillator
The pairs are quantum-mechanically entangled and have correlated arrival times at the detector
This reduces the randomness of the time distribution
IFO Signal

## Slide 53: Squeezing performance in O3
PhysRevLett.123.231107
Nature 583, pages 43–47 (2020)
6dB
3 dB of squeezing observed at high frequency = 40% quantum noise reduction (in amplitude); observation of quantum radiation pressure noise in both detectors
GEO

## Slide 54: Frequency Dependent Squeezing for O4
High finesse detuned “filter cavity” which rotates the squeezing angle as function of frequency
SHOT NOISE
RADIATION PRESSURE
NOISE
GW Signal
Quantum Noise
~30Hz
~30Hz
Kimble et al., Phys. Rev. D 65(2) 022002 2001
Highlight from Virgo:
300 m filter cavity already
built and locked and characterized, commissioning in progress
Credit: Antonio Pasqualetti

## Slide 55: Initial results for Frequency Dependent Squeezing LIGO Hanford

## Slide 56: The Cosmic Explorer Project Organization today
Team members from
MIT Cal State Fullerton Syracuse Penn State Caltech University of Washington Bothell
University of Oregon
University of Florida
Texas Tech University
University of Arizona
Bard College
Stanford
Harvard
UC Riverside
The Australian National University
Albert Einstein Institute
University Birmingham
University of Glasgow

## Slide 57: The Cosmic Explorer Project Organization today
Team members from
MIT Cal State Fullerton Syracuse Penn State Caltech University of Washington Bothell
University of Oregon
University of Florida
Texas Tech University
University of Arizona
Bard College
Stanford
Harvard
UC Riverside
The Australian National University
Albert Einstein Institute
University Birmingham
University of Glasgow