## Slide 1: Suspending a 100kg mass (A# suspension design highlights)
Edgard Bonilla
on behalf of the Heavy SUS subgroup of the SWG

## Slide 2: The A# upgrade:
Recommended upgrade from the LSC “Post-O5” report T2200287
Push harder on the technologies that make Advanced LIGO great!
Practice for 3G detectors!
Adapted from G2400503

## Slide 3: The A# upgrade:
What could it get us?
Expectations from post O5 study [T2200287]
200-700 neutron star events a year.
1000-2000 Binary Black hole events a year.
Over 6 min of early warning for prototypical Binary Neutron Star signal.

## Slide 4: The A# upgrade:
We are here
Proposal goes here
A# starts here

## Slide 5: The BSC Heavy Quadruple Suspension [BHQS]
QUAD
BHQS
Great seismic isolation
Low thermal noise
40 kg test mass / 120 kg total
Cross-coupled translations and angles.
Top mass is sufficient for damping
Compact design
Augmented with high-frequency dampers
Design description: P1200056

## Slide 6: The BSC Heavy Quadruple Suspension [BHQS]
QUAD
BHQS
Great seismic isolation
Low thermal noise
40 kg test mass / 120 kg total
Cross-coupled translations and angles.
Top mass is sufficient for damping
Compact design
Augmented with high-frequency dampers
Great seismic isolation
Low thermal noise
100 kg test mass / 400 kg total
Decoupled translations and angles.
Damping with first two masses
Local Interferometric sensors
Built-in high-frequency dampers
Design description: P1200056
Design procedure: T2300137

## Slide 7
Mitigate thermal noise
Better installation/Operation
Mitigate
control noise
Mitigate quantum noise
1.5 MW laser power
100 kg test mass
Reduce angular cross coupling
Reduce control bandwidth
Higher stress fibers
Develop new coatings
Interferometric sensors
Violin mode damping
Bounce-Roll dampers
Acoustic mode dampers
Thermal compensation
Cartridge installation
10 dB squeezing
BHQS
The BSC Heavy Quadruple Suspension [BHQS]

## Slide 8
High stress fibers
Interferometric sensors
Angular decoupling
Payload distribution
The BSC Heavy Quadruple Suspension [BHQS]

## Slide 9
High stress fibers
The BSC Heavy Quadruple Suspension [BHQS]

## Slide 10: High-Stress Fibers
Thermal Noise
: Elastic modulus
: Fiber tension
: Area moment
: Fiber length
Goes as the fourth power of radius!
Benefits:
Less thermal noise from fiber bending.

## Slide 11: High-Stress Fibers
Bounce mode
Roll mode
1st Violin mode
Benefits:
Less thermal noise from fiber bending.
Better Bounce-Roll-Violin modes

## Slide 12: High-Stress Fibers
Benefits:
Less thermal noise from fiber bending.
Better Bounce-Roll-Violin modes
Curvature of Earth cross-couples
Vertical to Length
Roll to Yaw

## Slide 13
Bounce mode
Roll mode
1st Violin mode
Detection band
High-Stress Fibers
Benefits:
Less thermal noise from fiber bending.
Better Bounce-Roll-Violin modes
BHQS
Current QUAD

## Slide 14
Payload distribution
The BSC Heavy Quadruple Suspension [BHQS]

## Slide 15: Payload distribution
‘Optimal’ Isolation insights [T2100287]:
Payloads in geometric ratios.
Equal lengths for all stages.
Maximize payload for a given mass
Final mass
Total payload

## Slide 16: Payload distribution
Best Triple SUS
Best Quadruple SUS
Target suspoint Isolation
Current length
Longitudinal isolation at 10 Hz
P=400 kg
Mass ratio =1/4
BHQS
34 cm
34 cm
34 cm
60 cm
117 kg
100 kg
100 kg
83 kg
Long last stage for thermal noise
Same PUM as TST
Equal lengths for isolation
Mass distribution for isolation
Maximize total payload
100 kg test mass

## Slide 17
Angular decoupling
The BSC Heavy Quadruple Suspension [BHQS]

## Slide 18: Angular Decoupling
The idea:
Attaching wires above the center of mass causes translation-to angle coupling.
  Attach wires at center of mass.

## Slide 19: Angular Decoupling
The idea:
Attaching wires above the center of mass causes translation-to angle coupling.
  Attach wires at center of mass.
Lateral compliance of blade springs creates cross-coupling
  Set springs parallel to the beam direction to mitigate the effect

## Slide 20: Angular Decoupling
The idea:
Attaching wires above the center of mass causes translation-to angle coupling.
  Attach wires at center of mass.
Lateral compliance of blade springs creates cross-coupling
  Set springs parallel to the beam direction to mitigate the effect
Large inertias and stiffnesses protect against imperfections
Realistically we should expect some imperfections!
Top mass drive to test mass pitch coupling
*BHQS drive scaled by 4.03 (ratio of DC stiffnesses)

## Slide 21
Interferometric sensors
The BSC Heavy Quadruple Suspension [BHQS]

## Slide 22: Interferometric Sensors

## Slide 23: Interferometric Sensors
Noise floor is at least 1000 times lower than OSEMs above 1 Hz.
Enable active control from Top mass and UIM.
34 cm
34 cm
34 cm
60 cm
117 kg
100 kg
100 kg
83 kg
TOP
UIM
PUM
TST

## Slide 24: Work in progress
Design opportunities
  Hard mode visibility at the UIM.
  Even higher stress fibers.
  Control codesign optimization.
Cross-coupling models
  FEA for cantilever springs.
  Mitigation strategies for lateral blade spring compliance.
  DC alignment effect on cross-coupling.
Noise estimates
  Actuator noise modelling.
  Realistic drive distribution for length control.
Additional design work
  Reaction chain
  TransMon suspension
Prototyping
  First prototype under development at MIT
Want to get involved?
Contact edgard@stanford.edu
(or find me walking around at the LVK)
BHQS Parameters available on the SVN at: design_BHQS.m

## Slide 25: In summary
We are preparing for the LIGO A# era.
  More and earlier detections.
  Testbed for 3G technology
The suspension design plan is underway.
  The plan is to understand and account for as many noise sources as possible.
BHQS prototype coming soon!

## Slide 26: Extra Slides!

## Slide 27
Longitudinal Plant
Requirements:
6e-20 m/Hz1/2 at 10 Hz
Constraints:
60 cm last stage
100 kg test mass
Less than 400kg payload
Interferometric sensors enable damping of the suspension to low Q.
Thermal noise will limit the ultimate suspension performance at 10 Hz.
Improvements on the ISI infrastructure are now directly correlated with suspension performance

## Slide 28: Vertical mode exploration
Targets for Vertical:
Third mode at 3.6 Hz
Less than 2e-20 m/Hz1/2 for Length
10 Hz motion for 3.6 Hz Vertical mode
The red circle is around where min-maxing would give us small TOP and UIM stages for this frequency.
Stiffnesses (per spring):
KST2 = 3260 N/m , KTOP = 4650 N/m , KUIM = 2760 N/m
Current BHQS springs:

## Slide 29: Vertical Plant
Requirements:
2e-17 m/Hz1/2 at 10 Hz
Constraints:
1.6 GPa fibers
Blade springs must fit
10-3 [m/m] coupling to Longitudinal
Current Quad
Longitudinal Transmission
Workshop (old) BHQS
Current BHQS design
Target
Only top mass damping. Easy to meet the target.
Bounce mode increases the expected longitudinal motion between 4-8 Hz, but this is okay.
Expected test mass longitudinal motion

## Slide 30
Frequency [Hz]
Test Mass Pitch [rad/Hz1/2]
From ISI L
(± 1 mm)
From ISI P
The large inertia and stiffnesses limit the cross coupling even in the presence of unintended offsets
Even with random offsets of up to 1 mm, the Longitudinal degree of freedom mostly does not dominate the pitch of the optic.
Target
With only local control, we expect the RMS angle of the optic to be at around 5 nrad RMS.
Pitch Plant
Requirements:
1e-17 rad/Hz1/2 10 Hz
1 nrad RMS with IFO control
Constraints:
Test mass radius < 45 cm
10-3[m/rad] coupling to Longitudinal

## Slide 31
Suspension Modes
Suspension modes
Separated to an equivalent Q of 19.
Stiffer pitch plant helps with robustness

## Slide 32
Hard/Soft modes (first order)

## Slide 33
Hard/Soft modes (first order)

## Slide 34: Mode visibility at the UIM
Performance is at least 1000 times better than OSEMs above 1 Hz.
Enable active control from Top mass and UIM.
34 cm
34 cm
34 cm
60 cm
117 kg
100 kg
100 kg
83 kg
TOP
UIM
PUM
TST
Hard mode is visible at the UIM!